## Slide 1: Geodesy Review with discussion of NATRF2022 & SPCS2022
PSLS Annual Conference
January 2025
Jeff Jalbrzikowski, P.S., GISP, CFS
Appalachian Regional Geodetic Advisor
jeff.jalbrzikowski@noaa.gov
240-988-5486

## Slide 2: Organizational Structure
  -Department of Commerce (DoC)
  (~47,000 employees)
  -National Oceanic and Atmospheric Administration (NOAA)
  -National Ocean Service (NOS)
  -National Geodetic Survey (NGS)
  (~175 employees)
Notes: -We are the Federal Government’s oldest scientific agency.
-part of the Executive Branch
-I know it can seem kind of strange that NGS is part of the NOS, but the origins of NGS lie with the C&GS.
-we are a “Program Office” of the NOS
Survey of the Coast – 1807
Coast Survey – 1836
Coast and Geodetic Survey – 1878
NGS since 1970

## Slide 3: Organizational Structure
  -Department of Commerce (DoC)
  (~47,000 employees)
  -National Oceanic and Atmospheric Administration (NOAA)
  -National Ocean Service (NOS)
  -National Geodetic Survey (NGS)
  (~175 employees)
≠
We’re not USGS, we’re NGS
Notes: -as you can read my slide, I like to point that out because over my 2 years at NGS I’ve seen and heard this misunderstanding quite a bit
-don’t worry! it doesn’t offend us! and we do work closely with USGS, but we are separate agencies within totally different departments of the federal government

## Slide 4
Any references to any commercially available hardware or software do not constitute an endorsement or a disapproval of any manufacturers, developers, dealers, or suppliers.
Thanks.

## Slide 5: Let’s start with some alphabet soup

## Slide 6: NGS Mission
To define, maintain and provide access to the National Spatial Reference System (NSRS) to meet our Nation’s economic, social, and environmental needs.
NSRS
Notes: NGS develops and maintains the National Spatial Reference System, a national coordinate system that provides the foundation for transportation, navigation, land record systems, mapping and charting efforts, and a multitude of scientific and engineering applications
CLICK
You’ve all seen this or some similar graphic I’m sure. That bottom layer… that’s our baby, the NSRS.

## Slide 7: Yes, we are delayed.
  NSRS Modernization
Notes: So remember, today’s presentation is not JUST about new datums, it is about modernizing the NSRS as a whole.
You don’t know what the NSRS is? Stay tuned, we’ll get there as we go along.

## Slide 8: Delayed Release of the Modernized NSRS
How long will the delay be?
  NGS plans to roll out components of the modernized NSRS in 2025 or 2026.
Will the names stay the same?
  Yes, terms containing “2022” such as “NATRF2022” and “NAPGD2022” will remain the same.

## Slide 9: Modernizing the NSRS
Updating all NSRS coordinates
  Replace existing datums with new datums
  Replacing existing SPCS83 with new SPCS2022
  Accounting for coordinates changing with time
Improving NGS products and services
Simplifying customer contributions
Making the NSRS:
  More accurate
  More accessible
  More efficient
Rollout in
2025
begins

## Slide 10: NGS Mission
access… ? = traditionally  marks/disks/objects
= modern and future  NOAA CORS Network (NCN)
via OPUS
To define, maintain and provide access to the National Spatial Reference System (NSRS) to meet our Nation’s economic, social, and environmental needs.
Notes: Follow up thought
-like it or not, we know that the vast majority of our users are obtaining NSRS coordinates via OPUS
-while that is our plan for the future of primary access, modernized NSRS, as of now the official form of access (specifically to NAVD88) truly is to “touch brass” as they say  meaning occupy a benchmark

## Slide 11: NOAA CORS Network (NCN)
Notes: -I would like to point out we have a new, official name for the network you see represented on this map,
-The NOAA CORS Network, or NCN
CLICK
-this is neat little graphic with some stats on teh NCN you can find on our website
-below the gaphic youll find a search bar with more information

## Slide 12: CORS Networks
Global: International GNSS Service (IGS) Network
  The international standard since mid-1990s
  Supported by IGS Analysis Centers (ACs)  NGS is 1 of 7
  Overall system sponsored by NASA
NSRS: NOAA CORS Network (NCN)
  NGS processes/distributes data, but few are NGS-operated
  Subset of NGS-operated CORS comprise the under construction NOAA Foundation CORS Network (NFCN)
Regional/State/Commonwealth/Local Networks
  Real-Time Networks (RTN… aka “VRS”)
  Currently semi-coupled to the NCN
Notes: Global: International GNSS Service (IGS) Network
  The international standard since mid-1990s
  Supported by IGS Analysis Centers (ACs)  NGS is one AC of seven total
  Overall system sponsored by NASA
NSRS: NOAA CORS Network (NCN)
  NGS processes/distributes data, but few are NGS-operated
  Subset of NGS-operated CORS comprise the under construction NOAA Foundation CORS Network (NFCN)
Regional/State/Commonwealth/Local Networks
  Real-Time Networks (RTN… aka “VRS”)
  Currently semi-coupled to the NCN
    NGS sees the future as a close coupling of other networks with the NCN so users can seamlessly and confidently work in the NSRS using their favorite regional/local CORS network

## Slide 13: IGS Network
Source: https://www.igs.org/maps/#station-map
Notes: There are several CORS Networks.
The Global Standard is the IGS Network
  IGS = International GNSS Service
The NOAA CORS Network (NCN) which consists of:
  The NOAA Foundation CORS Network (NFCN), a sub-network being installed, owned, and operated by NGS
  and 2,000+ stations managed, but rarely owned by NGS
Other Regional/Local Networks (RTNs, etc.)
  Currently semi-coupled to the NCN
    NGS sees the future as a close coupling of these other networks with the NCN so users can seamlessly and confidently work in the NSRS using their favorite regional/local CORS network.

## Slide 14: NOAA CORS Network (NCN) in PA
Notes: where else but the federal government are you going to see two acronyms within one acronym?

## Slide 15: KeyNetGPS CORS Network
Notes: where else but the federal government are you going to see two acronyms within one acronym?

## Slide 16: NOAA CORS Network (NCN) in PA
Notes: where else but the federal government are you going to see two acronyms within one acronym?

## Slide 17: KeyNetGPS CORS Network
non-NCN CORS
Notes: where else but the federal government are you going to see two acronyms within one acronym?

## Slide 18: NOAA CORS Network (NCN)
Notes: -I would like to point out we have a new, official name for the network you see represented on this map,
-The NOAA CORS Network, or NCN
CLICK
-this is neat little graphic with some stats on teh NCN you can find on our website
-below the gaphic youll find a search bar with more information

## Slide 19: Passive Control
All marks are passive—they sit there and hold a point
Geodetic Control – Terminology
Notes: All marks are passive!—in that they sit there doing nothing in and of themselves besides holding a point
This includes the fixed antenna mount that is a part of a CORS.
But, some marks have permanently installed equipment that enable nearly continuous observations and these are called “active” stations.

## Slide 20
Passive Control

## Slide 21
Terminology - Passive Control

## Slide 22
Terminology - Passive Control
Notes: KW0392 –
https://www.ngs.noaa.gov/cgi-bin/ds_mark.prl?PidBox=KW0392
COLUMBIA COUNTY, PA, NEAR READING COMPANY REAILROAD STATION

## Slide 23
Notes: KR1724 - https://www.ngs.noaa.gov/cgi-bin/ds_mark.prl?PidBox=kr1724
Set 1946  Washoe County, NV, about 4 miles southwest of Reno
Recovery 1958  THE STATION MARK WILL BE PRESERVED BY MR. GARCIA, AND WILL BE IN THE CENTER OF HIS LIVING ROOM. - -> BUILT AS A BROKEN WAGON WHEEL WITH THE TRIANGULATION STATION THE HUB THERE-OF.
A STANDARD DISK STAMPED WHEELER 1946, 1958 IS BEING PROVIDED MR. GARCIA, TO PLACE IN THE FLOOR.

## Slide 24
Please … do not add a new dimple

## Slide 25: Active Control
Some marks have permanently installed equipment (e.g. CORS) that enables continuous observations
Geodetic Control – Terminology
But they still sit there and hold a point…
Notes: All marks are passive!—in that they sit there doing nothing in and of themselves besides holding a point
This includes the fixed antenna mount that is a part of a CORS.
But, some marks have permanently installed equipment that enable nearly continuous observations and these are called “active” stations.

## Slide 26: CORS
Continuously Operating Reference Station
RECEIVER
DATA STORAGE
POWER
COMMUNICATIONS
Active Control
GNSS ANTENNA
Notes: Note that the whole pillar could be considered a type of “mark”, being a passive do-nothing structure that holds a “point”, the GRP of this CORS.
But the point, given coordinates computed from all the data collected by that antenna, is probably in here somewhere, as a part of this huge pillar which is effectively one big mark, passive as can be….

## Slide 27
Active Control

## Slide 28
Active Control

## Slide 29
Active Control
Active Control

## Slide 30: Active vs. Passive Control
Passive – some sort of mark with a defined point
Active – some equipment continuously collecting observations on a point
In the modernized NSRS, our emphasis will be to provide accurate coordinates on Active Control… so that you can go out and set your own Passive Control
My point: surveying is still surveying
Notes: Often the term active geodetic control has been used to mean some equipment is continuously or at least frequently collecting observations at or near a point
Yet those observations are often used to compute coordinates (often time-dependent) at a point on a mark, which, by its nature is passive

## Slide 31
Positional Components of
the NSRS
Geometric
aka “Horizontal”
Latitude, Longitude, Ellipsoid Height
Geopotential
aka Orthometric Height
aka “Elevation”
NAD83
NAVD88
Notes: -geometric component is latitude, longitude, and ellipsoid height
-geopotential component is combined with the geometric components to calculate an ortho height or capital H

## Slide 32: Datum Defined
“The adopted standard latitude and longitude of a given station, together with the adopted standard azimuth of a line from that station.”
e.g. NAD27
  station Meade’s Ranch and it’s azimuth mark Waldo
Source: Proceedings of the 14th General Conference of the International Geodetic Association (IAG) - ”Report on Geodetic Operations in the United States”, O.H. Tittmann, Superintendent of the USC&GS
Notes: --Also table/podium example
-this is how things have been done historically, so let’s look closer at the example

## Slide 33
North American Datum of 1927 (NAD27)
Datum – Traditional Horizontal
Notes: -a great example to share is the North Ameiccan Datumof 1927
-what was selected as the Origin? a specific mark, that of PID KG0640
-it’s a triangulation station now on the property of one Kyle Brant.
-his contact info is in the datasheet and do give him a call a day in advance
--STORY: was passing by once on a return trip from CO to see family
-anyway, we define that mark as the origin and…
CLICK

## Slide 34
1Springer Handbook of Global Navigation Satellite Systems, Ch. 2, p. 34
= CORS
-the cake
-the recipe
Realizes the system by means of coordinates of definite points that are accessible directly by occupation or observation1
Reference Frame:
A set of prescriptions and conventions together with the modeling required to define a triad of coordinate axes1
Reference System:
Before you can realize a Reference Frame… you must define a Reference System
Reference System & Frame
Notes: An ITRS meets the following conditions: – Geocentric (origin is Earth centre of mass) – Uses the metre as the unit of length – Initial orientation given by BIH orientation at 1984 – The time evolution of the orientation is ensured by using a no-net rotation condition with regards to horizontal tectonic motions over the
whole earth.
• The ITRS is of very little use to the practitioner – we need a realisation (some coordinates)

## Slide 35
International Terrestrial Reference System (ITRS)
  IERS’s recipe
International Terrestrial Reference Frame
  Realized by the ITRF Network (the SGT stations)
True for any System and Frame
  Not just the ITRF
Reference System & Frame
Notes: Global: International GNSS Service (IGS) Network
  The international standard since mid-1990s
  Supported by IGS Analysis Centers (ACs)  NGS is one AC of seven total
  Overall system sponsored by NASA
NSRS: NOAA CORS Network (NCN)
  NGS processes/distributes data, but few are NGS-operated
  Subset of NGS-operated CORS comprise the under construction NOAA Foundation CORS Network (NFCN)
Regional/State/Commonwealth/Local Networks
  Real-Time Networks (RTN… aka “VRS”)
  Currently semi-coupled to the NCN
    NGS sees the future as a close coupling of other networks with the NCN so users can seamlessly and confidently work in the NSRS using their favorite regional/local CORS network

## Slide 36: Reference System
GRS80 ellipsoid
ITRF2020
NAD83
GRS = Geodetic Reference System
Reference Frame
Notes: -we’re going to back up and get to the non-egocentricity, stay with me here
-so there’s a nice little ellipse representing the shape of the GRS80 reference ellipsoid
CLICK
-what’s GRS80? well, it’s a reference system (being a reference ellipsoid, a gravity model, and more).
-GRS80 in itself is not a datum, although you will see/hear some folks misinterpret that
CLICK
-now once you take that reference system/ellipsoid and you tie it to the origin of your choice… badabing!
-now you’ve got a datum (or reference frame)
CLICK
-in this case, we’re talking about that blue which is symbolizing an ellipsoid with it’s origin locked to the Center Mass of the earth
-which represents the ITRF2020
-you may be thinking “jeff what is the ITRF?”… don’t worry we’ll get there for now the concept is more important
CLICK
-so now let’s look at how NAD83 compares, the orange there, see it’s shape is the same GRS80 ellipsoid… but with a different origin point
-not quite aligned to CM, but close… not bad, it was the 80s maaaan, they did the best they could!
-jokes aside, a pretty amazing feet to have only “missed the mark” by a few meters, they didn’t have the satellite technology or computer power we have back in the late 70s when the calcs for NAD83 were being run
-props to those folks!
CLICK

## Slide 37: ITRF vs NAD83
ITRF2020
NAD83
GRS80 ellipsoid
Notes: --zooming in to setup for next slide—
-Let’s zoom in a little to examine that situation

## Slide 38: Different Center of Mass point
~2.2 meters
NAD83
origin
ITRF2020
origin
Earth’s
Surface
h83
h14
GRS80
ellipsoid
Notes: -so there’s one quarter of both the NAD83 and ITRF2020 ellipsoid
CLICK
-important to note that both are using the same geometry (size, shape), the GRS80 ellipsoid, just with a different origin
CLICK
-so that dark red [maroon if you will] arrow there on the bottom left, it symbolizes and greatly exaggerates the difference between those origins
CLICK

## Slide 39: Update Center of Mass point of NAD83
Earth’s
Surface
GRS80
ellipsoid
NAD83
ITRF2020
NATRF2022
h22
Shift…
Notes: -and we’ll visualize the plan to remove the non-egocentricity of NAD83 with a little animation
CLICK
-our orange NAD83 ellipsoid shift over to match up with out blue ITRF ellipsoid
-and now there we see the result in red, our new NATRF2022 ellipsoid
CLICK
-what do I like to point out here?
-we’re still utilizing the GRS80 reference ellipsoid as the basis for NATRF2022
-why? because the size and shape, well the scientists nailed it on that one, like I said earlier they just didn’t quite get the CM
CLICK

## Slide 40
International Terrestrial Reference System (ITRS)
  IERS’s recipe
International Terrestrial Reference Frame
  Realized by the ITRF Network (the SGT stations)
True for any System and Frame
  Not just the ITRF
National Spatial Reference System
  NGS’s recipe
North American Terrestrial Reference Frame
  Realized by the NOAA CORS Network
  Accessible easily with GPS, by using OPUS
Reference System & Frame
Notes: Global: International GNSS Service (IGS) Network
  The international standard since mid-1990s
  Supported by IGS Analysis Centers (ACs)  NGS is one AC of seven total
  Overall system sponsored by NASA
NSRS: NOAA CORS Network (NCN)
  NGS processes/distributes data, but few are NGS-operated
  Subset of NGS-operated CORS comprise the under construction NOAA Foundation CORS Network (NFCN)
Regional/State/Commonwealth/Local Networks
  Real-Time Networks (RTN… aka “VRS”)
  Currently semi-coupled to the NCN
    NGS sees the future as a close coupling of other networks with the NCN so users can seamlessly and confidently work in the NSRS using their favorite regional/local CORS network

## Slide 41
NATRF2022
North American Terrestrial Reference Frame of 2022
will replace
NAD83
North American Datum of 1983
Technically, not just NATRF2022 but also its 3 sister TRFs…

## Slide 42: Four TRFs for Modernized NSRS
North American Terrestrial Reference Frame of 2022
(NATRF2022)
Pacific Terrestrial Reference Frame of 2022
(PATRF2022)
Caribbean Terrestrial Reference Frame of 2022
(CATRF2022)
Mariana Terrestrial Reference Frame of 2022
(MATRF2022)

## Slide 43: Plate Rotation visualized
Drift…

## Slide 44: Four TRFs for Modernized NSRS
North American Terrestrial Reference Frame of 2022
(NATRF2022)
Pacific Terrestrial Reference Frame of 2022
(PATRF2022)
Caribbean Terrestrial Reference Frame of 2022
(CATRF2022)
Mariana Terrestrial Reference Frame of 2022
(MATRF2022)

## Slide 45
Existing, accepted terminology
  International TRF
  first realization of the ITRF was 1988
  NATRF2022 will be based on ITRF2020
Terrestrial Reference Frame?
Notes: “Horizontal Datum” - misnomer for NAD83
  Really is a Geometric Reference Frame

## Slide 46
International Terrestrial Reference Frame (ITRF)
Is native coordinate system for NCN.
Is what OPUS uses.
Is what most of world uses.
Is what NGA aligns WGS-84 to.
Notes: So what is that acronym, ITRF?
-it is a global reference frame, the most widely adopted one, or the “gold standard” or the “Cadillac” or what-have-you
-ITRF is the internationally recognized standard
-who realizes the ITRF? well, NGS contributes to the realization but
CLICK
-The IERS is in responsible charge of defining, realizing and promoting the ITRF
-and the ITRF was formally adopted by the…yes, more acronyms
CLICK
IUGG some years ago

## Slide 47
Watch the grid!
ITRF concept
Epoch:
Notes: Ok, now ITRF mentioned a couple slides ago.
Most simplistic way to explain ITRF is to watch this animation.
This is a very loose representation/visualization of what the ITRF is, a characterization only.

## Slide 48: Plate-Fixed NSRS TRFs
ITRF
Frame = constant
NA Plate = rotating
NATRF
Frame = rotating
(relative to ITRF)
NA Plate = constant
(relative to NATRF2022)
Notes: We say “NATRF2022” is “fixed” to the N.A. Plate, making it a “plate fixed” frame
-the frame is constant to itself, but rotating within ITRF, and moving in a different direction than the other 3 frames

## Slide 49
ITRF – constant frame, rotating plate

## Slide 50: Plate-Fixed
NATRF – rotating frame, constant with plate

## Slide 51
ITRF or NATRF – your choice if you know epoch
if you know epoch

## Slide 52: Decades of continuously logged GPS data from the NOAA CORS Network (NCN).
  But how?

## Slide 53
NOAA CORS Network (NCN)
Notes: The NOAA CORS Network is a multi-purpose, multi-agency cooperative endeavor, combining the efforts of hundreds of government, academic, and private organizations.
The stations are independently owned and operated.
Each agency shares their GNSS observations and station metadata with NGS, which are analyzed and archived.
The data is distributed free of charge with multiple forms of access.

## Slide 54: Continuously Operating Reference Station

## Slide 55
NOAA CORS Network (NCN)

## Slide 56: Plate-Fixed
NATRF – rotating frame, constant with plate
= CORS

## Slide 57: Plate-Fixed
ITRF or NATRF
= CORS
Notes: ITRF is independent of any plates, tied to the layer below,
-”plate-agnostic” if we want to sound all silicon valley ish
-the plates go down about 200 km (125 mi) deep below our feet right now, as we’re on a continental plate
--(oceanic plates are roughly half the thickness, like 100 km)
- but thickness of the tectonic plates varies greatly, from down to 15 km up over the 200 km I mentioned earlier

## Slide 58
Epoch
eh-puck? ee-pock? … to-may-to, to-mah-to
an instant of time; timestamp
astronomy & geodesy use a decimal date
  2021.4762 = 23 June 2021 @ 19:16:00
  using epochs is important, not your format
    start preparing to assign epochs to your data
Terminology – Time/4D
Notes: -Where do you see an Epoch right now in NGS data?
CLICK
Datasheets! there you see the epoch of 2010.0
and of course OPUS Solution Reports!
note that in blue over there on the right you’ll see another epoch, in the ITRF, which I will explain later on

## Slide 59
Notes: -Where do you see an Epoch right now in NGS data?
Datasheets! there you see the epoch of 2010.0
and of course OPUS Solution Reports!
note that in blue over there on the right you’ll see another epoch, in the ITRF, which I will explain later on

## Slide 60
Reference Epoch
Survey Epoch
Notes: -Where do you see an Epoch right now in NGS data?
and of course OPUS Solution Reports!
note that in blue over there on the right you’ll see another epoch, in the ITRF, which I will explain later on

## Slide 61: What is a Reference Epoch?
First let’s look at complete nomenclature…
If you use NAD83 you’re already using one, but probably didn’t know it.

## Slide 62: Complete NAD83 Nomenclature
NAD83(2011) epoch 2010.00
Geometric
Datum
Realization
(aka Datum Tag)
Epoch
(in the case of NAD83, a Reference Epoch)
NAD83(1986) epoch 1984.00
NAD83(HARN) epoch 1993.62
NAD83(CORS96) epoch 2002.00
NAD83(2007) epoch 2007.00
Other NAD83 Reference Epochs
NAD83(1986) epoch 1984.00
NAD83(HARN) epoch 1993.62
NAD83(CORS96) epoch 2002.00
NAD83(2007) epoch 2007.00
NAD83(2011) epoch 2010.00
ITRF2014 epoch 2019.9185
IGS08 epoch 2005.00
NATRF2022 epoch 2020.00

## Slide 63
Reference Epoch
Survey Epoch
Notes: -Where do you see an Epoch right now in NGS data?
and of course OPUS Solution Reports!
note that in blue over there on the right you’ll see another epoch, in the ITRF, which I will explain later on

## Slide 64: What is a Survey Epoch?
If you use OPUS you’re already using one, but perhaps unaware.

## Slide 65: Complete ITRF Nomenclature
ITRF2014 (epoch 2021.0276)
Geometric
Datum
Epoch
(in the above example, a Survey Epoch)
ITRF92 epoch 1988.0
ITRF2000 epoch 1997.0
ITRF2005 epoch 2000.0
ITRF2008 epoch 2005.0
ITRF2014 epoch 2010.0
ITRF Reference Epochs
NAD83(1986) epoch 1984.00
NAD83(HARN) epoch 1993.62
NAD83(CORS96) epoch 2002.00
NAD83(2007) epoch 2007.00
NAD83(2011) epoch 2010.00
ITRF2014 epoch 2019.9185
IGS08 epoch 2005.00
NATRF2022 epoch 2020.00
ITRF2008 epoch 2012.2011
IGS08 epoch 2006.7572
ITRF2014 epoch 2017.4457
ITRF2014 epoch 2019.9185
ITRF2014 epoch 2021.0276
Examples of ITRF Survey Epoch

## Slide 66: Epochs in Current NSRS
Reference Epoch (RE)
Position after propagated back in time from SE to RE
Seen on OPUS Solution
Used in NAD 83
Ground movement will be hidden
Survey Epoch (SE)
Position at the moment of survey data collection
Seen on OPUS Solution
Necessary for ITRF
Ground movement will be illustrated

## Slide 67: Epochs in Modernized NSRS
Reference Epoch (RE)
Position after propagated back in time from SE to RE
Used in NATRF2022
REC = RE Coordinate
Ground movement will be hidden
Survey Epoch (SE)
Position at the moment of survey data collection
Used in NATRF2022
SEC = SE Coordinate
Ground movement will be illustrated

## Slide 68: 4D alignment – Epochs
One epoch in which ITRF2020 will be equal to NATRF2022…
At 00:00 on January 01, 2020 any given coordinates in
ITRF2020 (epoch 2020.0) = NATRF2022 (epoch 2020.0)
Notes: After that, they diverge and continue to do so, we’ll visualize that soon

## Slide 69
Convert
    change the type of coordinate
    NAD83(2011) latitude & longitude  NAD83(2011) SPCS
  Transform
    change the datum of coordinate
    NGVD29 height  NAVD88 height
    NAD 27 latitude & longitude  NAD 83(2011) latitude & longitude
Propagate
    change the epoch of coordinate
    NATRF2022 epoch 2023.243 to NATRF2022 epoch 2020.000
Coordinate Operations
Notes: Historically NGS has been inconsistent with these top two words.
Going forward, we will use them as:
  Conversion: Meaning to change the type of coordinate without changing the datum or frame
  Transformation: Meaning to change the datum or frame, without changing the type of coordinate

## Slide 70: NCAT
  How will you propagate coordinates back in time from SE to RE?
Epochs/Time/4D
NGS Coordinate Conversion And Transformation Tool (NCAT)
Notes: -so you’ve probably seen that phrase that I have front and center here, NSRS Modernization
-that’s the blanket term we use to refer to not just the new datums but other updates

## Slide 71: NGS Coordinate Conversion And Transformation Tool (NCAT)
Notes: NCAT includes the functionality of previous NGS tools:
NADCON 5.0
XYZWIN 2.0
UTMS 2.1
SPC83 2.1
USNG 2.3
Includes error estimate of transformation per point.
Available as the single-point graphic seen here, multi-point upload/download, as a downloadable executable fie to run from the DOS prompt, and as web services for inclusion in your own
It’s a great tool. Anyone using

## Slide 72
NGS Coordinate Conversion And Transformation Tool (NCAT)
Notes: NCAT includes the functionality of previous NGS tools:
NADCON 5.0
XYZWIN 2.0
UTMS 2.1
SPC83 2.1
USNG 2.3
Includes error estimate of transformation per point.
Available as the single-point graphic seen here, multi-point upload/download, as a downloadable executable fie to run from the DOS prompt, and as web services for inclusion in your own
It’s a great tool. Anyone using

## Slide 73
NCAT is available via web services

## Slide 74
NCAT is available via web services
Note that each operation is a separate service
Struggling?
Contact us.
We can help!

## Slide 75
NGS Coordinate Conversion And Transformation Tool (NCAT)
Notes: NCAT includes the functionality of previous NGS tools:
NADCON 5.0
XYZWIN 2.0
UTMS 2.1
SPC83 2.1
USNG 2.3
Includes error estimate of transformation per point.
Available as the single-point graphic seen here, multi-point upload/download, as a downloadable executable fie to run from the DOS prompt, and as web services for inclusion in your own
It’s a great tool. Anyone using

## Slide 76
NGS Coordinate Conversion And Transformation Tool (NCAT)
Notes: NCAT includes the functionality of previous NGS tools:
NADCON 5.0
XYZWIN 2.0
UTMS 2.1
SPC83 2.1
USNG 2.3
Includes error estimate of transformation per point.
Available as the single-point graphic seen here, multi-point upload/download, as a downloadable executable fie to run from the DOS prompt, and as web services for inclusion in your own
It’s a great tool. Anyone using

## Slide 77: NCAT source code is on GitHub

## Slide 81: What’s the difference?
NCAT
NSRS Datums
  NAD 27
  NAD 83
  NGVD 29
  NAVD 88
  PRVD 02
  ASVD 02
  NMVD 03
  GUVD 04
  VIVD 09
VDatum
NSRS Datums
Geoid Models
  Add/Subtract from Ellipsoid
Tidal Datums
  MHW, MLLW, MTL
Great Lakes Datum
  IGLD85
ITRF#### ≈ WGS84
Local Tidal (LT)

## Slide 82
Estimated Geometric Change - Horizontal
NAD83 (2011)  NATRF2022
3.6 ft
4.3 ft
3.9 ft
Direction of Shift
4.6 ft
3.0 ft
Notes: What’s the magnitude of the horizontal datum shift across Pennsylvania?
Minimum Shift ~3.75 feet
Maximum Shift ~3.97
Remember this is just an estimation, don’t hold me to the numbers please

## Slide 84: New Lat/Long = New XY
With a new horizontal datum…
  NAD 83 to be replaced by NATRF2022
There comes a new set of State Plane Coordinate System zones
  SPCS 83 to be replaced by SPCS2022

## Slide 85: A “flat” Earth for the future
State Plane Coordinate System of 2022 (SPCS2022)
Similar to existing State Plane…
  Same 3 map projection types
  Same ellipsoid (GRS 80)
But different…
  Based on new datums instead of NAD 83
  Designed to reduce difference between “grid” and “ground”
  Many more “zones”
  Zones “layers” will exist in most states
Transverse Mercator (TM)
Oblique Mercator (OM)
Lambert Conformal Conic (LCC)

## Slide 86
e.g., Lambert conformal conic
(used for SPCS)
Polar aspect
Oblique aspect
Central parallel
Standard parallels
Origin
e.g., stereographic (not used for SPCS)
One-parallel (tangent)
Two-parallel (secant)
Conic projections
Planar (azimuthal) projections
Developable surfaces: Planes and cones
Examples given are CONFORMAL projections
Standard parallel

## Slide 87
Cylindrical projections
Central meridian
Skew axis
Equator
“Regular” aspect
Transverse aspect
Oblique aspect
e.g., Mercator
(not used for SPCS)
e.g., transverse Mercator
(used for SPCS)
e.g., oblique Mercator
(used for SPCS)
Developable surfaces: Cylinders
Examples given are CONFORMAL projections

## Slide 88
Projection axis
Tangent ( = 1)
A map projection is a mathematical function
Grid distance > ellipsoid distance
Ellipsoid distance
Ellipsoid surface
Grid distance = ellipsoid distance
is projection axis scale factor
is constant value applied to conformal projection “grid”
= 1 by default if not defined

## Slide 89
Projection axis
Tangent ( = 1)
A map projection is a mathematical function
Grid distance > ellipsoid distance
Ellipsoid distance
Non-intersecting ( > 1)
Secant ( < 1)
Ellipsoid surface
Grid distance < ellipsoid distance
Grid distance > ellipsoid distance
Grid distance = ellipsoid distance
Grid distance = ellipsoid distance
Grid distance = ellipsoid distance
Ellipsoid distance
Can “move” conformal projection surface “up” or “down” by changing
Grid distance > ellipsoid distance everywhere

## Slide 90
Projection axis
“Secant” conformal map projection
Ellipsoid distance
Secant ( < 1)
Ellipsoid surface
Grid distance < ellipsoid distance
Grid distance > ellipsoid distance
Grid distance = ellipsoid distance
Grid distance = ellipsoid distance
Ellipsoid distance
Zone width to balance positive and negative distortion (scale error) with respect to ellipsoid
14.5%
71%
14.5%

## Slide 91
Projection axis
“Non-intersecting” conformal map projection
Non-intersecting
( > 1)
Ellipsoid surface
Purpose is to reduce linear distortion at “ground” (topographic surface).
But distortion can vary considerably across area of interest.
Grid distance = ground distance at a point
Grid distance = ground distance at a point
Grid distance ≈ ground distance over finite distance
Topographic surface

## Slide 92
Projection axis
“Non-intersecting” conformal map projection
Non-intersecting
( > 1)
Ellipsoid surface
Topographic surface

## Slide 93
Projection axis
Changing projection axis to reduce distortion variation
Non-intersecting
( > 1)
Ellipsoid surface
h2
h1
Grid distance = ground distance at many points
Only way to reduce variation in distortion is to change projection axis location.
IMPORANT: For large areas, there is no single defining ellipsoid height, h, for scaling the projection.
Ellipsoid height of surface not constant:
h1 ≠ h2
Topographic surface
Notes: Ellipsoid height of surface not constant, but those heights (h1 and h2) are not defining parameters of the projection

## Slide 94: Consider North Carolina SPCS 83 Zone
Central “standard” parallel
Ellipsoid
North standard parallel
South standard parallel
(projection axis)
Scale = 1
Scale = 1
Scale = 0.9998 7259…
Secant Lambert Conformal Conic projection, 2-parallel definition:
Standard parallels
North = 36°10’N (exact)
South = 34°20’N (exact)
It is EXACTLY the same as this 1-parallel definition:
Central standard parallel
35°15’06.33096…”N
Scale = 0.9998 7259…
An LCC projection is defined by its projection axis, which is ALWAYS the central standard parallel

## Slide 95: Secant Lambert Cone
Central “standard” parallel
(projection axis)
35°15’06.33096
Scale = 0.9998 7259…
Not Fitting Terrain
What Can We Do?
Note: Perpendicular Line to Cone (blue) is also Perpendicular to ellipsoid (yellow) at the Projection Axis
An LCC projection is defined by its projection axis, which is ALWAYS the central standard parallel

## Slide 96: Tangent Lambert Cone
Central “standard” parallel
(projection axis)
35°15’06.33096
Scale = 1
Move Cone Up
Same Projection Axis, Different scale factor
An LCC projection is defined by its projection axis, which is ALWAYS the central standard parallel

## Slide 97: Non-Intersecting Lambert Cone
Central “standard” parallel
(projection axis)
35°15’06.33096
Scale = 1.001
Move Cone Up Again
Same Projection Axis, Different scale factor
An LCC projection is defined by its projection axis, which is ALWAYS the central standard parallel

## Slide 98: Design to Fit Terrain 1
Central “standard” parallel
(projection axis)
Change Cone Angle
New Projection Axis, and Different scale factor
Scale = 1.010
36°00’00”
An LCC projection is defined by its projection axis, which is ALWAYS the central standard parallel

## Slide 99: Design to Fit Terrain 2
Central “standard” parallel
(projection axis)
Scale = 1.020
Change Cone Angle Again
New Projection Axis, and Different scale factor
37°00’00”
An LCC projection is defined by its projection axis, which is ALWAYS the central standard parallel

## Slide 100: Design to Fit Terrain 3
Central “standard” parallel
(projection axis)
An LCC projection is defined by its projection axis, which is ALWAYS the central standard parallel
Scale = 1.030
Change Cone Angle Again
New Projection Axis, and Different scale factor
38°00’00”

## Slide 101: Design to Fit Terrain 4
Central “standard” parallel
(projection axis)
Scale = 1.001
Move Cone Down
Retain Projection Axis, Different scale factor
38°00’00”
An LCC projection is defined by its projection axis, which is ALWAYS the central standard parallel

## Slide 102
State Plane Coordinate System of 1983
SPCS83
North and South Zones as they exist now
Notes: We start with the SPCS83 zones as a frame of reference
NOTE that the color shading of these zones is matched to that of the Preliminary SPCS2022 Zones that follow

## Slide 103: Linear distortion magnitudes ppm = parts per million (mm/km)
±20 ppm = 2 cm/km = 0.1 ft/mile = 1 : 50,000
  Often used as “low distortion” design criterion (at ground)
±50 ppm = 5 cm/km = 0.3 ft/mile = 1 : 20,000
  Minimum design criterion for SPCS2022 designs by NGS (at ground)
±100 ppm = 10 cm/km = 0.5 ft/mile = 1 : 10,000
  “Nominal” maximum State Plane value (on ellipsoid)
  Can be much greater at topo surface
±400 ppm = 40 cm/km = 2.1 ft/mile = 1 : 2,500
  Maximum design criterion for SPCS2022 zones (at ground)
  Maximum UTM value (on ellipsoid)
Nominal distortion criterion (on ellipsoid) for SPCS 27 and 83 zones (although greatly exceeded for some zones in SPCS 83).

## Slide 104
DRAFT

## Slide 105
DRAFT

## Slide 107
State Plane Coordinate System of 2022
SPCS2022
PA stakeholders requested 4-5 zones, which NGS designed, the following are preliminary maps
Notes: The following section illustrates the preliminary SPCS2022 zones
There are 4 zones in the NGS design, per request that we design “4-5 zones required to meet the minimum distortion acceptable” set by our design criteria of 50ppm
NOTE the request also included wording: “It is also requested that PennDOT districts be divded into no more than two zones”

## Slide 108: Stakeholders Involved in PA SPCS2022
PennDOT
PTC
PSLS
PSPE
PA Geospatial Coordinating Board (GeoBoard)
  Geodetic Working Group
County GIS Professionals Association of PA
PA-MAGIC (now Keystone GIS)
PA-MAPPS
Notes: A major component of SPCS2022 are stakeholders
Stakeholders have a role in helping define (and maintain) SPCS2022
Pennsylvania Department of Transportation
Pennsylvania Turnpike Commission
PSLS of course
PSPE – Society of Professional Engineers
The GeoBoard
County GIS Professionals Association of Pennsylkvania
PA Mapping & Geographic Information Consortium
Your State chapter of the Management Association for Private Photogrammetric Surveyors

## Slide 109
Notes: NOTE that the West Zone far surpasses the NGS design criteria of 50ppm

## Slide 110
Notes: This is the first, and likely final, draft of an Oblique Mercator projection for the Preliminary Central Zone
NOTE that even with the

## Slide 111
Notes: This is the second draft of a Preliminary North East Zone
NOTE this includes Columbia and Montour Counties, and the animation highlights the comparison between having these counties in the SE or NE Zone

## Slide 112
Notes: This is the second draft of a Preliminary South East Zone
NOTE this excludes Columbia and Montour Counties (they would fall in SE Zone)

## Slide 117
State Plane Coordinate System of 2022
SPCS2022
NGS will create a Single Statewide Zone for every State, the following is a Preliminary map

## Slide 118: Linear distortion magnitudes ppm = parts per million (mm/km)
±20 ppm = 2 cm/km = 0.1 ft/mile = 1 : 50,000
  Often used as “low distortion” design criterion (at ground)
±50 ppm = 5 cm/km = 0.3 ft/mile = 1 : 20,000
  Minimum design criterion for SPCS2022 designs by NGS (at ground)
±100 ppm = 10 cm/km = 0.5 ft/mile = 1 : 10,000
  “Nominal” maximum State Plane value (on ellipsoid)
  Can be much greater at topo surface
±400 ppm = 40 cm/km = 2.1 ft/mile = 1 : 2,500
  Maximum design criterion for SPCS2022 zones (at ground)
  Maximum UTM value (on ellipsoid)
Distortion range (at ground) for zones designed by NGS, as detailed in draft SPCS2022 policy and procedures.

## Slide 119: Linear distortion magnitudes ppm = parts per million (mm/km)
±20 ppm = 2 cm/km = 0.1 ft/mile = 1 : 50,000
  Often used as “low distortion” design criterion (at ground)
±50 ppm = 5 cm/km = 0.3 ft/mile = 1 : 20,000
  Minimum design criterion for SPCS2022 designs by NGS (at ground)
±100 ppm = 10 cm/km = 0.5 ft/mile = 1 : 10,000
  “Nominal” maximum State Plane value (on ellipsoid)
  Can be much greater at topo surface
±400 ppm = 40 cm/km = 2.1 ft/mile = 1 : 2,500
  Maximum design criterion for SPCS2022 zones (at ground)
  Maximum UTM value (on ellipsoid)
Distortion criterion (at ground) often used for “low distortion projection” (LDPs); designed by others for SPCS2022 (not by NGS)

## Slide 120
Notes: This Single Statewide Zone designed by NGS is color shaded to match the following section of slides that show UTM Zones linear distortion values
It is known that some user communities with large areas of responsibility choose to maintain geospatial data and work in UTM
This graphic as compared to the UTM serves to highlight in SPCS2022, users will see better performance (lower linear distortion) if they choose to work in the SPCS2022 Single Statewide Zone rather than one of the UTM Zones that fall within Pennsylvania

## Slide 121
UTM (NAD83) Zones as
UTM
The following are maps using existing UTM zones as a Single Statewide Zone
(included to highlight the lower performance as compared to Preliminary NGS Zone)

## Slide 124
Notes: The NGS designed preliminary single statewide zone is included again here at the end for easier visual comparisons.

## Slide 125
Notes: Reminder that you don’t have to cutoff data at any SPCS zone extent  just need to understand that they’re designed with certain extents in mind

## Slide 126: SPCS2022 Zone Layers in PA
Both Single Statewide and Multi-Zone Layers will coexist
Think about your data, your goals, your customers
  Remember that geographic coordinates are your friend!
Smaller zones not “the best” … it all depends on usage & goals

## Slide 127: Which is best?
Each has strengths and each has weaknesses.
Single Statewide Zone Layer
Multi-Zone Layer

## Slide 128: SPCS2022 Zone Layers and LDPs
Each state may have max of 3 zone “layers”
  One layer must be statewide zone
    Pennsylvania Single Statewide
  Other layers have two or more zones
    Pennsylvania Multi-Zone
  A third layer can exist, but must be discontinuous coverage
    Left open for possibilities in Pennsylvania
      Low Distortion Projections (LDPs) for specific areas?

## Slide 129: Pennsylvania Coordinate System Law
Problems
Designates specific zones
Parameters of projections included
Restricts datum usage to 1983 or 1927
Unit of measure designated as Survey Foot
Anyone familiar with the requirement that SPCS coordinates in recorded land records must be certified by the surveyor?
Act of Dec. 16, 1992, P.L. 1224, No. 161

## Slide 130: Pennsylvania Coordinate System Law
Update drafted by GeoBoard Geodetic Working Group
  included participation from PSLS and Keystone GIS
Final version reviewed in October 2024
Introduced last year
Reintroduce in upcoming legislative session
Thanks to all contributors, especially Bob Regola

## Slide 131
State Plane Coordinate System of 2022
SPCS2022
Not just Pennsylvania
Notes: The following section illustrates the preliminary SPCS2022 zones
There are 4 zones in the NGS design, per request that we design “4-5 zones required to meet the minimum distortion acceptable” set by our design criteria of 50ppm
NOTE the request also included wording: “It is also requested that PennDOT districts be divded into no more than two zones”

## Slide 132: SPCS2022 linear distortion (prelim)
846 zones (CONUS)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 76% | 71% | 58%
±50 | 92% | 89% | 76%
±100 | 98% | 97% | 89%
±400 | 100% | 100% | 99.9%
City and area statistics (ppm): |  |  | 
 | Min | -407 | -1438
 | Max | +486 | +2624
 | Range | 893 | 4062
 | Mean | -6 | -23
Mean weighted by pop = -4 |  |  | 

## Slide 134: SPCS2022 Zone Layers and LDPs
Each state may have max of 3 zone “layers”
  One layer must be statewide zone
    West Virginia Single Statewide
  Other layers have two or more zones
    Multi-Zone
  A third layer can exist, but can only be partial coverage
    Low Distortion Projections (LDPs) for specific areas

## Slide 135: Zone Layers
Single Statewide
Multi-Zone Complete
Multi-Zone Partial

## Slide 136: Zone Layers

## Slide 137
Notes: What’s the best performing zone layer anywhere?

## Slide 139: SPCS2022 linear distortion (prelim)
846 zones (CONUS)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 76% | 71% | 58%
±50 | 92% | 89% | 76%
±100 | 98% | 97% | 89%
±400 | 100% | 100% | 99.9%
City and area statistics (ppm): |  |  | 
 | Min | -407 | -1438
 | Max | +486 | +2624
 | Range | 893 | 4062
 | Mean | -6 | -23
Mean weighted by pop = -4 |  |  | 

## Slide 140
The Survey Foot is dead!
Long live the Survey Foot!
US Survey Foot was deprecated 31 December 2022…
But will always be available in NGS tools for NAD83 and NAD27
Notes: We start with the SPCS83 zones as a frame of reference
NOTE that the color shading of these zones is matched to that of the Preliminary SPCS2022 Zones that follow

## Slide 141
Deprecated 31 December 2022
Which begs the question
  What should you be doing now?
What happened to the US Survey Foot?

## Slide 142: What should you be doing now?
Prepare for this along with new datums
Understand the difference between sft and ift
  2 parts per million
Understand this is not enforced
  Neither NIST or NGS are a regulatory agency
  We support education/outreach of course
  But OPUS, NCAT, etc. will not have US Survey Foot options for output in SPCS2022 zones

## Slide 143
The Survey Foot is dead!
Long live the Survey Foot!
US Survey Foot was deprecated 31 December 2022…
But it will always be available in NGS tools for NAD83 and NAD27 coordinates

## Slide 144: NGS Products and Services
Not just OPUS
All exist in three environments:
  Development (DEV) - internal testing and development
    same as when you hear a company talk about an “Alpha” product
  Beta - continued internal testing, open for public testing
    key features have already been vetted/tested
  Production - final product, open to public use
    this is what you see first when navigating our website
Notes: I’ll be talking about OPUS today, but I need to clarify one of our processes for this to all be clear. I will also mention that this is a new-ish workflow for NGS, began in the past 8 or so years.
So all NGS Products & Services go thru this process as they are created, tested internally, open for testing by you our constituents, and then rolled out as final products.
CLICK
There’s three environments that products will exist in, listed here in the order they occur
First, a tool will be created on the “DEV” servers for internal NGS-only development, testing, and otherwise “working the bugs out”
this is the same phase as when you hear a software company or video game maker talk about their alpha products
CLICK
Next, after some level of confidence in the product is gained, it will be migrated to the Beta servers, thereby open to the public for their own testing
it’s important to note that when a product is available via our Beta page, when you use it you are indeed now a “beta tester”
key features will have already been tested in the Development environment, but it is still a beta, so as a beta tester please let us know if you have issues/complications/struggles or the like
CLICK
At some point, when all I’s are dotted and T’s crossed, the thing will be moved to the Production environment.
 by then, the tool is integrated into others, has been vetted with 2 testing phases and functions as expected, but may still continue to receive version updates by repeating this process

## Slide 145
www.ngs.noaa.gov
beta.ngs.noaa.gov
Remember, you won’t see the DEV environment…
Notes: So here we have 3 screenshots, first here showing the Production OPUS Projects gateway page
CLICK
Second is the Beta page, with the text here showing the URL for our Beta homepage
-How do you find that beta page? substitute “beta” for “www”
-or most tools that have a beta will have a link to that beta platform
CLICK
Last is the Development or DEV example, which again you will not see unless via a demo from NGS personnel

## Slide 146: Wait… how do I get to the NGS Beta site?

## Slide 147
www.ngs.noaa.gov
beta.ngs.noaa.gov

## Slide 148: Federal Geospatial Data Committee (FGDC)
FGCS = Federal Geodetic Control Subcommittee
  Under the umbrella of the FGDC, NGS leads the FGCS

## Slide 150: FGCS Member Agencies
DEPARTMENT OF AGRICULTURE
  USFS –US Forestry Service
  FSA – Farm Service Agency
DEPARTMENT OF COMMERCE
  USCB – US Census Bureau
  NIST – National Institute of Standards & Technology
  NOAA – National Oceanic and Atmospheric Administration
DEPARTMENT OF HOMELAND SECURITY
  USCG – US Coast Guard
  FEMA – Federal Emergency Management Agency
DEPARTMENT OF DEFENSE
  NGA – National Geospatial-Intelligence Agency
  USACE – US Army Corps of Engineers
  USNO – US Naval Observatory
DEPARTMENT OF THE INTERIOR
  BIA – Bureau of Indian Affairs
  BOEM – Bureau of Ocean Energy Management
  OSMRE – Office of Surface Mining and Reclamation Enforcement
  USBR – US Bureau of Reclamation
  USGS – US Geological Survey
  NPS – National Park Service
  BLM – Bureau of Land Management
  FWS – Fish and Wildlife Service
DEPARTMENT OF STATE
  IBC – International Boundary Commission
  IBWC – International Boundary and Water Commission
DEPARTMENT OF TRANSPORTATION
  DOT – Department of Transportation
  FAA – Federal Aviation Administration
INDEPENDENT AGENCIES
  NASA – National Aeronautics and Space Administration
  EPA – Environmental Protection Agency
  TVA – Tennessee Valley Authority
  FCC – Federal Communications Commission
Notes: Among all these agencies, we serve as the experts on geodetic control and geodesy for the United State government

## Slide 151: Preparing
Know the epoch of your data/datasets
  consider how you will track this
    full to-the-second timestamp on every feature?
      Modern survey equipment makes this possible
    labeling a year for each dataset?
      Easy to add to workflows, datasets/databases, folders
    something in-between that works for your needs?
2023.1957
2023:27
20230127
Epoch nomenclature is your choice

## Slide 152: Preparing
Reprocessing your data
  perfect world = everyone reprocesses everything
    what does this mean?
      consider an ALTA w/topo
        start over with the onsite GNSS-based control
        reorient all your shots/ties (hopefully linked)
        recreate all the drainage features in new datum
    unrealistic! … and unnecessary for majority users
Notes:   Reprocessing your data
    in a perfect world, everyone would reprocess data
        consider a final product like you use everyday - a hydro-enforced DEM
          starting fresh with the raw GNSS/IMU processing
          generate new ellipsoid height point clouds
          recreate all the drainage features in new datum
    this is totally unrealistic  both from a financial and programmatic perspective

## Slide 153: Preparing
  Transforming your data
    NCAT - NGS Coordinate Conversion and Transformation Tool
      ASCII up/download, Web Services, Download, GitHub
      ask your software provider(s) about integration
        we envision COTS integrations as most popular method of access
        Industry Workshops - May 2021 and August 2022
          Esri, Trimble, Blue Marble, etc… all the well known names attended
        Geospatial Software Developers’ Summit – Nov/Dec
          International & Virtual  US NGS and NRCan CGS
Notes: Transforming your data
NCAT - NGS Coordinate Conversion and Transformation Tool
available now: ASCII upload and Web Services
ask your software providers about integration
we envision this as most popular method of access
Industry Workshop held this year – esri, trimble, bluemarble, all the major well known names were represented
labeling a year for each dataset?
something in-between that works for your needs

## Slide 154: Remember…
  What’s the goal of NATRF2022?
    Give you the stability in positions that you expect
  That’s the point of Reference Epochs (REs)
    Akin to the different realizations of NAD83
    REs will be published every 5 or 10 years
      you choose when you update
      in a perfect world, everyone would stay current
aka versions
Notes: What’s the goal of the way NATRF2022 was designed, by including EPP2022 and IFVM2022
Does a database of manholes in PA need cm-level coordinate updates on an annual basis? Probably not.

## Slide 155: Additional Resources

## Slide 156
Click this icon on homepage
Email Subscriptions
*Only 1-2 messages per month*
NGS News
  Includes quarterly NSRS Modernization newsletter
Webinar Series
Training
GPS on Benchmarks

## Slide 157
Jeff Jalbrzikowski, P.S., GISP, CFS
Appalachian Regional Geodetic Advisor
jeff.jalbrzikowski@noaa.gov
240-988-5486
https://www.ngs.noaa.gov/ADVISORS/
or search: “NGS advisors”

## Slide 158
SESSION
EVALUATION
HTTPS://WWW.SURVEYMONKEY.COM/R/2025PSLSEVAL

## Slide 159
What you see in a map of NSRS control…

## Slide 160
What we see in a map of NSRS control…