## Slide 1: The Future is Here
Michael L. Dennis, PhD, PE, PLS
SPCS2022 Project Manager
NOAA’s National Geodetic Survey
FIG Working Week 2023
Orlando, Florida, USA
28 May – 1 June, 2023
Introducing the State Plane Coordinate System of 2022
Paper #12044

## Slide 2: State Plane Coordinate System of 2022 (SPCS2022)
Part of modernizing the U.S. National Spatial Reference System
Third generation of State Plane
  First in 1930s (SPCS 27), second in 1980s (SPCS 83)
  Same 3 map projection types
  Same ellipsoid as SPCS 83 (GRS 80)
The same, but different…
  Based on new terrestrial reference frames instead of NAD 83
  Zone “layers” in most states
  More zones, most designed by state stakeholders
  Designed to reduce difference between “grid” and “ground” distances
Transverse Mercator
Hotine Oblique Mercator
Lambert Conformal Conic

## Slide 3: SPCS2022 zone layers
1 layer: 12 states plus 6 territories
2 layers: 28 states
3 layers: 10 states

## Slide 4: Number of SPCS2022 zones (preliminary)
Designs by NGS
  165 zones
  Includes 54 statewide zones and 3 “special use” zones (in more than one state)
Designs by state stakeholders
  802 zones in 28 states
Total = 967 zones for 56 states and territories
Compare to 125 zones in existing State Plane

## Slide 5: SPCS2022 distortion design philosophy
Linear distortion minimized at topographic surface (not at ellipsoid surface)
  Purpose: reduce difference between projected “grid” and actual “ground” distances
  Population distribution also taken into account
What is linear distortion?
  Projection “scale error” at topographic surface
  Unique (i.e., same in every direction) only for conformal projections
  Given here in parts per million (ppm) = mm of distortion per km
Linear distortion | = | Projected minus actual distance
 |  | Actual distance

## Slide 6: Linear distortion magnitudes
Parts per million | Centimeters per kilometer | Feet per mile | Dimensionless ratio | Examples
20 ppm | 2 cm/km | 0.1 ft/mile | 1:50,000 | Typical “low distortion projection” limit
50 ppm | 5 cm/km | 0.3 ft/mile | 1:20,000 | Minimum distortion for designs by NGS
100 ppm | 10 cm/km | 0.5 ft/mile | 1:10,000 | Historic State Plane distortion design limit
400 ppm | 40 cm/km | 2.1 ft/mile | 1:2,500 | UTM distortion design limit

## Slide 7: Existing SPCS 83 linear distortion
106 zones (CONUS)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 17% | 11% | 6%
±50 | 40% | 30% | 17%
±100 | 74% | 68% | 41%
±400 | 99% | 98% | 91%
City and area statistics (ppm): |  |  | 
 | Min | -913 | -1038
 | Max | +206 | +223
 | Range | 1120 | 1261
 | Mean | -98 | -178
Mean weighted by pop = -75 |  |  | 
7

## Slide 8: SPCS2022 linear distortion (prelim)
49 zones (CONUS)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 14% | 12% | 7%
±50 | 27% | 26% | 18%
±100 | 48% | 48% | 36%
±400 | 91% | 93% | 88%
City and area statistics (ppm): |  |  | 
 | Min | -1512 | -1627
 | Max | +2888 | +2987
 | Range | 4400 | 4614
 | Mean | -86 | -120
Mean weighted by pop = -100 |  |  | 
8

## Slide 9: SPCS2022 linear distortion (prelim)
646 zones (35 states)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 76% | 70% | 54%
±50 | 92% | 88% | 73%
±100 | 98% | 97% | 89%
±400 | 100% | 100% | 99.9%
City and area statistics (ppm): |  |  | 
 | Min | -400 | -684
 | Max | +245 | +295
 | Range | 644 | 979
 | Mean | -5 | -23
Mean weighted by pop = -4 |  |  | 
9

## Slide 10: SPCS2022 linear distortion (prelim)
187 zones (10 states)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 79% | 79% | 73%
±50 | 91% | 91% | 88%
±100 | 99.8% | 99% | 97%
±400 | 100% | 100% | 100%
City and area statistics (ppm): |  |  | 
 | Min | -256 | -465
 | Max | +120 | +230
 | Range | 376 | 693
 | Mean | -3 | -13
Mean weighted by pop = -0.5 |  |  | 
10

## Slide 11: Where to learn more about SPCS2022
geodesy.noaa.gov
Thank you!