## Slide 1: Brave New Coordinates
The Next Generation of State Plane in the United States
Michael L. Dennis, PhD, PE, PLS
SPCS2022 Project Manager
Blue Marble GeoTalks 2024
January 24, 2024

## Slide 2: State Plane Coordinate System of 2022 (SPCS2022)
Part of modernizing the National Spatial Reference System (NSRS)
Third generation of State Plane
  First in 1930s (SPCS 27), second in 1980s (SPCS 83)
  Same 3 conformal map projection types
  Same ellipsoid as SPCS 83 (GRS 80)
Same as existing State Plane, but different…
  Based on new terrestrial reference frames instead of NAD 83
  More zones, most designed by state stakeholders
Transverse Mercator
Hotine Oblique Mercator
Lambert Conformal Conic

## Slide 3: SPCS2022 zone layers
1 layer: 12 states plus 6 territories
2 layers: 28 states
3 layers: 10 states

## Slide 4: Number of SPCS2022 zones (preliminary)
Designs by NGS
  165 zones
  Includes 54 statewide zones…
  …and 3 “special use” zones (in more than one state)
Designs by state stakeholders
  802 zones in 28 states
Total = 967 zones for 56 states and territories
Compare to 125 zones in existing State Plane

## Slide 5: State Plane Coordinate System of 2022 (SPCS2022)
Part of modernizing the National Spatial Reference System (NSRS)
Third generation of State Plane
  First in 1930s (SPCS 27), second in 1980s (SPCS 83)
  Same 3 map projection types
  Same ellipsoid as SPCS 83 (GRS 80)
Same as existing State Plane, but different…
  Based on new terrestrial reference frames instead of NAD 83
  More zones, most designed by state stakeholders
  Designed to reduce linear distortion at topographic surface (i.e., reduce difference between “grid” and “ground” distances)
Transverse Mercator
Hotine Oblique Mercator
Lambert Conformal Conic

## Slide 6: State Plane Coordinate Systems of 1983 and 1927

## Slide 7: State Plane Coordinate System of 2022

## Slide 8: SPCS2022 distortion design philosophy
Linear distortion minimized at topographic surface (not ellipsoid surface)
  Purpose: reduce difference between projected “grid” and actual “ground” distances
  Population distribution also taken into account in NGS designs
What is linear distortion?
  Map projection “scale error” at topographic surface
  Unique (i.e., same in every direction) only for conformal projections
  Given here in parts per million (ppm) = mm of distortion per km
Linear distortion | = | Projected minus actual distance | 
 |  | Actual distance | 

## Slide 9: Linear distortion magnitudes
Parts per million | Centimeters per kilometer | Feet per mile | Dimensionless ratio | Examples
20 ppm | 2 cm/km | 0.11 ft/mile | 1:50,000 | Typical “low distortion projection” limit
50 ppm | 5 cm/km | 0.26 ft/mile | 1:20,000 | Minimum distortion for designs by NGS
100 ppm | 10 cm/km | 0.53 ft/mile | 1:10,000 | Historic State Plane distortion design limit
400 ppm | 40 cm/km | 2.11 ft/mile | 1:2,500 | UTM distortion design limit

## Slide 10
SPCS2022 linear distortion (preliminary)
Green is ±50 ppm (±0.26 ft/mile)
Distortion performance: ±370 ppm
Performance percentages:
90% population
91% cities & towns
86% total area
Mean weighted by population: -99 ppm
GREEN: grid = ground (within ±50 ppm or ±0.26 ft/mile)
Grid versus ground distance
BLUE: grid SHORTER than ground
RED: grid LONGER than ground

## Slide 11
SPCS 83 linear distortion (existing)
Green is ±50 ppm (±0.26 ft/mile)

## Slide 12
SPCS 83 linear distortion (existing)
Green is ±50 ppm (±0.26 ft/mile)
These zones will be removed

## Slide 13
SPCS 83 linear distortion (existing)
Green is ±50 ppm (±0.26 ft/mile)
This zone will change, additional zones may be added

## Slide 14
SPCS2022 linear distortion (preliminary)
Green is ±50 ppm (±0.26 ft/mile)
Distortion performance: ±45 ppm
Performance percentages:
90% population
87% cities & towns
69% total area
Mean weighted by population: -4 ppm

## Slide 15
SPCS 83 linear distortion (existing)
Green is ±50 ppm (±0.26 ft/mile)
Distortion performance: ±159 ppm
Performance percentages:
90% population
85% cities & towns
59% total area
Mean weighted by population: -75 ppm

## Slide 16
SPCS2022 linear distortion (preliminary)
Green is ±50 ppm (±0.26 ft/mile)
Distortion performance: ±45 ppm
Performance percentages:
90% population
87% cities & towns
69% total area
Mean weighted by population: -4 ppm

## Slide 17: When will SPCS2022 be done?

## Slide 18: Alpha products are NOT final products!
Preliminary
For illustrative purposes only
Not authoritative
Under active development
Subject to change without notice
Feedback to: ngs.feedback@noaa.gov
https://alpha.ngs.noaa.gov/index.shtml

## Slide 19: Alpha SPCS2022 Home
https://alpha.ngs.noaa.gov /SPCS/index.shtml
Gives date last updated (on all SPCS2022 pages)
Links to other SPCS2022 pages in sidebar:
  Zone information
  Distortion maps
  Online interactive maps (SPCS2022 Experience)
  Alpha NCAT
  Additional information
  Feedback

## Slide 20: Zone Information
Interactive tables
  Zone definitions
  Example coordinates
Downloadable data and other tables will be added later
Blue Marble has already made use of this information for preliminary testing

## Slide 22: ArcGIS Online SPCS2022 Experience
Online interactive maps
Shows distortion and gives projection definitions
  Zone parameters not all given to full precision
  Cannot get distortion values from maps

## Slide 24: NSRS Modernization
Alpha site is ONLY for NSRS Modernization
Rollout 2025
More to it than just SPCS2022…
  Deprecation of U.S. survey foot
  Terrestrial reference frames
  Geopotential datum
  Time-dependence
  Reference epoch coordinates
  And more…
PRELIMINARY

## Slide 25: That’s great, but when will SPCS2022 be done?
SPCS2022 included with rollout of Modernized NSRS in 2025
But SPCS2022 design will be done sooner
  Getting feedback from stakeholders and others now
  In process of updating projection algorithms
  Blue Marble has already made use of preliminary designs
  Finalize designs by mid-2024
Designs done and shared with the world in 2024!
  Will provide definitions directly usable by our commercial partners
  Includes Blue Marble, Esri, Trimble, Hexagon, Topcon, Carlson, Autodesk, etc.
  Definitions also in EPSG Geodetic Parameter Dataset and ISO Geodetic Registry

## Slide 26: Where to learn more…
geodesy.noaa.gov
Thank you!