## Slide 1
Geodesy Fundamentals
February 9, 2018
Professional Surveyors Association of Nebraska
1
Professional Surveyors Association of Nebraska
Winter Seminar
Dave Zenk
NGS Advisor
February 9, 2018
Kearney, NE

## Slide 2: SPCS2022 Webinar
Webinar on State Plane Coordinates on March 8, 2018 by Michael Dennis
February 9, 2018
Professional Surveyors Association of Nebraska
2
https://geodesy.noaa.gov/web/science_edu/webinar_series/Webinars.shtml

## Slide 3: Class Outline
Review the basics
  Astronomy
  Geodetic Systems
  Datums
  Map Projections
  GPS
February 9, 2018
Professional Surveyors Association of Nebraska
3

## Slide 4: Astronomy
Earth, Sun, Stars System
  Earth Orbit around Sun
  Geometry and Vocabulary
Practical Astronomy and Celestial Coordinates
  Altitude-Azimuth System
  Right Ascension-Declination System
  Sidereal Hour Angle – Local Hour Angle System
  PZS Triangle
  Methods for finding latitude, longitude, and azimuth.
February 9, 2018
Professional Surveyors Association of Nebraska
4
Elgin, Knowles & Senne, Inc. (Archer-Elgin)
310 E. 6th St., Rolla, MO 65401
http://www.rollanet.org/~eksi/2008EPHEM.pdf
https://www.blm.gov/cadastral/Manual/73man/id34.htm
Sections 2-53 to 73

## Slide 5: Astronomy
Earth’s Elliptical Orbit Around the Sun (Northern Hemisphere)
  1) Winter Solstice (December 21)
    Perihelion (January 3)
  2) Spring Equinox (March 21)
  3) Summer Solstice (June 21)
    Aphelion (July 3)
  4) Autumn Equinox (September 21)
February 9, 2018
Professional Surveyors Association of Nebraska
5
closer to sun
further from sun
Perihelion = closest to sun on January 3 (147 M km)
Semi-dia = 0-16’-15.9”
Aphelion = furthest from sun on July 3 (152 M km)
Semi-dia = 0-15’-43.9”
23.5 degree axis tilt from ecliptic plane
Image by NASA

## Slide 6: Astronomy
Intersection of Orbital Plane and Equatorial Plane forms a line which points to First Point of Aries, γ (vernal equinox) and First Point of Libra, Ω (autumnal equinox)
Astronomers prefer the vernal equinox and so it is the reference point in the sky.
February 9, 2018
Professional Surveyors Association of Nebraska
6
Image by NASA
2 planes intersect to form a line which points to γ
γ
γ
γ
γ

## Slide 7: Astronomy
Moon’s orbit is tilted 5 degrees from ecliptic plane
February 9, 2018
Professional Surveyors Association of Nebraska
7
Image by NOAA/NASA SciJinks

## Slide 8: Astronomy
Celestial Sphere (infinite radius)
Rotates east-to-west
February 9, 2018
Professional Surveyors Association of Nebraska
8
(first point of Aries)
Celestial Equator
Pole
Sun or Star
Itty-Bitty Earth
Autumnal Equinox
(first point of Libra)
Which direction is Earth rotating?
γ
Vernal Equinox

## Slide 9: Astronomy
Right Ascension - Declination (Sidereal Hour Angle) System
February 9, 2018
Professional Surveyors Association of Nebraska
9
Vernal Equinox
Celestial Equator
Pole
Sun or Star
Sidereal Hour Angle (SHA)
Declination Angle
Right Ascension (RA)
γ

## Slide 10: Astronomy
Altitude-Azimuth System (based on local horizon of observer)
February 9, 2018
Professional Surveyors Association of Nebraska
10
North
Horizon
South
East
West
Nadir
Zenith
Azimuth Angle
Sun or Star
Altitude Angle

## Slide 11: Astronomy
PZS Triangle
February 9, 2018
Professional Surveyors Association of Nebraska
11
Vernal Equinox
Celestial Equator
Pole
Sun or Star
Zenith
P
Z
S

## Slide 12: Astronomy
PZS Triangle
February 9, 2018
Professional Surveyors Association of Nebraska
12
Sun or Star
S
Zenith
Z
Pole
P
90⁰ - Latitude
90⁰ - Declination
90⁰ - Altitude
“Azimuth”
LHA
Parallactic Angle

## Slide 13: Astronomy
Spherical Trigonometry
  3 sides and 3 angles – all are expressed in angular units of measure!
  If one knows any 3 of the 6 parts, one can solve for the other 3 parts.
Spherical Law of Sines
Spherical Law of Cosines
February 9, 2018
Professional Surveyors Association of Nebraska
13
A
B
C
b
a
c
sin A sin B sin C
----- = ----- = -----
sin a sin b sin c
cos a – cos b cos c
cos A = -------------------
sin b sin c

## Slide 14: Astronomy
What do we know and what do we measure?
  Latitude
  Altitude
  Declination
  Azimuth
  Local Hour Angle (LHA)
  Parallactic Angle
Choice and circumstance dictate!
Traditionally know: Latitude, Longitude, & Declination
  Measure altitude, then use “Altitude Method” to solve for azimuth
  Measure time, then use “Hour Angle Method” to solve for azimuth
February 9, 2018
Professional Surveyors Association of Nebraska
14

## Slide 15: Astronomy
Derive practical equations for both methods (Caltrans)
  http://www.dot.ca.gov/hq/row/landsurveys/LSITWorkbook/04.pdf
  See Unit 4, page 4
Altitude Method
  Uses Latitude, Declination, and Altitude
Hour Angle Method
  Uses Latitude and Declination, then Longitude, Time, and Right Ascension (to compute LHA)
February 9, 2018
Professional Surveyors Association of Nebraska
15
sin LHA
Z = tan-1 ---------------------------------
sin LAT cos LHA – cos LAT tan DEC
sin DEC – sin LAT sin ALT
Z = cos-1 -------------------------
cos LAT cos ALT

## Slide 16: Astronomy
Refraction Correction – Altitude Method
  One of the difficulties of the Altitude Method is refraction due to the atmosphere.
February 9, 2018
Professional Surveyors Association of Nebraska
16

## Slide 17: Astronomy
February 9, 2018
Professional Surveyors Association of Nebraska
17
Altitude angle error due to refraction by atmosphere
Actual Sun
Apparent Sun

## Slide 18: Astronomy
Refraction Correction – Altitude Method
  Angular refraction error is a function of altitude
  Also semi-diameter correction
February 9, 2018
Professional Surveyors Association of Nebraska
18
Altitude | Approximate Correction
90⁰ | 0⁰
70⁰ | - 0⁰00’18”
50⁰ | - 0⁰00’48”
30⁰ | - 0⁰01’36”
10⁰ | - 0⁰05’18”
Date | Semi-diameter
January 3 | 0-16’-15.9”
July 3 | 0-15’-43.9”
Affected by atmospheric temperature and pressure, which can only be measured at position of observer.

## Slide 19: Astronomy
The dynamic relationships of Earth, Sun, & Stars are important concepts and so is the vocabulary and geometry to describe it.
The best way to master practical astronomy is to go outside and do the observations.
Learn to cast solar shadows of the telescope’s crosshair on a white card – do not look through telescope!
February 9, 2018
Professional Surveyors Association of Nebraska
19
SUN
You can see why measurements are usually made to the tangent trailing edge of the moving SUN

## Slide 20: Astronomy
NGS datasheets often contain a BOX SCORE showing the measured AZIMUTH to nearby objects.
These can be a good resource for a field exercise.
February 9, 2018
Professional Surveyors Association of Nebraska
20
1 National Geodetic Survey, Retrieval Date = OCTOBER 4, 2016
LH1243 ***********************************************************************
LH1243 DESIGNATION - 80 3
LH1243 PID - LH1243
LH1243 STATE/COUNTY- NE/HALL
LH1243 COUNTRY - US
LH1243 USGS QUAD - WOOD RIVER (1993)
LH1243
LH1243 *CURRENT SURVEY CONTROL
LH1243 ______________________________________________________________________
LH1243* NAD 83(1995) POSITION- 40 46 28.66144(N) 098 32 59.95328(W) ADJUSTED
LH1243* NAVD 88 ORTHO HEIGHT - 592.0 (meters) 1942. (feet) VERTCON
LH1243 ______________________________________________________________________
LH1243 GEOID HEIGHT - -24.911 (meters) GEOID12B
LH1243 LAPLACE CORR - -2.14 (seconds) DEFLEC12B
LH1243 HORZ ORDER - SECOND
LH1243|---------------------------------------------------------------------|
LH1243| PID Reference Object Distance Geod. Az |
LH1243| dddmmss.s |
LH1243| CN8485 80 3 RM 1 10.898 METERS 13358 |
LH1243| CN8486 80 3 RM 2 19.983 METERS 23512 |
LH1243| CN8484 80 3 AZ MK 2493549.5 |
LH1243| LH1239 WOOD RIVER MUNICIPAL TANK APPROX. 6.7 KM 3175921.5 |
LH1243|---------------------------------------------------------------------|

## Slide 21: Astronomy
Q. Why Is Astronomy Important in Geodesy?
Because it is the FOUNDATION of all geodetic observations.
The entire United States was surveyed by astronomic observations to set out the passive control marks we have today.
February 9, 2018
Professional Surveyors Association of Nebraska
21
State of Nebraska

## Slide 22: Astronomy
Q. Why Is Astronomy Important in Geodesy?
Sometimes in retracing an old description, it will reference TRUE NORTH.
That was determined by astronomy – or by magnetic bearing corrected for magnetic declination, which was itself measured by astronomy.
A good surveyor knows how it was done then and could still retrace it by the same methods.
February 9, 2018
Professional Surveyors Association of Nebraska
22

## Slide 23: Geodesy
How does Geodesy differ from Astronomy?
  Geodesy seeks to describe the size, shape, and other physical characteristics of the Earth.
  Deeply related to gravity, geology, geometry, and physics.
  Astronomical observations are all conducted relative to the vertical defined by the direction of local gravity
  Geodetic calculations are all computed on the surface of an ellipsoid chosen to represent the Earth
  On a perfect Earth with a perfect choice of ellipsoid there’d be no differences.
  Unfortunately, nothing’s perfect.
February 9, 2018
Professional Surveyors Association of Nebraska
23

## Slide 24: We Must Choose a Reference Surface
We need a reference surface from which to base measurements.
NGS has chosen the equipotential surface that most closely matches the mean sea surface on a global basis as the reference surface.
This surface is called the GEOID.
Then selected an ellipsoid that is a “best fit” to the geoid and whose center is located at Earth’s center of mass.
Compared to a smooth mathematical surface, the GEOID is lumpy.
February 9, 2018
Professional Surveyors Association of Nebraska
24

## Slide 25: Some Trial Geoid Shapes to Consider
February 9, 2018
Professional Surveyors Association of Nebraska
25
least bad choice

## Slide 26: What the Geoid Looks Like
The “geoid” represents the equipotential (level) surface that best approximates the mean sea surface (which is NOT a level surface)
February 9, 2018
Professional Surveyors Association of Nebraska
26
https://earthobservatory.nasa.gov/Features/GRACE/page3.php

## Slide 27: Geodesy
Many astronomic and geodetic concepts are related, but need to be modified and refined for the reality of the Earth.
  Astronomic vs Geodetic
    Vertical
    North
    Azimuth
    Latitude
    Longitude
    Other terms
February 9, 2018
Professional Surveyors Association of Nebraska
27

## Slide 28: Geodesy
Vertical
February 9, 2018
Professional Surveyors Association of Nebraska
28
perpendicular to ellipsoid
perpendicular to geoid = direction of gravity
Angular difference is a few arc-seconds and leads to Laplace correction:
geodetic azimuth = astronomic azimuth + Laplace correction
deflection of the vertical
geoid
ellipsoid

## Slide 29: Geodesy
Laplace Correction
February 9, 2018
Professional Surveyors Association of Nebraska
29
Pole
Horizon
Astronomic North
Setup perpendicular to gravity

## Slide 30: Geodesy
Laplace Correction
February 9, 2018
Professional Surveyors Association of Nebraska
30
Pole
Horizon
Setup perpendicular to ellipsoid
Geodetic North
Astronomic North
Laplace correction = angular difference in azimuth
geodetic azimuth = astronomic azimuth + Laplace correction

## Slide 31: Geodesy
Laplace Correction is listed on appropriate NGS datasheets
February 9, 2018
Professional Surveyors Association of Nebraska
31
1 National Geodetic Survey, Retrieval Date = OCTOBER 4, 2016
LH1243 ***********************************************************************
LH1243 DESIGNATION - 80 3
LH1243 PID - LH1243
LH1243 STATE/COUNTY- NE/HALL
LH1243 COUNTRY - US
LH1243 USGS QUAD - WOOD RIVER (1993)
LH1243
LH1243 *CURRENT SURVEY CONTROL
LH1243 ______________________________________________________________________
LH1243* NAD 83(1995) POSITION- 40 46 28.66144(N) 098 32 59.95328(W) ADJUSTED
LH1243* NAVD 88 ORTHO HEIGHT - 592.0 (meters) 1942. (feet) VERTCON
LH1243 ______________________________________________________________________
LH1243 GEOID HEIGHT - -24.911 (meters) GEOID12B
LH1243 LAPLACE CORR - -2.14 (seconds) DEFLEC12B
LH1243 HORZ ORDER - SECOND
LH1243|---------------------------------------------------------------------|
LH1243| PID Reference Object Distance Geod. Az |
LH1243| dddmmss.s |
LH1243| CN8485 80 3 RM 1 10.898 METERS 13358 |
LH1243| CN8486 80 3 RM 2 19.983 METERS 23512 |
LH1243| CN8484 80 3 AZ MK 2493549.5 |
LH1243| LH1239 WOOD RIVER MUNICIPAL TANK APPROX. 6.7 KM 3175921.5 |
LH1243|---------------------------------------------------------------------|

## Slide 32: Geodesy
The Prime Vertical is a great circle passing through the geodetic zenith from east-to-west.
The prime vertical component of deflection of the vertical leads to Laplace correction.
Meridional component does not.
February 9, 2018
Professional Surveyors Association of Nebraska
32
Celestial Equator
Pole
Zenith
Prime Vertical
East
West

## Slide 33: Geodesy
Astronomic Latitude is the angle from the equator up to the observer’s astronomic zenith.
Geodetic Latitude is the angle from the equator up to the observer’s geodetic zenith.
Affected by meridional component of deflection of the vertical
February 9, 2018
Professional Surveyors Association of Nebraska
33
Pole
Celestial Equator
Zenith

## Slide 34: Geodesy
Latitude affected by Meridional component of deflection of the vertical
February 9, 2018
Professional Surveyors Association of Nebraska
34
perpendicular to ellipsoid
opposite of gravity
meridional component of deflection of the vertical
geoid
ellipsoid
Equator
Astronomic Latitude
Geodetic Latitude

## Slide 35: Geodesy
Longitude affected by Prime Vertical component of deflection of the vertical
February 9, 2018
Professional Surveyors Association of Nebraska
35
Equator
Pole
Zenith
Prime Vertical component of deflection of the vertical
Reference Meridian
Zero
Astronomic Longitude
Geodetic Longitude

## Slide 36: Geodesy
Datums
  Horizontal (NAD27, NAD83)
  Vertical (NGVD29, NAVD88)
Types
  Geometric
  Geopotential
  3D (NATRF2022 – which includes NAPGD2022)
February 9, 2018
Professional Surveyors Association of Nebraska
36

## Slide 37: Geodesy
8 Horizontal Datum Definition Requirements
  Size and Shape of Reference Ellipsoid (2 elements)
  3 Translations (relative to a chosen point on or in the Earth)
  3 Rotations (relative to a chosen point on or in the Earth)
Specifically, the 8 Defining Elements of Horizontal Datum include:
    Semi-major Axis length
    Flattening Ratio
    Latitude of Initial Point
    Longitude of Initial Point
    Ellipsoid Height of Initial Point
    Prime Meridian Deflection of the Vertical at Initial Point
    Meridional Deflection of the Vertical at Initial Point
    Geodetic Azimuth of a Line at Initial Point
February 9, 2018
Professional Surveyors Association of Nebraska
37

## Slide 38: Geodesy
Among the infinite choices for Reference Ellipsoid are the following commonly used ellipsoids with their names:
February 9, 2018
Professional Surveyors Association of Nebraska
38
Ellipsoid Name | Semi-major Axis | Flattening Ratio (approx.)
Airy | 6377563.396 | 299.32
Australian National | 6378160.000 | 298.25
Bessel 1841 | 6377397.155 | 299.15
Clarke 1866 | 6378206.400 | 294.9786982
Clarke 1880 | 6378249.145 | 293.47
Everest | 6377276.345 | 300.80
Fischer 1960 (Mercury) | 6378166.000 | 298.30
Fischer 1968 | 6378150.000 | 298.30
GRS 1967 | 6378160.000 | 298.25
GRS 1980 | 6378137.000 | 298.257222101
Helmert 1906 | 6378200.000 | 298.30
Hough | 6378270.000 | 297.00
International | 6378388.000 | 297.00
Krassovsky | 6378245.000 | 298.30
WGS 60 | 6378165.000 | 298.30
WGS 66 | 6378145.000 | 298.25
WGS-72 | 6378135.000 | 298.26
WGS-84 | 6378137.000 | 298.257223563

## Slide 39: Geodesy
NAD27
  used Clarke 1866 ellipsoid and oriented at Meades Ranch and Waldo.
NAD83
  used GRS80 ellipsoid and tried to orient at mass center of Earth
WGS84
  used WGS84 ellipsoid and tried to orient at mass center of Earth
February 9, 2018
Professional Surveyors Association of Nebraska
39

## Slide 40: Geodesy
Datum-to-Datum Conversion Methods are needed to convert coordinates to-from-between datums.
Several Methods with often confusing names
  3 parameter (NADCON)
  7 parameter (Helmert)
  7 parameter (Bursa-Wolfe)
  7 parameter (Molodensky)
  10 parameter (Molodensky-Badekas)
  14 parameter (scientific community)
Exactness of geometry is often sacrificed for simplicity
February 9, 2018
Professional Surveyors Association of Nebraska
40

## Slide 41: Geodesy
3 parameter (NADCON) cannot model more than a limited patch on the Earth.
DX,DY, DZ here not same as there
February 9, 2018
Professional Surveyors Association of Nebraska
41
NADCON used a 15’ x 15’ grid in CONUS. (About 15 miles x 10 miles). See page 10, NOAA Technical Memorandum NOS NGS-50, 1990.

## Slide 42: Geodesy
7 & 10 parameter are more rigorous and cover a larger area.
14 parameter also includes velocities for the 7-parameters.
Note that in the long-term, the velocities are also changing, so maybe we should consider a 21 parameter solution someday!
February 9, 2018
Professional Surveyors Association of Nebraska
42

## Slide 43: Geodesy
Datum Conversion “mileage chart problem”
Any datum should be convertible to any other datum.
Since large numbers of datums (N) exist, there are (N2) conversions needed.
So, a common datum is used as an intermediary datum.
Scientific community cooperates by creating International Terrestrial Reference Frame (ITRF).
Only need 2N conversions: X>ITRF and ITRF>Y
  But, only need to tabulate N conversions - (then treat as to or from)
Also makes it easier to add a new datum if needed.
February 9, 2018
Professional Surveyors Association of Nebraska
43

## Slide 44: Geodesy
Datum Conversion Table and Parameters
  (https://www.ngs.noaa.gov/CORS/coords.shtml#Col1Exp)
February 9, 2018
Professional Surveyors Association of Nebraska
44
14 parameters

## Slide 45: Geodesy
14 Parameters from NGS
  3 translations, 3 rotations, 1 scale factor
  and 7 Velocities
February 9, 2018
Professional Surveyors Association of Nebraska
45

## Slide 46: Geodesy
Datum Conversion Chart for direct conversions
February 9, 2018
Professional Surveyors Association of Nebraska
46
DATUM NAME | NAD27 | NAD83 | NATRF2022 | AGD84
NAD27 | Null | s dx, dy, dz, ω, φ ,κ | s dx, dy, dz, ω, φ ,κ | s dx, dy, dz, ω, φ ,κ
NAD83 | s dx, dy, dz, ω, φ ,κ | Null | s dx, dy, dz, ω, φ ,κ | s dx, dy, dz, ω, φ ,κ
NATRF2022 | s dx, dy, dz, ω, φ ,κ | s dx, dy, dz, ω, φ ,κ | Null | s dx, dy, dz, ω, φ ,κ
AGD84 | s dx, dy, dz, ω, φ ,κ | s dx, dy, dz, ω, φ ,κ | s dx, dy, dz, ω, φ ,κ | Null
AGD84 = Australian Geodetic Datum 1984
N2 entries
Not needed – these are negatives of the others
½ (N2 – N) entries

## Slide 47: Geodesy
Datum Conversion Chart using intermediary conversions
February 9, 2018
Professional Surveyors Association of Nebraska
47
DATUM NAME | ITRF
NAD27 | s dx, dy, dz, ω, φ ,κ
NAD83 | s dx, dy, dz, ω, φ ,κ
NATRF2022 | s dx, dy, dz, ω, φ ,κ
AGD84 | s dx, dy, dz, ω, φ ,κ
Chart is even simpler using intermediary datum
Only N entries

## Slide 48: HEIGHTS
February 9, 2018
Professional Surveyors Association of Nebraska
48

## Slide 49: Geodesy
Heights above or below a reference surface
  Mean Sea Level Heights
  Ellipsoid Heights
  Orthometric Heights
  Geoid Heights
  Vertical Datums
    1912
    NGVD29
    NAVD88
  Dynamic Heights
February 9, 2018
Professional Surveyors Association of Nebraska
49

## Slide 50: Geodesy
February 9, 2018
Professional Surveyors Association of Nebraska
50
terrain
mean sea level
Height above Mean Sea Level
Positive is UP, negative is down

## Slide 51: Geodesy
February 9, 2018
Professional Surveyors Association of Nebraska
51
ellipsoid
terrain
Height above Ellipsoid
Positive is UP, negative is down
h

## Slide 52: Geodesy
February 9, 2018
Professional Surveyors Association of Nebraska
52
geoid
terrain
Height above Geoid (Orthometric)
Positive is UP, negative is down
H

## Slide 53: Geodesy
February 9, 2018
Professional Surveyors Association of Nebraska
53
geoid
ellipsoid
Geoid Height above ellipsoid
Positive is UP, negative is down
N

## Slide 54: Geodesy
February 9, 2018
Professional Surveyors Association of Nebraska
54
geoid
ellipsoid
terrain
mean sea level
Height above Mean Sea Level
Height above Ellipsoid
Height above Geoid (Orthometric)
Geoid Height
Positive is UP, negative is down

## Slide 55: Geodesy
February 9, 2018
Professional Surveyors Association of Nebraska
55
geoid
ellipsoid
terrain
mean sea level
Height above Mean Sea Level
Height above Ellipsoid
Height above Geoid (Orthometric)
Geoid Height
H
N
h
H = h - N
Note that N is negative in most of CONUS.
Note that h may be negative near coastlines.
Could H be negative?
Positive is UP, negative is down

## Slide 56: Geodesy
Vertical Datums in the United States
  There have been several vertical datums in use across the United States. The earliest ones were “local”, since the leveling did not form an interconnected network.
  The earliest unified datums were the 1912 Datum (4th General Adjustment).
  Followed by the NGVD29 adjustment.
  Followed by the NAVD88 adjustment.
February 9, 2018
Professional Surveyors Association of Nebraska
56

## Slide 57: Geodesy
NGVD29 consists of a leveling network across the United States.
  Leveling was adjusted to fit tide gauges which forced the NGVD29 datum surface to be an approximation of the mean sea surface.
  Unfortunately, the sea surface is NOT level (fails to conform to gravitational potential energy due to salinity, temperature, and currents.
  It seemed like a good idea at the time.
  Resulted in the severely misleading term “Mean Sea Level”.
    Preferred term “mean sea surface”.
February 9, 2018
Professional Surveyors Association of Nebraska
57

## Slide 58: Geodesy
NAVD88 consists of a leveling network on the North American Continent, ranging from Alaska, through Canada, across the United States, affixed to a single origin point on the continent.
  Leveling was adjusted “internally” and tied to only 1 point – Pointe au Pere (Father’s Point) in Quebec
    Tide Station & Location = Pointe-au-Pere, Rimouski, Quebec, Canada
    Located in corner of a school building at Rue St Germaine and Goulet Avenue
    PID = TY5255
    Bench Mark = 1250 G
    Height above LMSL = 6.271 meters
February 9, 2018
Professional Surveyors Association of Nebraska
58

## Slide 59: Geodesy
February 9, 2018
Professional Surveyors Association of Nebraska
59
terrain
Height above Mean Sea Level
Height above Ellipsoid
Height above Geoid (Orthometric)
Geoid Height
ellipsoid
geoid
mean sea level
v
NAVD88
NGVD29
As if we weren’t confused already, let’s add the datum surfaces to the diagram.
v
1912
The datums are NOT parallel, nor smooth.

## Slide 60: Geodesy
Vertical Datum Conversions
  There is NO SINGLE VALUED conversion between 1912, NGVD29, nor NAVD88.
    Datums are not parallel.
    Datums are not smooth.
    Underlying leveling is not error-free.
Must research the relationship among the known published datum heights for specific passive marks in the area of interest.
Devise a diagram for your local area.
  See “Digging for Datums” by David Zenk (2012)
  Sample next slide - - - >
February 9, 2018
Professional Surveyors Association of Nebraska
60

## Slide 61: Draw a DATUM PROFILE
February 9, 2018
Professional Surveyors Association of Nebraska
61
Dresbach, MN
(PBM 182)
Elevation above datum = Depth to datum
0.013 m
0.071 m
0.078 m
2.148 m
St. Paul, MN
(PBM 67)
NAVD88
1912
NGVD29
Memphis
Mean Gulf
0.046 m
0.098 m
0.003 m
2.222 m
NAVD88
1912
NGVD29
Memphis
Mean Gulf

## Slide 62: Geodesy
Dynamic Heights
  A dynamic height is directly related to the amount of potential energy at a given point.
  As an object is raised it acquires gravitational potential energy.
  Potential energy = Work Done in raising a weight through a Distance
  PE = D x F
February 9, 2018
Professional Surveyors Association of Nebraska
62
F = Weight
F = Mass x Gravity
F = 1 kg x 9.8 m/sec2
D = Distance (m)
D = 1 m
PE = 1 m x 1 kg x 9.8 m/sec2
PE = 9.8 kg m2/sec2

## Slide 63: Geodesy
Note that gravity varies over distances, so equal potential energy surfaces are not parallel.
February 9, 2018
Professional Surveyors Association of Nebraska
63
F = Weight
F = Mass x Gravity
F = 1 kg x 9.8 m/sec2
D = Distance (m)
D = 1 m
PE = 1 m x 1 kg x 9.8 m/sec2
PE = 9.8 kg m2/sec2
F = Weight
F = Mass x Gravity
F = 1 kg x 9.7 m/sec2
D = Distance (m)
D = 1.01 m
PE = 1.01 m x 1 kg x 9.7 m/sec2
PE = 9.8 kg m2/sec2
weaker gravity zone
stronger gravity zone

## Slide 64: Geodesy
Equal PE but not equal distances.
Geopotential surfaces are not parallel, but ARE level.
February 9, 2018
Professional Surveyors Association of Nebraska
64
PE = 9.8 kg m2/sec2
D = 1.01 m
D = 1 m
PE = 9.8 kg m2/sec2
PE = 0 kg m2/sec2
PE = 0 kg m2/sec2

## Slide 65: Geodesy
Every geopotential surface could be computed and labeled with its Geopotential Number.
All such geopotential surfaces directly denote level surfaces.
Water does not flow along these level surfaces.
A set of Geopotential Numbers can be divided by a constant amount and all resulting numbers are still in proportion and still represent a series of level surfaces.
So choose to divide by normal gravity at 45⁰ latitude (9.806199 m/sec2) and by 1 kg.
Result is a Dynamic Height whose unit is meters, but is not an actual height – it is merely a label for a level surface.
February 9, 2018
Professional Surveyors Association of Nebraska
65

## Slide 66: Geodesy
Here’s what NGS has to say about DYNAMIC HEIGHTS near the Great Lakes
Special Note on IGLD 85 Heights
Dynamic heights are relevant near large bodies of water such as reservoirs or very large lakes, so the Great Lakes are an ideal candidate for dynamic heights. However, the Great Lakes are referenced to the International Great Lakes Datum of 1985 (IGLD 85) dynamic heights. The difference between IGLD 85 dynamic heights and NAVD 88 dynamic heights is known as a hydraulic corrector. An application which includes these hydraulic correctors is available for users who wish to compute IGLD 85 heights directly.
February 9, 2018
Professional Surveyors Association of Nebraska
66

## Slide 67: Geodesy
February 9, 2018
Professional Surveyors Association of Nebraska
67

## Slide 68: End
February 9, 2018
Professional Surveyors Association of Nebraska
68
Dave Zenk PE, LS
National Geodetic Survey
Northern Plains Regional Advisor 1735 Lake Drive West
Chanhassen, MN 55317-8581
763-600-6912 home office 952-368-2548 office 612-414-9522 mobile dave.zenk@noaa.gov (federal business) zenkx002@umn.edu (personal business)