## Slide 1: GEOID12 Technical Details
Daniel Roman1, Xiaopeng Li2, and Simon Holmes3
1 Geosciences Research Division, NGS, NOAA, Silver Spring MD
2 Earth Resources Technology (ERT), Inc., Silver Spring MD
3 Stinger Ghaffarian Technology (SGT) Inc., Greenbelt MD
The Survey Summit
Sunday, 22 July 2012 (Manchester Grand Hyatt), Geodesy Session, 1030-1200

## Slide 2: Basic Concepts on Modeling
Start with a gravimetric geoid (USGG2012)
Use control data to fit to local datums
  Appropriate versions of NAD 83
  Respective local Vertical Datum (if one exists)
Use LSC to determine correlated signal
For complex areas (e.g., CONUS), use MMLSC
Apply grid of correlated signal to USGG2012
Results in GEOID12 with high frequency nature from USGG2012 but fit to local control

## Slide 3: Hybrid Geoid Height Models (e.g., GEOID12), Gravimetric Geoid Height Models (e.g., USGG2012) and Conversion Surfaces using GPS on BM data
Gravimetric Geoid systematic misfit to BM’s but best fits “true” heights
Hybrid Geoid “converted” to fit local BM’s, so best fits NAVD 88 heights
Conversion Surface model of systematic misfit derived from BM’s in IDB
Earth’s Surface
h
h
h
h
h
H
H
H
H
H
N
N
N
N
N
Ellipsoid
Hybrid Geoid
Gravimetric Geoid
-0.737 M in
Salt Lake –
2009 model
Notes: Salt Lake City North ZLC A AA3680 40 47 06.80308 (N) 111 57 09.07339 (W)
GEOID09: -16.943 + -0.717 - -16.923 = -0.737
GEOID03: -16.958 + -0.717 - -17.266 = -0.409

## Slide 4: USGG2012 – USGG2009
Notes: -USGG2009-USGG2003 changes were about an order of magnitude greater – reflecting incorporation of GRACE
-Now changes derive from GOCE – more at the dm-level and below
-future changes will likewise be smaller still

## Slide 5: Control Data for GEOID12 Modeling
Region | Reference Frame | Vertical Datum | # GPSBM used (# Rejected) | #OPUSDB used (# Rejected)
CONUS | NAD 83 (2011) | NAVD 88 | * 24,003 (868) | 478 (258)
- VTDP Region | NAD 83 (2011) | NAVD 88/VTDP | 357 (153) | 1 (17)
Alaska | NAD 83 (2011) | NAVD 88 | ** 105 (4) | 2 (1)
Puerto Rico | NAD 83 (2011) | PRVD 02 | 38 | 0
U.S. Virgin Islands | NAD 83 (2011) | VIVD 09 | 21 (3) | 0
Hawaii | NAD 83 (PA11) | Geoid (W0) | n/a | n/a
American Samoa | NAD 83 (PA11) | ASVD 02 | 19 (3) | 0
Guam | NAD 83 (MA11) | GUVD 04 | 33 | 0
CNMI | NAD 83 (MA11) | NMVD 03 | 55 | 0
* Supplemented by 574 (5 rejected) in Canada and 674 (70 rejected) in Mexico
** Supplemented by 88 (2 rejected) in Canada
http://www.ngs.noaa.gov/GEOID/GEOID12/GPSonBM12.shtml

## Slide 6: Ellipsoid Height Changes (NA2011-NA2007)

## Slide 7: Rejections based on adjustment error (NA2011 => ‘h’ Reject code)

## Slide 8: Rejections based on adjustment error (NA2011 => ‘h’ Reject code)

## Slide 9: Orthometric Height Changes (mm)

## Slide 10: Orthometric Height Changes (mm)

## Slide 11: Large error points (‘H’ Reject)

## Slide 12: Distribution of OPUSDBBM12

## Slide 13: Distribution of OPUSDBBM12

## Slide 14: MMLSC for CONUS with and without (w/o) OPUSDBBM12

## Slide 15: GEOID12 with OPUS

## Slide 16: GEOID12 without OPUS

## Slide 17: The Impact of OPUS

## Slide 18: GEOID12 Error Map for Southwest
Triangles show locations of GPSBM2012 & OPUSDBBM12 control points.
Error increases based on the size of the gap.
Dense coverage yields < 1 cm.
Errors will be provided with GEOID12 hts.

## Slide 19: Inverse Distance Plot to Control Data (Interpolation Gap Magnitude)

## Slide 20: Inverse Distance Plot to Control Data (Interpolation Gap Magnitude)

## Slide 21: An additional 6,000 points?

## Slide 22: GEOID12 – GEOID09

## Slide 23: GEOID12 – GEOID03
Same
Scale
as 12-9

## Slide 24: Summary
GEOID12 is complete for all regions
It converts between NAD 83 (**11) and the local vertical datum (NAVD 88 in CONUS)
Modeling is much the same as before (MMLSC)
Incorporation of data in Mexico and OPUSDBBm12 is new and has had an impact
Error maps will be available to provide estimated errors along with geoid heights

## Slide 25: Questions?
Geoid Models Page:
  http://www.ngs.noaa.gov/GEOID/
GRAV-D Page:
  http://www.ngs.noaa.gov/GRAV-D/
Geoid Team: 301-713-3202
  Dan Roman (x161), Yan Wang (x127), Xiaopeng Li (x210)