## Slide 1
Gravity for the Redefinition of the American Vertical Datum (GRAV-D) Update
Monica Youngman
GRAV-D Project Manager
Simon Holmes
Geoid Researcher
Webinar Series
National Geodetic Survey
February 9, 2017

## Slide 2: Agenda
  Purpose of Airborne Gravity
  GRAV-D Project
    Scope and Methods
    Data Collection Status
    Research and Development
  Future Updates and Impacts
    Maintenance Plans
    Experimental Geoids
  Impacts to the Geoid in Alaska

## Slide 3
Part 1: Purpose of Airborne Gravity

## Slide 4: NGS Mission Statement
To define, maintain and provide access to the National Spatial Reference System (NSRS) to meet our nation’s economic, social, and environmental needs.
The NSRS is a consistent coordinate system that defines latitude, longitude, height, scale, gravity, and orientation throughout the United States.

## Slide 5: The National Spatial Reference System supports
Emergency Response Imagery, Flood zones for the
National Flood Insurance Program
Federal Emergency Management Agency
Levee Safety Program to determine levee heights & positions
United States Army Corps of Engineers
NSRS gravity data for the geospatial mission of NGA
National Geospatial-Intelligence Agency
Topographic Maps and interior water data for the nation
United States Geological Survey
Nautical charts, among many other geospatial applications
National Oceanic and Atmospheric Administration
Aeronautical Data Quality Assurance
Federal Aviation Administration

## Slide 6
Geodetic Datums
  Horizontal
  2-D (Latitude and Longitude) (e.g. NAD 27, NAD 83 (1986))
  Vertical/Geopotential
  1-D (Orthometric/Dynamic Height) (e.g. NGVD 29, NAVD 88, IGLD 85)
  Geometric
  3-D (Latitude, Longitude and Ellipsoid Height)
  Fixed and Stable(?) - Coordinates seldom change
  (e.g. NAD 83 (1993), NAD 83 (2007), NAD 83 (2011))
  also
  4-D (Latitude, Longitude, Ellipsoid Height, Velocities)
  Coordinates change with time
  (e.g. NAD 83, ITRF00, ITRF05)

## Slide 7: NAVD 88: Current Vertical Datum
NAVD 88: North American Vertical Datum of 1988
  The surface of equal gravity potential to which orthometric heights shall refer in the United States
How Defined:
  Massive leveling and gravity campaign across the country in the 1980’s yielded measurements at >500,000 benchmarks
  Minimally constrained adjustment of level/gravity data, holding geopotential value fixed at one point: 6.271 meters (along the plumb line) below the geodetic mark at “Father Point/Rimouski”
Realization:
  NAVD 88 is only defined at these benchmarks.
Father Point Lighthouse Quebec, Canada
Notes: By fixing the geopotential value at the origin point, it was possible to ensure that the origins of IGLD 85 and NAVD 88 aligned.
*It should be pointed out that while the datum was defined in such a way as to be usable on the North American continent, it was never actually adopted in Canada. It can be used there, but it’s not their official civilian datum.
Note that the designation of the vertical control point at Father Point is “1250 G=NAVD 88 DATUM POINT” for PID# TY5255 and is not available from the publicly accessible NGSIDB.

## Slide 8
1954-2017: Subsidence
House
BM
House
BM
1954: Leveling Performed
to bench mark
2017: Published NAVD 88 height for this BM is from 1954 leveling
The published NAVD 88 height is no longer the true height for this BM
H88(published)
H88(true)
NAVD 88 zero height surface
Subsidence and Bench Mark Height

## Slide 9
Approximate mismatch between NAVD 88 (zero surface) and the global geoid (i.e. sea level)
NAVD 88 Problems
Notes: This map reflects the sort of height changes that users could expect if NAVD 88 were replaced with a geoid-based vertical datum.
This is only a large scale approximation and should not be used as an absolute guide. Each benchmark might have its own level
Of mismatch, say from uplift or subsidence, not captured by this broad brush.
Also, this is the difference between the zero level of NAVD 88 and the actual geoid. The difference between NAD 83 ellipsoid heights and
ITRF/GRS-80 ellipsoid heights has NO influence on this graph and should not be part of the story.
Updated October 2010

## Slide 10: Modernizing the Datum
Problems:
  Gaps in gravity data coverage
  Inconsistent terrestrial surveys
  No medium wavelength information
Ex. Southern U.S. Coast
20-100 km gravity gaps along coast
Goal:
  Achieve 2 cm accurate heights where possible
  Use gravity data to achieve a 1 cm accurate geoid (leaving 1 cm for GNSS uncertainty)

## Slide 11
Building a Gravity Field
Long Wavelengths
(≥ 250 km)
GRACE/GOCE/Satellite Altimetry
Intermediate Wavelengths
(500 km to 20 km)
Airborne Measurement
Surface Measurement and
Predicted Gravity from Topography
Short Wavelengths
(< 100 km)
+
+

## Slide 12
Part 2: The GRAV-D Project

## Slide 13: GRAV-D Project Overview
Overall Target: 2 cm accuracy orthometric heights from GNSS and a geoid model
GRAV-D Goal: Create gravimetric geoid accurate to 1 cm where possible using airborne gravity data
GRAV-D: Two thrusts of the project
  Airborne gravity survey of entire country and its holdings
  Long-term monitoring of geoid change
Leveraging partnerships to improve and validate gravity data
Notes: Target is to be able to achieve 2 cm accuracy orthometric heights (where possible) using a GNSS receiver and a geoid model
Roughly 1 cm uncertainty from GNSS and 1 cm from the geoid model
GRAV-D
Phase 1: snapshot of the entire country to provide a consistent data set
Phase 2: long term monitoring of geoid change – in development
Work with partners to incorporate additional gravity data, particularly surface gravity data, validate existing data, and monitor change

## Slide 14: Data Collection Scope
Entire U.S. and territories
  Total Square Kilometers: 15.6 million
  Initial target area for 2022 deadline
  ~200 km buffer around territory or shelf break if possible
Notes: Project Scope:
Scope of the project: cover roughly 15.6 million square kilometers – contiguous united states, Alaska, Hawaii, Guam, and American Samoa
In order to blend with satellite altimetry data the airborne survey is done to the continental shelf where possible or ~ 200 km beyond the shoreline or border, whichever is further
Deadline of 2022 for datum rollout, which means a target of 2021 to finish the airborne survey
Priority areas were defined as Alaska and coastal areas
Challenges:
Fixed annual budget and time  design of surveys had to fit within an annual budget of $3.5 million and meet the deadline
This was a major factor in setting altitude and line spacing

## Slide 15: Priority Order for Surveys
Greatest Datum Needs
Alaska
Coastal US & Great Lakes
Hawaii & Pacific Islands
Aleutians
Interior CONUS
  Mountains first
Other Variables to Consider
Need to meet annual collection metric
Aircraft availability and capability
Appropriate season for measurement
Contract fuel availability
Notes: NGS evaluated the US and all of its territories and established a priority order according to the where the datum is in greatest need of repair. Alaska has the biggest need, so tops the list. Next in priority are the coastal regions of the US and the Great Lakes. Then the Hawaiian and Pacific Islands, the Aleutians, and then interior CONUS. The mountainous regions have the greatest geoid errors and will get our first attention. The actual order we fly the surveys is also informed by the availability of aircraft, the appropriate seasons for measurement, the availability of government contract fuel, and the coordination of logistical constraints so as to most efficiently use our resources.

## Slide 16: Performance Metric For Airborne Surveys
Measure: Percentage of the U.S. and its territories with GRAV-D data available
to support a 1 cm geoid supporting 2 cm orthometric heights.
FY09 Baseline | Targets vs Actual |  |  |  |  |  |  |  |  |  |  |  | 
 | FY10 | FY11 | FY12 | FY13 | FY14 | FY15 | FY16 | FY17 | FY18 | FY19 | FY20 | FY21 | FY22
6.14% | 7.5% | 12% | 20% | 28% | 36% | 45% | 53% | 62% | 70% | 79% | 87% | 96% | 100% and Implement
6.14 | 8% | 15% | 24% | 31% | 38% | 45% | 55% | 58% |  |  |  |  | 
Notes: We’ve set up a basic GIS GPRA monitoring in the War Room. We will report the coordinates of our survey monthly and they will calculate our percentages.

## Slide 17: GRAV-D Status 3-1-16: 49%

## Slide 18: GRAV-D Status 1-31-17: 58%

## Slide 19: Survey and Block Plans
Blocks designed based on aircraft capabilities, available airports, and target area
Data lines spaced 10 km apart
Cross lines spaced 60-80 km apart
Flight altitude 20,000 ft
Nominal speed 220-250 kts
Notes: Block layout based on aircraft, adjust size of block if needed

## Slide 20: Gravity Tie and GPS Base Stations
Parking spot ID
A10 measurement
Vertical gravity gradient
GPS Base Stations

## Slide 21: GRAV-D Aircraft
US NOAA
  Gulfstream Turbo Commander Jet Prop
  NOAA P-3 Hurricane Hunter
US Bureau of Land Management
  Pilatus PC-12
US Naval Research Lab
  King Air RC-12
Dynamic Aviation (contractor)
  King Air 200T
Aurora Flight Sciences (contractor)
  Centaur OPA
Fugro (contractor)
  King Air E-90A
  Cessna Conquest
Pilatus PC-12
King Air E-90A
Centaur OPA
NOAA P-3 (background) NOAA Turbo Commander (foreground)
Notes: GRAV-D surveys have been operating on a number of aircraft. In order to accomplish our objectives within budget, we utilize a “portfolio” of aircraft of both government and contract origin. We’ve used the NOAA Jet Prop and the P-3, although little opportunity exists for further use of these aircraft. We operate about five months/year aboard the BLM Pilatus PC-12 aircraft. This aircraft is used for fire-spotting during warmer weather months in AK and the western US. This year we began working with Fugro to provide us aircraft services. We plan also to work this year with the Naval Research Lab and the VXS-1 Navy Squadron aboard their RC-12 King Air aircraft.

## Slide 22
Data Collection
Equipment
  Micro-g TAGS III Air-Sea Gravimeter
  GNSS Antenna and Receiver on aircraft
  NovAtel SPAN Inertial Measurement Unit with Honeywell µIRS IMU
  At least 2 GNSS antennas and receivers at the airport
Installation
  Lever arm
  Ground testing
  Test flight
Micro-g LaCoste TAGS Gravimeter
NovAtel SPAN-SE
Notes: Equipment
Gravimeter: Micro-g TAGS III Air-Sea Gravimeter
GPS Antenna and Receiver
NovAtel SPAN IMU
Data Collection
Blocks are designed with data lines spaced at 10 km and cross lines at 80 km
Flights conducted at 20,000 feet or about 6,000 m
Speed is roughly 250 kts
Survey design was heavily influenced by the timeline and amount of coverage needed – flying lower was considered, but

## Slide 23: Airborne Surveying Challenges
Goal is two flights per day when/if:
  Weather/atmosphere is calm (meter cannot tolerate turbulence)
  Instruments and aircraft are in working order
  Good GPS geometry, no GPS jamming
  Military airspaces are not “hot”
  We have the operators/pilots to support two flights per day

## Slide 24
Field Quality Control Processing
  Lever arm applied
  Differential kinematic positioning in the field
  Gravity processed with in-house software (Issac)
  Identify lines needing reflights
Final Processing
  GPS/IMU combined solution using Precise Point Positioning
  Gravity processed with in-house software (Newton)
  Quality evaluated and data minimally trimmed
  Processed data and documentation released
Data Processing
Notes: Data Processing
In the field a differential GPS-IMU solution is used to evaluate daily whether flights need to be reflown because precise ephemeris are not available
Final processing is done using Precise Point Positioning (PPP) – an analysis was done comparing differential and PPP, there was either no effect or small improvements in the gravity solutions from PPP
Gravity processing done using in-house software, Newton, which applies the absolute gravity tie, removes drift, and applies a vertical acceleration, Eotvos, and offlevel corrections and then is filtered three times with a time-domain frequency filter
End of line trimming
Data documentation produced and package released on the website
This plot is an example of part of the output. We aim for +/- 5 mGals from EGM08 – as you can see in this plot there is a significant section that deviates from that. However, part of the goal of the airborne campaign is to improve upon EGM08, so while it is a good guide, it cannot be the final determination. This line, for example, if you compare to an adjacent line it looks like this.

## Slide 25
Lake Michigan
Notes: These are two lines over Lake Michigan where the airborne data (blue) shows significant deviations from EGM08 (Green). However, the x-axis is latitude and you can see that the deviations are supported independently by both lines. This type of visual analysis is extremely useful day-to-day in the field as we determine which lines need to be reflown. In the final processing we also do line to line cross correlation to evaluate overall line agreement.

## Slide 26: Internal Validation
Internal Validation
  Crossover analysis
  Line to line comparison
  Line reflights
Data Release
  These quality control measures are why partial blocks are not released
Notes: Internal:
Start with internal comparison
Crossover analysis compares intersection points, aim for RMS of residuals of less than 5 mGals – identifies errors that may need to be removed
Line to line comparison, as was shown earlier, but look at the cross correlation of the entire block
Reflights of lines provide repeatability statistics
External:
Geoid comparison --
Compared to EGM08 the airborne data often agrees with the satellite gravity
Most updates are seen in areas of poor data coverage
Shown is Lake Michigan, the gridded airborne data, EGM2008 versus GOCE, and then adding the airborne data to EGM2008 and again comparing with GOCE
GSVS –
Three surveys: first flat and low gravity signal, second flat and high gravity signal, third rugged and high gravity signal
First is completed and published, second completed and papers in progress, third in the planning stages
2011 survey confirmed that the airborne gravity was contributing to the goal of a 1 cm accurate geoid

## Slide 27: GRAV-D Website
http://www.ngs.noaa.gov/GRAV-D

## Slide 28: Part 3: Future Updates and Impacts

## Slide 29: After 2022- Updates to the Datum
Develop a long-term geoid-monitoring service
  Will there be new satellite data?
  Monitoring will depend on gravity signals that affect geoid change, this could include:
    A tracking network
    Repeat gravity measurements, airborne or terrestrial
    Geophysical models
  Current project underway to evaluate how to monitor changes

## Slide 30
Geopotential Datum Changes
USGG2012
Notes:   Approximately +0.1 m (Florida) to -1.3 m (Washington)
  More than 2 meters of change in Alaska

## Slide 31: Experimental Geoids
The gravity data from satellites, airborne, corrected surface data, and terrain predictions will be blended into a gravity field
Methods for blending will be tested to prepare for 2022
Available on the Website
http://beta.ngs.noaa.gov/GEOID/xGEOID/

## Slide 32: Experimental Geoids
Annually update an experimental gravimetric geoid with GRAV-D data
  Evolution as we move
    from USGG2012 (last non-GRAV-D gravimetric geoid)
    through xGeoid201X (annual experimental geoid)
    to USGG2022 (the final geoid with GRAV-D)
  Each model published in June with all data released by the previous December
  Starting 2014: requirement for annual experimental geoid

## Slide 33: Part 4: Impacts to the Geoid in Alaska

## Slide 34: Summary
GRAV-D currently at 58% complete and on track to finish data collection in 2022
All studies show improvement with the airborne gravity data, although areas with current poor information show more improvement
Expected height changes up to around 1 meter in CONUS and around 2 meters in Alaska
Thank you for your attention!