## Slide 1
Intro to OPUS Projects?
New Hampshire Land Surveyors Association
December 02, 2022
Dan Martin
Northeast Regional Geodetic Advisor
ME, NH, VT, MA, CT, RI, NY, NJ
Dan.martin@noaa.gov
240-676-4762

## Slide 2
THE FOLLOWING PREVIEW HAS BEEN APPROVED FOR
ALL SURVEY AUDIENCES
BY THE NATIONAL GEODETIC SURVEY
THE TOOL ADVERTISED HAS BEEN RATED
TR-13
ABOUT 13 TRAINING HOURS REQUIRED
KNOWLEDGE IN THE USE OF GPS STRONLY SUGGESTED
USEFUL VISUALIZATION, MANAGEMENT AND PROCESSING TOOLS CONTAINED WITHIN

## Slide 3: Operating systems and browsers.
No guarantee that OPUS Projects will work with your computer is implied. It has been successfully tested on X86 PC’s in various combinations of the following…
Operating systems: Linux® and Microsoft Windows ®
Browsers: Chrome™ Firefox® Internet Explorer® 8 through 10 Opera® Safari®

## Slide 4: What is OPUS Projects?
OPUS Projects offers Web-based access to simple visualization, management and processing tools for multiple marks and multiple occupations. Some of its advantages include:
Data uploading through OPUS.
Processing using the PAGES software.
Graphical visualization and management aids.
Significant support of bluebooking (submitting to NGS for publication).

## Slide 5: Why complicate OPUS?
solution HATFIELD
solution MCCOY
OPUS
Session
Adjustment
CORS1
CORS2
CORS3
CORS4
CORS5
Notes: OPUS solutions are independent of each other, but they may be indirectly related …
Marks might “share” their environment (similar atmosphere over both).
Data might “share” the same GNSS constellation geometry.
OPUS solutions may “share” some or all of the same CORS.
Etc.
These correlations can increase with project size.

## Slide 6: Why complicate OPUS?
session 001
solution HATFIELD
solution MCCOY
OPUS
Session
Adjustment
CORS1
CORS2
CORS3
CORS4
CORS5
Notes: Combining your data logically can improve results:
Neutral atmosphere (tropo) corrections can be improved which, in turn, can help with other things like phase ambiguity resolution.
Common mode effects, like baselines connecting the same CORS common to different marks, can be de-correlated.
OPUS Projects tries to logically group data together:
Data from the same mark are associated with that mark.
Marks simultaneously occupied are grouped into sessions. Session processing improve consistency and accuracy.

## Slide 7: Why complicate OPUS?
session 001
solution HATFIELD
solution MCCOY
OPUS
Session
Adjustment
CORS1
CORS2
CORS3
CORS4
CORS5
session 002
session N
Notes: These concepts can be extended to other marks and other sessions.

## Slide 8: Why complicate OPUS?
network adjustment
session 001
solution HATFIELD
solution MCCOY
OPUS
Session
Adjustment
CORS1
CORS2
CORS3
CORS4
CORS5
session 002
session N
Notes: Ultimately, combining session solutions into an adjustment can improve accuracy for the entire network.

## Slide 9
2 cm
2 cm
4 cm (0.16 ft)
X
X (m) | X(ft) |  | accuracy
100 | 328 | 00-01-22 | 1:2,500
200 | 656 | 00-00-41 | 1:5,000
300 | 984 | 00-00-28 | 1:7,500
400 | 1312 | 00-00-21 | 1:10,000
800 | 2624 | 00-00-08 | 1:20,000
Geometric Geodetic Accuracy Standards and Specifications for using GPS Relative Positioning Techniques

## Slide 10: What’s in it for me?
OPUS solutions = pretty good, but each treated as independent and assumes “perfect” CORS.
Sessions = simultaneously-observed marks processed together in sessions increases consistency.
Adjustments = interlinking sessions through network adjustments increases accuracy.

## Slide 11: Do we really need another OPUS version?
The practical answer is probably yes. The NGS and other groups have a history of projects whose specifications can’t be entirely supported by OPUS.
The academic answer is probably yes. As good as OPUS does, and that is very good indeed, sacrificing simplicity for flexibility can improve results.

## Slide 12: What does this mean operationally?
Plan your project
Collect data and metadata (photos and mark descriptions)
Gather data and metadata onto one computer
Process the data
Perform a network adjustment
Publish (if desired)
Notes: Very broadly, you probably go through these or very similar steps for every project.

## Slide 13: What does this mean operationally?
Plan your project
Create an OPUS project
Collect data and metadata
Upload data to your project using OPUS
Process sessions
Perform network adjustment
Publish (if desired).
Notes: The steps when using OPUS Projects are very similar, but the steps in black use OPUS Projects rather than your own resources.

## Slide 14: What does this mean operationally?
Admittedly an oversimplification, nevertheless there is value in thinking of OPUS Projects as four steps with an optional fifth step.
Creating A Project
Uploading Data
Session Processing
Network Adjustment
Publishing to the NGS Integrated Database
Notes: Publishing to the NGS Integrated Database is covered separately (Bluebooking using OPUS Projects).

## Slide 15: The steps represented graphically.
Processor or Manager
Data &
Metadata
Network
Adjustment
Manager
Session
Solution
Session
Solution
Session
Solution
Session
Solution
Copy To User
Your OPUS Project
Copy To User
Copy To User
OPUS Solution
OPUS Solution
OPUS Solution
Publish To NGSIDB
Notes: Projects exists on an NGS server and are only accessible through the OPUS Projects Web interface.
The entire white box represents a project.
The allocation of resources for a project is step 1.
The orange icons on the left represent step 2: uploading data into the project.
The green icons in the middle represent step 3: processing individual sessions and solution quality control.
The blue icons on the right represent step 4: network adjustment.
The purple icons on the far right represent the publishing options.

## Slide 16: Are there any side effects?
Exploiting a Web-based application like OPUS Projects can mean:
Less backtracking.
  Data consolidated while teams are in the field.
  Rapid data quality assessment.
Simpler logistics.
  Data are immediate availability through on-line storage.
  Automated organization.
Less worry.
  Share information.
  Share results.

## Slide 17: Limitations?
Uploads through OPUS-Static.
  Dual-frequency (GPS only).
  2 hrs ≤ data span ≤ 48 hrs (≤ 2 GPS midnights).
  Observation interval = a factor of 30 (seconds).
Minimum project size.
  None
Maximum project size.
  There are practical limits to a project’s maximum size.
  About 100 marks in a single session.
  Number of data files < a few hundred.
Notes: The number of data files < a few hundred implies:
A few marks occupied many times.
Many marks occupied a few times.

## Slide 18: G.I.G.O.
We still need surveyors. We hope OPUS Projects can help, but it can’t do your job for you.
Follow your project’s specifications.
Use best practices and careful field procedures.
Select permanent marks of public interest.
Good coordinates come from good data.
http://gis.larc.nasa.gov/
Notes: G.I.G.O. = garbage in, garbage out

## Slide 19: A Little Background Information
Understanding a little about how processing is done within OPUS Projects informs your planning and helps ensure that you observation meet your project needs.
Plan the work and work the plan

## Slide 20: Independent vs Dependent Baselines
Number of independent (non-trivial) baselines = n-1
Total number of baselines = n(n-1)/2
Independent (non-trivial)
Dependent (trivial)

## Slide 21: Sequential or (Baseline) Processing vs Simultaneous or (Session) Processing
Baseline Solution
  One baseline at a time
  Ignores mathematical correlations between baselines observed in the same session.
  Must include all independent and dependent baselines for each session
  Must be properly scaled before combining sessions into network adjustment
Session Solution
  Solution from simultaneous processing of all independent baselines with mathematical correlations between baselines

## Slide 22: Which Baselines to Create? (non-OPUS Projects)

## Slide 23: Independent Baselines Only by Session

## Slide 25: OPUS Projects uses Session Processing
By default, independent baselines for each session are created from a single “HUB”
  Think of the hub and spokes of a wheel
By default, OPUS Projects will select the most central CORS within a session and designate it as the HUB
The relationship between all (non-HUB) marks (dependent baselines) are represented by mathematical correlations.
This approach has some significant benefits, and will be discussed further in the session processing module.

## Slide 27: GNSS Vector EXchange Format (GVX)
Website: https://www.ngs.noaa.gov/data/formats/GVX/index.shtml
Detailed documentation
Schema (XSD)
Example vector files
GVX is written in Extensible Markup Language (XML)
Designed to store and carry data in plain text format
Flexible representation of arbitrary data structures
Extensible – new elements can be added later without breaking applications
Both machine-readable and human-readable
Schemas can be used to define “must haves” and “should haves”

## Slide 28: Design for OPUS-Projects and GVX
[Adapted from Weaver et al. 2018]
GVX file (from RTK survey or baseline processing in other software)
500-800 km
OPUS-Projects (from static GNSS session processing)
RTK Base or “From” Mark
RTK Rover or “To” Mark
Vector
Vector in GVX File
500-800 km

## Slide 29: Three Cases for RTK/RTN Bases
RTN Base = CORS
Automatically attaches GVX vectors to official coordinates for CORS
Constrain CORSs
RTK/RTN Base = Not a CORS and new to NGS
Upload static GPS data logged at the base during the days of the RTK survey
Perform session baseline processing to connect to CORSs
Constrain CORSs
3. RTK/RTN Base = Not a CORS but has a datasheet
Could constrain coordinates on datasheet
Or, upload static data at the RTN base, logged during the days of the RTK survey; perform session baseline processing; constrain CORSs

## Slide 30: Network Design and Schedule Considerations
Which marks to include in an observation session?
Standard/Specification
  Session length
  Number of occupations
  Repeat occupation criteria
  Baseline length
  Ties to existing passive marks
Resources available
  Equipment
  Observers
Field constraints
  Travel between stations
  Site access
  Site safety

## Slide 31: Which Marks to Observe together in a Session
Marks that are intervisible, e.g., a mark and it’s azimuth mark
Any group of marks for which relative “Local Accuracies” are desired
  Points that will control the beginning and end of a future traverse
  Any place where you want to maximize the internal precision between points
Existing Passive Control (especially vertical) and nearest neighbors
Vertical Control
Real Time Base Station

## Slide 32: Network Design and Schedule Considerations
Which marks to include in an observation session?
Standard/Specification
  Session length
  Number of occupations
  Repeat occupation criteria
  Baseline length
  Ties to existing passive marks
Resources available
  Equipment
  Observers
Field constraints
  Travel between stations
  Site access
  Site safety

## Slide 33
 | Requirement | PRIMARY | SECONDARY | LOCAL
4.1 | Requirements for ALL METHODS Repeat occupations and offset time | Offset sessions/occupations by 3 to 21 hours. See Specifications for detailed explanation. |  | 
4.2 | Requirements for OPUS PP Required TOTAL Static GNSS Observation Time (T) Recommended GNSS Session Durations | 0 to 200 km T = 20 hours (2) 10 hour sessions or (3) 7 hour sessions or (4) 5 hour sessions Requires at least 1 session on a different day. | 0 to 100 km T = 4 hours 0 to 150 km T = 6 hours 0 to 200 km T = 8 hours (2) 2 hour sessions (2) 3 hour sessions (2) 4 hour sessions | 0 to 200 km T = 4 hours (2) 2 hour sessions
Table 4 - Standards for Observation Requirements by Method
4.3 | Requirements for GDX PP - Number and duration of sessions | 3 sessions 0 to 25 km 60 minutes each 25-50 km 90 minutes each Requires at least 1 session on a different day. | 3 sessions 0 to 25 km 30 minutes each 25-50 km 60 minutes each | 3 sessions 0 to 25 km 15 minutes each 25-50 km 30 minutes each
4.4 | Requirements for GDX NRTK - Number and duration of occupations | (6) 5 minutes Requires at least 3 occupations on a different day. | (3) 5 minutes | (3) 5 minutes
4.5 | Requirements for GDX SRTK - Number and duration of occupations | Not allowed | (5) 5 minutes Requires at least 2 occupations on a different day. | (4) 5 minutes Requires at least 1 occupation on a different day.

## Slide 34: Network Design and Schedule Considerations
Which marks to include in an observation session?
Standard/Specification
  Session length
  Number of occupations
  Repeat occupation criteria
  Baseline length
  Ties to existing passive marks
Resources available
  Equipment
  Observers
Field constraints
  Travel between stations
  Site access
  Site safety

## Slide 35: What Resources are Available?

## Slide 36: Resources
How many field observers are available?
  Are there a different number of observers available on different days?
  Are there certain marks the require specific observers?
    Hike required
    4WD vehicle required
How many sets of equipment are available?
  Certain antenna, tripod, extension, cable length needed because of how/where the mark is set?

## Slide 37: Network Design and Schedule Considerations
Which marks to include in an observation session?
Standard/Specification
  Session length
  Number of occupations
  Repeat occupation criteria
  Baseline length
  Ties to existing passive marks
Resources available
  Equipment
  Observers
Field constraints
  Travel between stations
  Site access
  Site safety

## Slide 38: Field Constraints - Travel
How much time is needed for all observers to get to next station/session?
  Miles/speed limits
  Traffic/City driving
  Off-road travel or hike required

## Slide 39: Field Constraints – Site Access
Hours of access
  Restricted to certain days/hours
  Gated
  Security
  High water/tide

## Slide 40: Field Constraints – Site Safety
Can the equipment be left unattended during long observations?
  Can the equipment be secured (lock, cable, etc…)

## Slide 41: Develop the Schedule
Draw sessions based on available resources
Assign Day, Start time, and duration to the first session
If conducting more than one session per day
  Determine longest travel time between session A and session B stations and use that to determine what time the next session will begin.
Write stations for each session onto schedule grid for the first day
Repeat process for next day. Stagger start time by 3-hours if it is a repeat observation
Session | Start UTC | End UTC | dd/mm/yyyy Julian Day ddd |  | 
 |  |  | John | Bill | Dan
A | 1200 | 1500 | 0001 | 0003 | 0005
B | 1530 | 1830 | 0002 | 0005 | 0004
0001
0002
0003
0005
0004

## Slide 42: Live Demo