## Slide 1
NSRS Modernization –
Big Steps Forward and What Comes Next
Dru Smith
NSRS Modernization Manager
NOAA’s National Geodetic Survey

## Slide 2: Outline
Background
Recent decisions
Recent big steps: The first products are released!
What comes next

## Slide 3: Background

## Slide 4: Background
NSRS Modernization began with a dream in 2007:
What if we could fix all of the problems of NAD 83 and NAVD 88?
Like…
Correcting the 2+ meter discrepancy between NAD 83 and GPS?
Earth’s surface
GPS “Z” axis
GPS “X” axis
Center of Earth, about which GPS satellites orbit
NAD 83
“Z” axis
NAD 83
“X” axis
2+ meter discrepancy

## Slide 5: Background
NSRS Modernization began with a dream in 2007:
What if we could fix all of the problems of NAD 83 and NAVD 88?
Like…
What if we could collect enough gravity to build a geoid good enough to define a cm-accurate vertical datum?
GRAV-D

## Slide 6: Background
And so NSRS Modernization was born!
Accuracy, modern tools, improvements focusing on both science and customer service
NGS 10 year plan

## Slide 7: Background
NSRS Modernization morphed, grew, clarified
  Deadlines changed:
    2018 became 2022 which became 2025
    Which has recently become 2025-2026 (FRN Doc. 2024-23347; Oct 9, 2024)
  Definitions changed:
    2008-2018 ten year plan
    2013-2023 ten year plan
    Blueprint documents (v1; 2017), then Blueprint documents (v2; 2021)
    Adjusted to currently available resources

## Slide 8: Background (Geometric example)
MYCS3 / ITRF2020
EPP2022:
N/P/C/MATRF2022 defined
Geometric REC project puts N/P/C/MATRF2022 epoch 2020.00 coordinates on over 100,000 geodetic control points
IFDM2022
SPROCCET
LASER
SPCS2022
NADCON / NCAT updated
M-PAGES
OPUS-S
and
OPUS-Projects
NSRS DB
and
Data Delivery System
Formal
approval
process
Notes: So where does that bring us today? The dominoes on the slide represent a list of milestones or deliverables (in our *geometric* track. There is a similar one for our *geopotential* track, but the two charts would meet at the “Formal approval process” line) – many internal to NGS. The dominoes are beginning to “fall into place” as we move toward attaining a formal recommendation to approve of the “whole package” of the modernized products and services.
NGS wants all NSRS users to eventually use the modernized NSRS, but the bulk of today’s presentation will focus on some recent decisions and updates related to these milestones.

## Slide 9: Recent decisions

## Slide 10: Recent decisions
External Input | Internal Changes

## Slide 11: Recent decisions
External Input | Internal Changes
2025 Industry workshop participants told us “finalizing" products early would accelerate preparation and adoption | 

## Slide 12: Recent decisions
External Input | Internal Changes
2025 Industry workshop participants told us “finalizing" products early would accelerate preparation and adoption | A phased release/approval approach. First products released: June 2025

## Slide 13: Recent decisions
External Input | Internal Changes
2025 Industry workshop participants told us “finalizing" products early would accelerate preparation and adoption | A phased release/approval approach. First products released: June 2025
Staffing changes | 

## Slide 14: Recent decisions
External Input | Internal Changes
2025 Industry workshop participants told us “finalizing" products early would accelerate preparation and adoption | A phased release/approval approach. First products released: June 2025
Staffing changes | Removed plans to “update” OPUS-Projects, in favor of an accelerated build of an entirely new suite, called OPUS 6. Extend the deadline into 2026
Notes: The change to OPUS plans was sent out in a NEWS bulletin earlier this month. While we strive to minimize changes, when they occur we'll create news bulletins and update our web pages accordingly. Please subscribe to NGS NEWS if you haven't already.

## Slide 15: The new approach
Approve the whole package
NCN on ITRF2020
N/P/C/MATRF2022 defined
NAPGD2022 defined
SPCS2022 defined
SPCS2022 available through a limited beta version of NCAT
“The first subset”
Everything Else
Approve the first subset of products
Notes: The “second subset” of products in the initial set of products and services of the modernized NSRS will be “everything else”, though each product or service in that subset will be released on its own date, as opposed to how five products/services were released en masse in subset #1. We do not expect the release of a third subset.

## Slide 16: Recent big steps: The first products are released!

## Slide 17: beta.ngs.noaa.gov
Note: A very different look/feel from previous NGS web designs
Using U.S. Web Design Standards

## Slide 18: MYCS3: The entry point to ITRF2020
Multi-Year CORS Solution #3
  Re-processing all NOAA CORS Network (NCN) data to estimate CORS Coordinate Functions (CCFs) in ITRF2020
Not on Beta, but is behind everything
ITRF2020 is the foundation for every part of the modernized NSRS
CCFs are now non-linear
  Periodic + Exponential/Logarithmic post-seismic relaxation
Notes: This is a pretty technical slide. It is important to be sure, but may be of interest to only a smaller portion of the audience.

## Slide 19: Defined N/P/C/MATRF2022

## Slide 20: Defined N/P/C/MATRF2022
XYZ coordinates in N/P/C/MATRF2022 are defined through three simple plate rotation parameters relative to ITRF2020
These rotation parameters are in a model called the Euler Pole Parameters of 2022 (EPP2022)
  Tends to stabilize latitude and longitude, over time, in the stable parts of each plate

## Slide 21: CORS Velocities – ITRF2020

## Slide 22: CORS Velocities – NATRF2022

## Slide 23: NAPGD2022 defined
Notes: Officially GEOID2022 defines the relationship between h(ITRF2020) and H(NAPGD2022).

## Slide 24: NAPGD2022 defined
The big star: GEOID2022
  Defines the official relationship between ellipsoid heights in ITRF2020 and orthometric heights in NAPGD2022
The other excellent components:
  DEFLEC2022
  GM2022
  Surface gravity estimator
  Dynamic height estimator
Notes: Officially GEOID2022 defines the relationship between h(ITRF2020) and H(NAPGD2022).

## Slide 25: SPCS2022 defined and NCAT updated

## Slide 26: SPCS2022
A significant change from SPCS27 and SPCS83
Very customer-driven
Low-distortion projections

## Slide 27: NCAT (beta)
Maintains existing functions:
  Converting: (XYZ, lat/lon/ht, SPCS, etc.)
  Transforming: (NAD 27, NAD 83, etc.)
Adds:
  SPCS2022, but
    Does not yet support N/P/C/MATRF2022
    Thus input latitude and longitude in (say) NAD 83(2011) epoch 2010.00 will yield SPCS2022 answers that will differ from true SPCS2022 coordinates, since SPCS2022 is built to support input from N/P/C/MATRF2022
Does not yet add:
  Geometric to geopotential conversions
  Global 14-parameter Helmert transformations between terrestrial reference frames

## Slide 28: Next steps for the first subset of products
NGS is proactively engaging federal partners
  Education about NSRS Modernization
  Seeking top-down support
  Send comments or questions to NGS.Feedback@noaa.gov

## Slide 29: What comes next

## Slide 30: Prioritizing the order of releasing products
NGS promised a modernized NSRS with certain features and functionality. These promises were put out in our “Blueprint Documents”
Most of those promises stand, though some have required minor changes
In 2022 we fully realized that we would only fulfill a limited number of our promises by our self-imposed deadline of 2025
  This required prioritizing what comes before 2025 and what comes after

## Slide 31: Preliminary releases (Beta) for testing and evaluation
The modernized NSRS will be limited, at first
  “The initial set of products and services of the modernized NSRS”
Good data now, then better tools
After approval of the initial set, we will continue to move toward improving and expanding the products of the modernized NSRS
  But after the initial set becomes official, the term “modernized NSRS” will simply become “NSRS”

## Slide 32: What are the remaining preliminary releases for testing/evaluation?
Promise | Will this be part of the preliminary testing and initial roll-out? | What does this mean to you?
Reference epoch coordinates (geometric) | Yes (~100k points) | N/P/C/MATRF2022 epoch 2020.0 coordinates and NAPGD2022 epoch 2020.00 orthometric heights on 100k existing geodetic control marks
Reference epoch coordinates (orthometric) | Yes (~1M points) | NAPGD2022 epoch 2020.00 orthometric heights on an additional 900k existing geodetic control marks
NADCON expansion (in NCAT) | Yes | Ability to transform from NAD 83 and NAVD 88 (et al) to the new reference frames and geopotential datum
VERTCON expansion (in NCAT) | Yes | 
OPUS-S | Yes | OPUS-Static functionality
Data Delivery System (Limited) | Yes | Searchable/downloadable “Geodetic Mark Pages” and “Geodetic Station Pages” to replace current datasheets and CORS station pages
OPUS-Projects for GPS | No | No OPUS-Projects for GPS functionality
OPUS-Projects for leveling, and others | No | No OPUS-Projects for leveling, and other functionalities

## Slide 33: Data Delivery System (Limited)
Users will be able to query the NSRS Database (our new database!) for information about geodetic marks and geodetic stations
  Replacing “Datasheets” and “CORS pages”
The DDS will continue to expand for years

## Slide 34: OPUS-Projects
NGS has decided to stop efforts to modify the existing OPUS-Projects to work in the modernized NSRS
Rather, we have engaged on a fresh build
  An OPUS suite, called “OPUS 6”
  From reconnaissance to network adjustment
  GNSS, leveling, other
  Timeline: Start now
    GNSS first
    Minimize the gap where users have no “OPUS-Projects” in the modernized NSRS
OPUS-6 will not be released as part of the initial set of products and services in the modernized NSRS

## Slide 35: Preliminary vs Final vs Official

## Slide 36: Definitions
Preliminary = This is when the component is first introduced to the public by being released on the Beta website.
  While on the Beta website, this component will undergo testing and evaluation.
Final = After testing and evaluation, NGS will stop making changes to a preliminary component.
  This means that the component is not expected to change before being made official.
Official = A final component becomes official when NGS has moved it from the Beta website and fully integrated it into existing components of the modernized NSRS on the production website/production database

## Slide 37: The official NSRS
The current NSRS (NAD 83, NAVD 88, etc.) remains the official NSRS of the United States.
  It resides at the main NGS web site: geodesy.noaa.gov
The initial set of products and services of the modernized NSRS will be released in phases
  It will reside at the Beta web site: beta.ngs.noaa.gov

## Slide 38: The official NSRS
The current NSRS (NAD 83, NAVD 88, etc.) will remain the official NSRS of the United States until two things happen:
  The initial set of products and services of the modernized NSRS is approved
  Every component of that initial set has been successfully moved from the Beta web site to the main NGS web site, and fully integrated into production
Afterwards, the current NSRS will become superseded
  NGS is considering a short overlap period between the two before ultimately shutting down all tools which actively work in the current NSRS

## Slide 39: The official NSRS
Some modernized products and services may be finalized before approval of the entire initial rollout
  Such final products remain unofficial!
For instance, SPCS2022 might be finalized in late 2025
  Meaning no further changes to it will happen.
  But that does not mean it is part of the official NSRS yet.
    That only happens after the entire initial set has been approved and all beta products moved to the main NGS web page
Once the initial set of products and services of the modernized NSRS is “official”, the modernized NSRS becomes “the NSRS”

## Slide 40: Summary

## Slide 41: Summary
NSRS Modernization is still happening!
We’ve already released some products!
  Awaiting feedback and testing
  Will be finalized later this year (but still not “official”!!)
The “switch” to making the modernized NSRS “official” is planned for 2026
But work will continue to add functionality and tools to the (you don’t need to call it “modernized” anymore) NSRS for many years after 2026

## Slide 42: What can you do to get prepared?
Review NGS webpages about assessing your datasets, workflows and requirements
NGS Engagement Team is proactively working with targeted groups that span a variety of workflows
  Today’s timelines “ended” with the modernized NSRS becoming “official”
  However, we recognize that will just mark the beginning for our partners and users
  NGS is committed to working with our users through the transition
Subscribe to NGS News and NGS Webinars where we’ll announce future information

## Slide 43: Thank you!

## Slide 44: Questions?