## Slide 1
NSRS Modernization
Jeff Jalbrzikowski, P.S., GISP
Appalachian Regional Geodetic Advisor
jeff.jalbrzikowski@noaa.gov
240-988-5486
PLSO Fall Seminar
October 2019

## Slide 2: My Background
Licensed Surveyor in OH, PA, and WV
Certified GIS Professional
University of Akron graduate
Came to NGS from USACE (Pittsburgh, PA)
  primary experience is engineering surveys, including structural deformation, hydrographic/bathymetric, terrestrial LiDAR, GNSS control, local/legacy datum resolution
  previously survey intern, Cadastral Surveyor, GIS Technician, warehouse picker/packer, busboy…

## Slide 3
Have you already heard that NAD83 and NAVD88 are scheduled to be replaced?
Who’s nervous?
Who’s ready?
Who’s already working in ITRF?

## Slide 4: Organizational Structure
Federal Government – Executive Branch
  -Department of Commerce (DoC)
  (~47,000 employees)
  -National Oceanic and Atmospheric Administration (NOAA)
  -National Ocean Service (NOS)
  -National Geodetic Survey (NGS)
  (~175 employees)

## Slide 5: NGS Mission
To define, maintain and provide access to the National Spatial Reference System (NSRS) to meet our Nation’s economic, social, and environmental needs.

## Slide 6: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach/COMET

## Slide 7: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach/COMET

## Slide 8: Continuously Operating Reference Station (CORS)
2000+ sites
~225 organizations

## Slide 9: NOAA CORS Network (NCN)
2000+ sites
~225 organizations

## Slide 10: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach/COMET

## Slide 11: National Height Modernization Program
…the establishment of accurate, reliable heights using GNSS technology in conjunction with traditional leveling, gravity, and modern remote sensing information…
-propagation and long-term monitoring (for subsidence) of control thru static GPS campaigns, GPS on BMs, digital leveling
-combined with relative gravity data, LiDAR, etc

## Slide 12: National Height Modernization Program
Participating and Interested States
Current Funded Partners
States engaged in HM without federal funding assistance
Spatial Reference Centers
Regional Leaders
Other funded partners

## Slide 13: National Height Modernization Program
supports various non-NGS Federal Programs
  FEMA: FIRMs, ECs, etc.
  USACE: Levee/Dam Safety Programs, etc.
and countless non-Federal programs
still an active program but there have not been any grants in a few years

## Slide 14: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach/COMET

## Slide 15: Gravity for the Redefinition of the American Vertical Datum
Two major campaigns within GRAV-D
High-resolution snapshot of gravity
  primarily airborne observations, all relative gravity, estimated cost of ~$39 million
Low-resolution “movie” of gravity changes
  primarily terrestrial, episodic observations of absolute gravity sites

## Slide 16: Gravity for the Redefinition of the American Vertical Datum
As of AUG2019:
78% complete
10 km data lines
70 km cross lines
20,000 ft altitude
230 kt flight speed
Green = Complete
Blue = In Processing
Yellow = Underway
White = Planned

## Slide 17: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach/COMET

## Slide 18: Aeronautical Survey Program
Interagency Program with the FAA
  Primary Airport Control Station (PACS) and Secondary Airport Control Stations (SACS)
  Airports GIS (AGIS)
  Airport Obstruction Charts (AOC)
Primary function of NGS is to serve as QA and SME for airport surveys (of all types) that are contracted by airports

## Slide 19: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach/COMET

## Slide 20: GPS Orbit Data aka Ephemerides
NGS orbit analysis and computation is performed together with, and as a component of, the International GNSS Service (IGS)
  IGS coordinates the collection of satellite tracking data
Designated with this responsibility by the Civil GPS Service Interface Committee (CGSIC)
If you’re using OPUS, it’s all behind-the-curtain

## Slide 21
Link to NGS GPS Calendar

## Slide 22: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach/COMET

## Slide 23: National Shoreline
The official national shoreline data, in support of NOAA nautical charting mission
Available for download as Shapefile in Mean High Water and Mean Lower Low Water datum
Organized by “Project Area”
hyperlink to the National Shoreline homepage

## Slide 24: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach/COMET

## Slide 25: https://www.ngs.noaa.gov/ADVISORS/

## Slide 26: Regional Geodetic Advisor Program
www.ngs.noaa.gov/ADVISORS/
query any major search engine: “ngs advisors”

## Slide 27: State Geodetic Coordinators
not an NGS employee
a liaison between the State’s geospatial community and the NGS

## Slide 28: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach/COMET

## Slide 29: Emergency Response Imagery
Mission of the Remote Sensing Division
Pre-Storm and Post-Storm photos are taken along the coastal CONUS
Supports Homeland Security (DHS) and Emergency Response (FEMA, etc.) events

## Slide 30: Emergency Response Imagery

## Slide 31: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach/COMET

## Slide 32: Phase Center Offset - conceptual
Orange dot = mean point of signal reception
Blue dot = Antenna Reference Point (ARP)
Red line = Phase Center Offset (PCO)

## Slide 33: Phase Center Offset - conceptual
The PCO is one reason it is important to select the correct antenna for OPUS upload!

## Slide 34: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach/COMET

## Slide 35: NGS Coordinate Conversion and Transformation Tool

## Slide 36: Beta NCAT – includes VERTCON 3.0 for NGVD29 to NAVD88 transformation

## Slide 37: Coordinate Transformation Tool
X, Y, Z
USN G
UTM
SP C
X, Y, Z
USN G
UTM
SP C
X, Y,
Z
USN
G
UTM
SP
C
, , h
(NCAT / NADCON 5.0)
USSD
NAD 27
NAD 83 (1986)
Relating coordinates: then & now
NAD 83 (2011)
NAD 83 (NSRS2007)
NAD 83 (FBN)
, , h
NAD 83 (HARN)
, , h
2022

## Slide 38: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach/COMET

## Slide 39: Continually Updated Shoreline Product
Just what it says, a dynamic product
Available for download as Shapefiles
Developed by image interpretation and/or vertical modeling using water level stations (tide or lake gages)
Referenced to a computed Mean High Water
hyperlink to the CUSP homepage

## Slide 40: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach/COMET

## Slide 41: Calibration Base Lines
Three types of CBL defined by NGS
  Primary CBL (PCBL): in Woodford, VA at NGS TTC; it is open for use to organizations like the PLSO
  Federal CBL (FCBL): established with EDM checked at the NGS PCBL and IAW NOAA TM NGS-8
      13 across Ohio, 1 reported unstable condition in Defiance
  Cooperative CBL (CCBL): established with EDM checked on an FCBL and IAW that same NGS-8 manual

## Slide 42: Calibration Base Lines
NGS commitment to the CBL Program:
  A minimum of one FCBL per State
  Establishment procedures document
  Public access to the CBL database
  Software to process your observations
  Verification and re-measurement data review
  Technical support (Advisors or other personnel)

## Slide 43: Beta CBL Map Viewer

## Slide 44: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach/COMET

## Slide 45: Cooperative program for Operational Meteorology, Education, and Training
Meteorology… why?
The origin of the program was the National Weather Service, also a NOAA sub-agency.
It expanded to various NOAA missions, cinluding NGS

## Slide 46: Outreach and COMET

## Slide 47: Note on NGS Outreach
All the Regional Advisors are considered a part of the overall outreach mission.
Get in touch if you are coordinating a meeting, info session, or some sort of educational event.
Availability based on first-come first-serve and travel funding.

## Slide 48: NGS Mission
To define, maintain and provide access to the National Spatial Reference System (NSRS) to meet our Nation’s economic, social, and environmental needs.

## Slide 49: National Spatial Reference System (NSRS)
A consistent coordinate system that defines
latitude
longitude
height
scale
orientation
gravity
throughout the United States.
…and their time variants

## Slide 50: National Spatial Reference System (NSRS)
These items ARE part of the NSRS
Horizontal Datums (aka Geometric Reference Frames) | Vertical Datums | Great Lakes Datums | Geoid Models | Transformations and Conversions
NAD83 | NAVD88 | IGLD85 | GEOID12A & B | NADCON
NAD27 | NGVD29 | IGLD55 | GEOID09 | VERTCON
USSD | VIVD09 |  | GEOID06 | 
 | GUVD04 |  | GEOID03 | SPCS83
 | NMVD03 |  | GEOID99 | SPCS27
 | ASVD02 |  | GEOID96 | 
 | PRVD02 |  | ALASKA94 | 
 |  |  | GEOID93 | 
 |  |  | GEOID90 | 

## Slide 51: National Spatial Reference System (NSRS)
Horizontal Datums (aka Geometric Reference Frames) | Vertical Datums | Geoid Models | Transformations and Conversions
WGS84 | IHRS (by IAG) | OSU91A | CORPSCON
WGS72 |  | EGM96 | Appendix B.6 of DMA TR 8350.2 (WGS 84)
ITRF (Intl. Terrestrial Reference Frame by IERS) |  | EGM2008 | Oregon Coordinate Reference System (ORCS)
IGS (Intl. GNSS Service reference frame) |  |  | The Kansas Regional Coordinate System
These items are NOT part of the NSRS
Hyperlink to ITRF station map

## Slide 52: NSRS … do I have to use it?
Office of Management and Budget: Circular A-16
  requires all Federal civilian agencies to utilize geodetic control for their geospatial activities
  dictates DoC in responsible charge of that control
  NGS has defined that control as the NSRS
  FGCS has issued requirements, via FRNs, to reference data to the most recent components of the NSRS
            1989 FRN designated NAD 83
            1993 FRN designated NAVD 88
Hyperlink to NAVD88 FRN
Hyperlink to NAD83 FRN

## Slide 53: NSRS … do I have to use it?
No, not really! But it is a good idea.
States may mandate use
State, Local, Regional entities, or the Private Sector have no requirement to maintain their data in reference to the NSRS
But if you want to get involved in survey contracting with the Federal Government it’s a necessity

## Slide 54: Not just new datums…
  NSRS Modernization
Replace NAD83
Replace NAVD88
Re-invent Bluebooking
Improve Geodetic Toolkit
Better Surveying Methods
Blueprint for 2022, Part 3
Blueprint for 2022, Part 1
Blueprint for 2022, Part 2

## Slide 55: Evolution of the NSRS
NAD27
NAD83 (1986)
NAD83 (2011)

## Slide 56: Modernized NSRS is our “smartphone”
You resisted it for a while…
It was a little cumbersome to get used to…
But you were soon hooked!

## Slide 57
Two Major Components of Modernized NSRS
NATRF2022 – geometric (LLh)
NAPGD2022 – geopotential (H)

## Slide 58
North American Terrestrial Reference Frame of 2022
NATRF2022
(pronounced: nat-ref)

## Slide 59: Reference Frame ≈ Datum
Reference Frame is a more scientifically appropriate way of saying “datum”
could be debated that “datum” was misused
you will continue to see NGS use the phrase “New Datums” for 2022

## Slide 60: Reference Frame Defined
A point of view or a ‘frame of reference’.
If your reference frame is North America, you are standing somewhere within North America, seeing how other places move from your point of view.

## Slide 61: Why replace NAD83?
Main driver: Global Navigation Satellite System (GNSS)
ACCESS
  GNSS equipment is fast, inexpensive, reliable
  Reduces reliance on physical control marks
ACCURACY
  Insensitive to distance-dependent errors
  Immune to monument instability; active control via CORS
CONSISTENCY
Eliminates systematic errors in current datums
Aligned with global reference frames
Integrated system for both position and height

## Slide 62: A very brief history of U.S. horizontal & geometric datums
time
+
shift
<10 m
tens of meters
few 0.1m
few 0.01m
few 0.01m
triangulation
GNSS
+
+
+
+
+
<2m
NATRF2022

## Slide 63: Replacing NAD83
develop four "plate-fixed" reference frames
remove non-geocentricity of NAD83
align to ITRF2014 at epoch 2020.00
remove most of tectonic plate rotation from ITRF2014 via Euler Pole Parameters
(pronounced: “oiler”)
Shift and Drift…

## Slide 64: Replacing NAD83
develop four "plate-fixed" reference frames
remove non-geocentricity of NAD83
align to ITRF2014 at epoch 2020.00
remove most of tectonic plate rotation from ITRF2014 via Euler Pole Parameters
(pronounced: “oiler”)
Shift and Drift…

## Slide 65: Four “Plate-Fixed” Reference Frames
North American Terrestrial Reference Frame of 2022
(NATRF2022)
Pacific Terrestrial Reference Frame of 2022
(PATRF2022)
Caribbean Terrestrial Reference Frame of 2022
(CATRF2022)
Mariana Terrestrial Reference Frame of 2022
(MATRF2022)
+

## Slide 67: Four “Plate-Fixed” Reference Frames
North American Terrestrial Reference Frame of 2022
(NATRF2022)
Pacific Terrestrial Reference Frame of 2022
(PATRF2022)
Caribbean Terrestrial Reference Frame of 2022
(CATRF2022)
Mariana Terrestrial Reference Frame of 2022
(MATRF2022)

## Slide 68: Replacing NAD83
develop four "plate-fixed" reference frames
remove non-geocentricity of NAD83
align to ITRF2014 at epoch 2020.00
remove most of tectonic plate rotation from ITRF2014 via Euler Pole Parameters
(pronounced: “oiler”)
Shift and Drift…

## Slide 69: Non-geocentricity of NAD83
~2.2 meters
NAD83
origin
ITRF2014
origin
Earth’s
Surface
h83
h14
GRS80
ellipsoid

## Slide 70: Geometric change due to ellipsoid non-geocentricity
Horizontal (Lat, Lon)
Ellipsoidal (h)
Shift…

## Slide 71: Replacing NAD83
develop four "plate-fixed" reference frames
remove non-geocentricity of NAD83
align to ITRF2014 at epoch 2020.00
remove most of tectonic plate rotation from ITRF2014 via Euler Pole Parameters
(pronounced: “oiler”)
Shift and Drift…

## Slide 72
International Terrestrial Reference Frame
(ITRF)
International Earth Rotation and Reference Systems Service (IERS)
International Union of Geodesy and Geophysics (IUGG)

## Slide 73: International Terrestrial Reference Frame
The stable coordinate system that allows us to measure change over space, time and evolving technologies.
An accurate, stable set of station positions and velocities.
Network measurements interconnected by co-location of different space geodetic techniques.
“Approximately represents the motions of the tectonic plates with respect to the Earth's deep interior”… huh?

## Slide 74
Watch the grid!
ITRF concept
Drift…

## Slide 75: Replacing NAD83
develop four "plate-fixed" reference frames
remove non-geocentricity of NAD83
align to ITRF2014 at epoch 2020.00
remove most of tectonic plate rotation from ITRF2014 via Euler Pole Parameters
(pronounced: “oiler”)
Shift and Drift…

## Slide 76: The wrong question, circa 2022:
“What’s the position of that point?”
The right question, circa 2022:
“What’s the position of that point, on some specific date?”
Drift…

## Slide 77: Two types of drift
Tectonic Plate Rotation
    horizontal
Everything Else
    residual motions left after rotation
    regional linear motions
    localized subsidence or uplift
simple to model
complex

## Slide 78
Tectonic Plate Rotation
    horizontal
simple to model

## Slide 79
Euler Pole Parameters
of 2022
EPP2022

## Slide 80: Plate Rotation visualized
Drift…

## Slide 81: Euler Poles and “Plate-Fixed”
  In the ITRF, many tectonic plates have a dominant motion: rotation
  Euler Pole - point about which a plate rotates (yellow star)
NATRF2022 Euler Pole

## Slide 82: Euler Poles and “Plate-Fixed”
ITRF
Frame = constant
NA Plate = rotating
NATRF
Frame = rotating
NA Plate = constant

## Slide 83: Euler Poles and “Plate-Fixed”
ITRF
Frame = constant
NA Plate = rotating
NATRF
Frame = rotating
(relative to ITRF)
NA Plate = constant
(relative to NATRF2022)

## Slide 84
ITRF – constant frame, rotating plate

## Slide 85: “Plate-Fixed”
NATRF – rotating frame, constant with plate

## Slide 86
ITRF or NATRF – your choice, just use EPP

## Slide 87: EPP – Euler Pole Parameters
Latitude
Longitude
Rotation Speed
yellow star off west coast of S. America

## Slide 88: CORS Velocities in ITRF2014
Drift…

## Slide 89
CORS Velocities in NATRF2022
Think of this map as ITRF2014 + EPP2022
Still SomeDrift…

## Slide 90
The North American Terrestrial Reference Frame of 2022
(NATRF2022)
The Caribbean Terrestrial Reference Frame of 2022
(CATRF2022)
The Pacific Terrestrial Reference Frame of 2022
(PATRF2022)
The Mariana Terrestrial Reference Frame of 2022
(MATRF2022)
Rotation of the
North American Plate
Rotation of the
Caribbean Plate
Rotation of the
Pacific Plate
Rotation of the
Mariana Plate
ITRF2014
EPP2022
ITRF2014 + EPP2022 = --TRF2022

## Slide 91
The North American Terrestrial Reference Frame of 2022
(NATRF2022)
The Caribbean Terrestrial Reference Frame of 2022
(CATRF2022)
The Pacific Terrestrial Reference Frame of 2022
(PATRF2022)
The Mariana Terrestrial Reference Frame of 2022
(MATRF2022)
Rotation of the
North American Plate
ITRF2014
EPP2022
ITRF2014 + EPP2022 = --TRF2022

## Slide 92: Two types of drift
Tectonic Plate Rotation
    horizontal
Everything Else
    residual motions left after rotation
    regional linear motions
    localized subsidence or uplift
simple to model
complex

## Slide 93
Everything Else
    residual motions left after rotation
    regional linear motions
    localized subsidence or uplift
complex
Still SomeDrift…

## Slide 94
Intra-Frame Velocity Model of 2022
IFVM2022

## Slide 95
Longitude (Easting) History of DI4044
BLUE IS ITRF COORDINATE
RED IS NATRF2022
COORDINATE
Trend: -14.3 mm / year
Trend: -1.7 mm / year
2004 2006 2008 2010 2012 2014 2016 2018
Still Some Drift…
Concept of goal of IFVM

## Slide 96: Still Some Drift…
  Everything in the world moves
  Coordinates will be associated with the actual date when the data was collected!
  Velocities at all marks can be estimated using this Intra-Frame Velocity Model
  IFVM goal being to move collected data thru time to Reference Epochs for coordinate comparisons/analysis

## Slide 97
A model of all residual velocities, after removal of tectonic rotation via EPP:
  Horizontal residual motion
  Total vertical motion (ellipsoid heights)
  Replaces / Improves upon HTDP
Given t1 and t2, compute Df, Dl, Dh at any point, accounting for all motions (drifts, earthquakes, GIA, etc.)
Likely be built upon CORS data, geodynamic models and InSAR
Intra-Frame Velocity Model

## Slide 98
EPP2022 – Euler Pole Parameters – Simple Rotation
  Three parameters: lat, lon, rotation speed
  Horizontal only: just latitude and longitude
  Changes the frame: ITRF2014 + EPP2022 = NATRF2022
  Does not change the epoch
IFVM2022 – Intra-Frame Velocity Model - Complex
  Complex set of parameters
  Residual horizontal motion: all the motion leftover after Euler Pole rotation
  All vertical motion: localized subsidence or uplift
  Changes the epoch
  Does not change the frame: “intra” = on the inside; within

## Slide 99: EPP2022 IFVM2022
They work together to account for the Drift…
Two new tools that will make time dependent geodetic control practical

## Slide 100: Example of application of EPP and IFVM
It’s 2039 and you are working in San Diego using NATRF2022
And you need to compare your work to another survey from 2028
Important: This slide only covers geometric coordinates.
NATRF2022
ep. 2028.048
PATRF2022
ep. 2028.048
ITRF2014
ep. 2028.048
NATRF2022
ep. 2039.704
ITRF2014
ep. 2039.704
PATRF2022
ep. 2039.704
EPP2022
(PA)
EPP2022
(NA)
EPP2022
(NA)
EPP2022
(PA)
IFVM2022
(PA)
IFVM2022
(NA)
…the catch is, that survey was done in PATRF2022

## Slide 101: Alright Jeff... enough jibba-jabba, what’s the impact?

## Slide 103
What’s that going to look like?
PHOTO = NAD83
RED = NAD83 shoreline data
GREEN = shoreline transformed to NATRF2022

## Slide 104: If you’re only working in this region…
North American Terrestrial Reference Frame of 2022
(NATRF2022)

## Slide 105
North American-Pacific Geopotential Datum of 2022
NAPGD2022
(pronounced: nap-jee-dee)

## Slide 106
A very brief history of (the most prevalent) U.S. vertical datums

## Slide 107
NGVD29
The National Geodetic Vertical Datum of 1929 is referenced to 26 tide gauges in the US and Canada

## Slide 108
4 cm
125 cm
70 cm
85 cm
102 cm
NGVD 29
Referenced to 26 Tide Gages
NAVD 88
Referenced to 1 Tide Gauge
(Father’s Point)
NAVD88 minus LMSL(1960-1978)
-23 cm
-23 cm
-11 cm
-11 cm

## Slide 109: Why Replace NAVD88?
tilt/bias in zero reference surface
subsidence, uplift, freeze/thaw of BMs
limited access, availability of undisturbed marks
Approximate Error in NAVD88 "zero elevation”

## Slide 110: Known Issues with NAVD88
tilt/bias in zero reference surface
subsidence, uplift, freeze/thaw of BMs
limited access, availability of undisturbed marks
Approximate Error in NAVD88 "zero elevation”

## Slide 111: Passive marks may lie still… but they still may lie! small instability x long time = large inaccuracy

## Slide 112: Replacing NAVD88
primary access via GNSS and geoid (OPUS, etc.)
accurate continental gravimetric geoid (1-2 cm)
aligned with:
  NATRF2022 (or CATRF, PATRF, MATRF)
  global mean sea level (GMSL)
monitor time-varying nature of gravity (NGS Geoid Monitoring Service GeMS)

## Slide 113: Replacing NAVD88
Two types of geoid models
  Gravimetric
  Hybrid

## Slide 114
  Gravimetric geoid is created from “scratch” with various types of gravity data
      USGG2003, USGG2009, USGG2012, xGEOID19
  Hybrid geoid is simply a gravimetric geoid warped to fit some vertical datum… like NAVD88
      GEOID03, GEOID09, GEOID12B, GEOID18
Replacing NAVD88

## Slide 115
      USGG2003, USGG2009, USGG2012, xGEOID19
      GEOID03, GEOID09, GEOID12B, GEOID18
Replacing NAVD88
best fit to NAVD88
best fit to NAVD88
best fit to NAVD88
best fit to NAVD88

## Slide 116: Building a Geopotential Field Model
Airborne Observations
(GRAV-D)
Terrestrial/Surface Measurement and Predicted Gravity from Topography
Short Wavelengths (< 100 km)
+
Long Wavelengths
(> 250 km)
GRACE/GOCE/Satellite Altimetry
Intermediate Wavelengths
(20km to 300 km)

## Slide 117: GRACE - 2 Satellites measuring separation

## Slide 118: GRAV-D – airborne relative gravimeters

## Slide 119: Terrestrial Gravimeter - Relative

## Slide 120: Terrestrial Gravimeter - Relative

## Slide 121: Terrestrial Gravimeter - Absolute

## Slide 122: Terrestrial Gravimeters - Absolute and Relative

## Slide 123: Individual Components of NAPGD2022
global model of the geopotential field
  GM2022
geoid undulation models by region
  GEOID2022 aka “0 elevation”
deflection of the vertical (DoV) models by region
  DEFLEC2022
surface gravity models by region
  GRAV2022
    static – SGRAV2022
    dynamic – DGRAV2022

## Slide 124: Sea Level Change and the Geoid

## Slide 125: Sea Level Change and the Geoid

## Slide 126: Sea Level Change and the Geoid

## Slide 127
Estimated change in orthometric heights from NAVD88 to NAPGD2022
(NAPGD2022 approximated using xGEOID16B)

## Slide 128
(NAPGD2022 approximated using xGEOID16B)
Estimated change in orthometric heights from NAVD88 to NAPGD2022
Vertical change of about -0.6 to -2.0 feet

## Slide 129
North American-Pacific Geopotential Datum of 2022
(NAPGD2022)

## Slide 130: Where did this all start? How is all this possible? And what will users get out of it?
Well, besides learning a whole new set of terminology and methods…

## Slide 131: National Geodetic Survey Ten-Year Strategic Plan
  By 2022, reduce all definitional & access-related errors in geometric reference frame to 1 cm when using 15 min of GNSS data
  aka “Replace NAD83”
  By 2022, reduce all definitional & access-related errors in orthometric heights in geopotential datum to 2 cm when using 15 min of GNSS data
  aka “Replace NAVD88”
https://geodesy.noaa.gov/web/about_ngs/info/tenyearfinal.shtml

## Slide 132: How is all this possible?
CORS
Co-location of space geodetic instruments worldwide
Teamwork with other geodetic organizations
Research and Development
Testing
Science!

## Slide 133: Co-location Site NASA Goddard Space Flight Center, Greenbelt MD, USA
  GNSS, SLR, VLBI, DORIS

## Slide 134: Co-location Site NASA Goddard Space Flight Center, Greenbelt MD, USA
  GNSS, SLR, VLBI, DORIS

## Slide 135: Co-location Site NASA Goddard Space Flight Center, Greenbelt MD, USA
  GNSS, SLR, VLBI, DORIS

## Slide 136: SLR
Satellite Laser Ranging

## Slide 138: Co-location Site NASA Goddard Space Flight Center, Greenbelt MD, USA
  GNSS, SLR, VLBI, DORIS

## Slide 139: VLBI
Very Long Baseline Interferometry

## Slide 140
VLBI

## Slide 141: Co-location Site NASA Goddard Space Flight Center, Greenbelt MD, USA
  GNSS, SLR, VLBI, DORIS

## Slide 142: DORIS
Doppler Orbitography and Radiopositioning Integrated by Satellite

## Slide 143
Doppler Orbitography and Radiopositioning Integrated by Satellite

## Slide 144: Space Geodesy Co-location Diagram
Generic concept of “co-location survey”, typically more complex.

## Slide 145: Altogether now!
All these techniques work together to create a well-defined, robust reference frame that improves positioning for users globally.

## Slide 146: Not just new datums…
  NSRS Modernization
-OPUS enhancements/additions
-new types of coordinates
-new methods for establishing control
-streamlined Bluebooking

## Slide 147
https://www.ngs.noaa.gov/ADVISORS/
-use any major search engine: “NGS advisors”
Jeff Jalbrzikowski, P.S., GISP
Appalachian Regional Geodetic Advisor
jeff.jalbrzikowski@noaa.gov
240-988-5486