## Slide 1: The Future in a Dynamic National Spatial Reference System
NSGIC Midyear Meeting
March 6, 2019
Brian Shaw
brian.shaw@noaa.gov

## Slide 2
Presentation Outline
Who is NGS and what is the NSRS
Modernization of the NSRS
    Our dynamic world
Prepare for 2022

## Slide 3
NOAA and NGS
Our Nation’s First Civilian Science Agency
1807
Thomas Jefferson
Survey of the Coast
1811
Ferdinand Hassler
Superintendent
1836
U.S. Coast
Survey
1878
U.S. Coast and
Geodetic Survey
1970
NOAA is established
Notes: NGS has been around a long time. For more than 200 years, NGS and its predecessor agencies have collaborated with public and private organizations to establish reference stations at precisely determined locations.
We began on a mission established by Thomas Jefferson in 1807 to conduct a “Survey of the Coast” (as the United States Coast Survey).
(Pictured are Thomas Jefferson and Ferdinand Hassler, the first Superintendent of the Coast Survey). We were renamed the U.S. Coast and Geodetic Survey in 1878. NOAA was established in 1970.
Traditionally, precise positioning locations have been identified by setting a survey mark—usually a brass, bronze, or aluminum disk. Locations might also be identified by a deeply driven rod, or a prominent object, such as a water tower or church spire.

## Slide 4
NGS’ Mission
To define, maintain and provide access to the National Spatial Reference System (NSRS) to meet our Nation’s economic, social, and environmental needs.
…………………………………………….........................
The NSRS is a consistent coordinate system that defines latitude, longitude, height, scale, gravity, orientation, and shoreline throughout the United States.
Notes: The National Spatial Reference System is our nations geospatial infrastructure from which all positioning (with the exclusion of military/DOD) is referenced to.
This system provides a consistent framework that allows people to use data in the same reference system to perform analysis and make meaningful comparisons and decisions from that analysis.

## Slide 5
The Importance of Geodesy
1816-1817
1969
Today
Notes: In 1807 Thomas Jefferson created the Survey of the Coast. Ferdinand Hassler was later appointed the first superintendent and completed the first survey of New York Harbor. Commerce from shipping has always been important and for safe shipping you need to know the bathymetry of the harbors. To understand the bathymetry accurately requires you to know where the land is and the bathymetry relative to these points on land which is where geodesy comes in. This is the reason why in 1878 the name was changed to the U.S. Coast and Geodetic Survey and remained in the name until it was combined with other agencies to form the National Oceanic and Atmospheric Administration.

## Slide 6
The Earth is Infinitely Complex
Build Models to Simplify
Notes: Models are used to simplify complex phenomena for humans and computers to understand and perform calculations and analysis.
The geoid is an approximation of sea level and used to calculate elevations (orthometric heights) above this “sea level” surface
Spheroid image https://www.kisspng.com/png-sphere-shape-ball-grid-line-circle-draw-5378189/
Ellipsoid image https://www.kisspng.com/png-figure-of-the-earth-oblate-spheroid-ellipsoid-4129812/
Geoid Image https://www.reddit.com/r/MapPorn/comments/3xf6a0/geoid_height_of_new_global_gravity_field_models/

## Slide 7
Gravity is Fundamental
Aristotle (350BC)
Al-Khazini (1121)
Galileo (1590)
Newton (1687)
Einstein (1913)
Objects fall proportional to mass
Gravitational potential energy
Terminal velocity
Gravity inverse-square law
Theory of general relativity
Notes: Galileo graphic https://commons.wikimedia.org/wiki/File:GalilEXP.jpg
Spacetime curvature graphic https://www.nasa.gov/mission_pages/gpb/gpb_012.html
Aristotle (384–322 BCE)
Objects fall at a speed proportional to their mass.
The Aristotelian explanation of gravity is that all bodies move toward their natural place. For the elements earth and water, that place is the center of the (geocentric) universe;
al-Khazini (11th to 12th centuries)
In 1121, al-Khazini, in The Book of the Balance of Wisdom, proposed that the gravity and gravitational potential energy of a body varies depending on its distance from the centre of the Earth.
Galileo Galilei (1564-1642)
Leaning Tower of Pisa Experiment (1589-92) - Law of Falling Bodies
Objects fall at the same speed, independent of their mass or shape
Isaac Newton (1643-1727)
In 1687, English mathematician Sir Isaac Newton published Principia, which hypothesizes the inverse-square law of universal gravitation.
Albert Einstein (1879-1955)
Between 1911-1915 Einstein developed the theory of general relativity. In general relativity, the effects of gravitation are ascribed to spacetime curvature instead of to a force. To deal with this difficulty, Einstein proposed that spacetime is curved by matter, and that free-falling objects are moving along locally straight paths in curved spacetime. (This type of path is called a geodesic).

## Slide 8
Gravity for the Redefinition of the
American Vertical Datum
GRAV-D
Notes: More information on GRAV-D
https://geodesy.noaa.gov/GRAV-D/
Data Download for GRAV-D blocks
https://geodesy.noaa.gov/GRAV-D/data_products.shtml

## Slide 9
Some things I want you to remember
Know and understand your data
Accuracy Needs (Mapping/Survey)
Metadata
Datum (realization)
Epoch
Original Observations
Data Requirements (contracts)
How collected/processed

## Slide 10
Datums and Reference Frames
A reference surface or framework to reference your data to for consistency
aka P(L,L,H)
= lat.
= long.
= ht.
X,Y,Z vs Lat,Lon,Ht
60”
60”
40”
20”
60”, 2019
52”, 2018
40”, 2017
Notes: What is a datum? https://oceanservice.noaa.gov/facts/datum.html
Datums Overview https://geodesy.noaa.gov/datums/
New Datums https://geodesy.noaa.gov/datums/newdatums/
Horizontal and Geometric Datums https://geodesy.noaa.gov/datums/horizontal/
Vertical Datums https://geodesy.noaa.gov/datums/vertical/
A Datum or reference frame is in essence a reference surface or framework to reference your data to for consistency.
In the first image on the right there is a person who has been measuring their height over time (2017-2019 in this example). For consistency you can imagine that the floor next to the wall they are being measured is this ‘reference surface’ or datum. Lets say the first measurement was taken when the floor was carpet and you installed hard wood floors before the 2018 measurement you would have in essence changed the ‘reference surface’ and it would be inaccurate to compare the 2018 and 2019 values without a proper transformation, or height offset value.
The second image (when animating) shows why you should not try to compare values when using two different reference surfaces.

## Slide 11
Why Modernize the NSRS
Current models built on old technology
  NAD83 not truly Geocentric (~2.2m)
  NAVD88 relies on marks in the ground
  and is not easily maintained
  Today’s technology needs better accuracy
Notes: NSRS Modernization News
https://geodesy.noaa.gov/datums/newdatums/TrackOurProgress.shtml

## Slide 12
Benefits of Modernizing the NSRS
International/National/Local Consistency
Better Accuracy
Easy transformation between ITRF

## Slide 13
Terminology
Datum
Reference Frame
Coordinate System
Orthometric (Elevation)
Time (epoch)
Geometric
Equipotential
Geopotential
Notes: There will be a bit of new terminology to get used to in the modernized NSRS.
Datum and Reference Frame can by assumed as the same thing.
Coordinate Systems in COTS like ArcGIS and QGIS often refer to Datums/Reference Frames as Geographic Coordinate Systems. Projected Coordinate Systems are projections of coordinates referenced to a particular datum but projected for differing purposes. Universal Transverse Mercator (UTM) and the State Plane Coordinate System (SPCS) are examples of projected coordinate systems.
Book on Map Projections - https://pubs.er.usgs.gov/publication/pp1453
Time (epoch) will be very important in the future NSRS since coordinates will be given for a specific time.
All realizations of NAD83 except the original NAD83(1986) are actually 3 dimensional or often called geometric.
Equipotential is a term for a surface of points that have the same potential. If you think of a plastic sheet that was an equipotential surface and you poured a glass of water on it the water would distribute itself equally across the whole sheet. Isobars or contours on a map could be considered an equipotential surface since they represent the same value for the line.
Geopotential is the same thing as equipotential but generally applied to a gravimetric surface.

## Slide 14
Accuracy versus Precision
Accuracy is telling the “Truth”
— future NSRS —
Precision is telling the same story over and over again
— current NSRS —
Notes: Our current datums were made with the best technologies of their time but we understand a lot more about the errors inherent in them. While they are not necessarily accurate – for todays standards at least – they have provided a consistent framework for positioning.
The future NSRS will provide the most accurate and best system for positioning using the best science of today. No system will ever be perfect, but they can always be improved through sound science.

## Slide 15
Know your Accuracy Needs
  Mapping (~3m)
    Can assume WGS84 and NAD83 equal
    NADCON transformations good (~3dm)
  Geodetic/Survey (~3cm)
    Know datum, epoch, and processing
    Process original observations
Notes: Don’t hammer a nail with a sledgehammer if a small hammer will work. Know your accuracy needs or anticipate future needs to determine how accurate your data needs to be. Performing analysis using various data can only be as accurate as the least accurate data you are using.

## Slide 16
What to Expect?
~1 to 1.5 meters North America
~2.5 to 4 meters in Pacific
0 to 1.3 meters CONUS
Notes: New Datums What to expect https://geodesy.noaa.gov/datums/newdatums/WhatToExpect.shtml
NGS is not shifting the land, merely shifting the reference surfaces to which we reference the geospatial data to.

## Slide 17
The Future Reference Frames
Tectonic Plate based:
North America
Caribbean
Pacific
Mariana
[NATRF]
[CATRF]
[PATRF]
[MATRF]
Notes: NSRS Modernization Naming Conventions https://geodesy.noaa.gov/datums/newdatums/naming-convention.shtml

## Slide 18
Plate Tectonics and Velocities
“drift” : Annual changes to ITRF2014 coordinates
Notes: All plates are moving and through the constant collection of GNSS data using CORS we can now model where the land is moving. In the center of tectonic plates there is generally motion that can be measured but where plates converge can be thought of as a crunch zone and the modeling has much more uncertainty due to geophysical phenomena.

## Slide 19
Coordinates over time
Because latitude and longitude will behave significantly
differently in a plate-fixed system than in ITRF,
such graphs may look different.
CORS best estimate of dh/dt: -2.2 mm / year
NATRF2022 best estimate of dh/dt: -4.2 mm / year
NAD 83 best estimate of dh/dt: +2.8 mm / year
Notes: All surveying measurements in the future NSRS will provide coordinates for the time (epoch) it was surveyed.
The second graphic is a hypothetic view of how a station that has been observed multiple times may be plotted to understand where its moving.

## Slide 20
USSD
NAD 27
(1986)
(2011)
(NSRS2007)
(FBN)
(HARN)
NATRF2022
NAD 83
Transformations
NCAT/NADCON5
(No SPCS)
X, Y, Z
f, l, h
UTM
USNG
SPCS
f, l
UTM
USNG
SPCS
2D
3D
CONUS
f, l
f
l
h
- Latitude
- Longitude
- Ellip. Height
Notes: NCAT (implementation of NADCON5) - https://geodesy.noaa.gov/NCAT/
NADCON 5 Technical Report - https://geodesy.noaa.gov/PUBS_LIB/NOAA_TR_NOS_NGS_63.pdf
USSD – United States Standard Datum https://geodesy.noaa.gov/datums/horizontal/us-standard-datum.shtml
NAD 27 – North American Datum of 1927 https://geodesy.noaa.gov/datums/horizontal/north-american-datum-1927.shtml
NAD 83 – North American Datum of 1983 https://geodesy.noaa.gov/datums/horizontal/north-american-datum-1983.shtml
NATRF2022 – North American Terrestrial Reference Frame of 2022 https://geodesy.noaa.gov/datums/newdatums/naming-convention.shtml

## Slide 21
Vertical Motion
Subsidence
  Ground fluid withdrawal, sedimentation
Glacial Isostatic Adjustment (GIA)
  Crustal rebound from glaciers (uplift)
Geophysical Phenomena
  Earthquakes, calderas, Earth tides

## Slide 22
8.5 meters
50 years
San Joaquin Subsiding
20-24” in 16 months
May 2015
to
Sept 2016
Hudson Bay Uplifting
8 -13 mm/year
Vertical Motion
Notes: San Joaquin Subsidence article
http://www.digitaljournal.com/tech-and-science/technology/sinking-san-joaquin-valley-of-california-seen-from-space/article/487393
Hudson Bay Uplift article
https://www.researchgate.net/figure/Contour-map-of-observed-CBN-vertical-rates-Preliminary-results-from-the-combination-of_fig3_286867540
GIA

## Slide 23
NAPGD2022 Geopotential Datum
Not a vertical datum, it is more than just heights.
Guam/CNMI
American Samoa
Models included:
        Geopotential
        Deflection
        Gravity
        Geoid
¼ Earth’s Surface
Notes: As noted in the Blueprint 2 document
https://geodesy.noaa.gov/library/pdfs/NOAA_TR_NOS_NGS_0064.pdf
NAPGD2022 will include all of the following
Geopotential Model of 2022 (GM2022) will include:
Static Geopotential model of 2022 (SGM2022)
Dynamic Geopotential model of 2022 (DGM2022)
GEOID2022 will include:
Static Geoid model of 2022 (SGEOID2022)
Dynamic Geoid model of 2022 (DGEOID2022)
DEFLEC2022 will include:
Static Deflection of the Vertical model of 2022 (SDEFLEC2022)
Dynamic Deflection of the Vertical model of 2022 (DDEFLEC2022)
GRAV2022
Static Gravity model of 2022 (SGRAV2022)

## Slide 24
GPS on Bench Marks
GEOID18
2022 Transformations
2018 Prioritized List
~2500 of 5900 completed
3600 observations
Notes: GPS on Bench Marks Web Map (2018)
https://geodesy.noaa.gov/GPSonBM/webmap/

## Slide 25
GEOID18
Notes: As noted in the Blueprint 2 document
https://geodesy.noaa.gov/library/pdfs/NOAA_TR_NOS_NGS_0064.pdf
NAPGD2022 will include all of the following
Geopotential Model of 2022 (GM2022) will include:
Static Geopotential model of 2022 (SGM2022)
Dynamic Geopotential model of 2022 (DGM2022)
GEOID2022 will include:
Static Geoid model of 2022 (SGEOID2022)
Dynamic Geoid model of 2022 (DGEOID2022)
DEFLEC2022 will include:
Static Deflection of the Vertical model of 2022 (SDEFLEC2022)
Dynamic Deflection of the Vertical model of 2022 (DDEFLEC2022)
GRAV2022
Static Gravity model of 2022 (SGRAV2022)

## Slide 26
SPCS of 2022
https://geodesy.noaa.gov/SPCS/
Special Publication, Policy, Procedures, and FRN
State Plane Coordinate Systems of 1927 (134 zones) and 1983 (125 zones)
Notes: State Plane Coordinate System
https://geodesy.noaa.gov/SPCS/index.shtml
2022 Policy Changes
https://geodesy.noaa.gov/SPCS/draft-policy.shtml

## Slide 27
How Can You Prepare
Metadata is essential
    Improves reliability and accuracy of data
    Increases value and usefulness
Transform and collect data in current datums
    NAD83 (2011), NAVD88

## Slide 28
How Can You Prepare
Require/provide complete metadata for all mapping contracts
    What datum(s)
    how collected and processed
Preserve all original observations
    particularly when referenced to
    ellipsoid (GNSS)

## Slide 29
Recent Publications
Blueprint Documents for 2022
  Part 1: Geometric Coordinates
  Part 2: Geopotential Coordinates
  Part 3: Working in the modernized NSRS*
  *May 2019
The State Plane Coordinate System History, Policy, and Future Directions
  NOAA Special Publication NOS NGS 13
Notes: Links on the slide.

## Slide 30
Importance of Coordination
14 Advisors
32 Coordinators
Notes: NGS Regional Geodetic Advisors
https://geodesy.noaa.gov/ADVISORS/
State Geodetic Coordinators
https://geodesy.noaa.gov/ADVISORS/state-geodetic-coordinators.shtml

## Slide 31
NGS Resources
NGS Training Center
  https://geodesy.noaa.gov/web/science_edu/training/
Educational Videos
  https://geodesy.noaa.gov/datums/newdatums/WatchVideos.shtml
NGS Webinar Series
  https://geodesy.noaa.gov/web/science_edu/webinar_series/
Geospatial Summit (May 6-7, 2019 Silver Spring, MD)
  https://geodesy.noaa.gov/geospatial-summit/
Presentation Library
  https://geodesy.noaa.gov/web/science_edu/presentations_library/

## Slide 32
Questions?
NSGIC Midyear Meeting
March 6, 2019
Brian Shaw
brian.shaw@noaa.gov
Magnitude of the Deflection of the Vertical