## Slide 1: A New State Plane Coordinate System
for the Modernized National Spatial Reference System of the United States
Michael L. Dennis, PhD, PE, PLS
SPCS2022 Project Manager
American Geophysical Union
2024 Annual Meeting
Washington DC, December 9-13
NGS Presentations Library

## Slide 2: State Plane Coordinate System of 2022 (SPCS2022)
Part of modernizing the National Spatial Reference System (NSRS)
Third generation of State Plane
  First in 1930s (SPCS 27), second in 1980s (SPCS 83)
  Widely used in surveying, engineering, and GIS
  Same 3 conformal map projection types
  Same ellipsoid as SPCS 83 (GRS80)
Same as existing State Plane, but different…
  Based on new terrestrial reference frames instead of NAD 83
  More zones, most designed by state stakeholders
  Designed to reduce linear distortion at topographic surface (i.e., reduce difference between “grid” and “ground” distances)
Transverse Mercator
Hotine Oblique Mercator
Lambert Conformal Conic

## Slide 3: SPCS2022 zone layers
1 layer: 12 states plus 6 territories
2 layers: 28 states plus Gulf of Mexico
3 layers: 9 states
Plus 10 special use zones (2 zones overlap 5 states)
Every state and territory has a statewide zone layer

## Slide 4: Number of SPCS2022 zones (preliminary)
Designs by NGS
  153 zones
  Includes 54 statewide zones…
  …and 10 “special use” zones (in more than one state or no state at all)
Designs by state stakeholders
  819 zones in 28 states
Total = 972 zones for 56 states and territories
Compare to 125 zones in existing State Plane (SPCS 83)

## Slide 5: SPCS2022 distortion design philosophy
Linear distortion minimized at topographic surface (not ellipsoid surface)
  Purpose: reduce difference between projected “grid” and actual “ground” distances
  Population distribution also taken into account in NGS designs
What is linear distortion?
  Map projection “scale error” at topographic surface
  Unique (i.e., same in every direction) only for conformal projections
  Given here in parts per million (ppm) = mm of distortion per km
Linear distortion | = | Projected minus actual distance | 
 |  | Actual distance | 
= | Combined factor - 1

## Slide 6: Map projection linear distortion
Distortion at a point computed as:
  where
    k = grid point scale factor (distortion due to Earth curvature)
    h = ellipsoid height of point (distortion due to height)
    R = Earth geometric mean radius curvature
  < 0  projected (grid) distance shorter than true horizontal “ground” distance
  > 0  projected (grid) distance longer than true horizontal “ground” distance
Height (“elevation”) factor
Grid point scale factor
Combined factor

## Slide 7
Grid distance < ellipsoid distance < ground distance (k < 1 and δ < 0)
Grid distance > ellipsoid distance < ground distance (k > 1 and δ < 0)
Projection axis (k0 < 1)
Ellipsoid surface
Ellipsoid distance
Topographic surface
Horizontal ground distance
Ellipsoid distance
> ellipsoid distance and > grid distance
Linear distortion with respect to ellipsoid surface
Projection surface (secant)
This design approach used for SPCS 27 and 83 (minimizes distortion with respect to ellipsoid)
7
k0 = scale on projection axis
LCC: central parallel
TM: central meridian
OM: skew axis

## Slide 8
Projection axis
Changing projection axis to reduce distortion variation
Non-intersecting
( > 1)
Ellipsoid surface
h2
h1
Grid distance = ground distance at many points
Ellipsoid height of surface not constant:
h1 ≠ h2
Topographic surface
8
This design approach used for SPCS2022 (minimizes distortion with respect to topography)
R2
R1

## Slide 9: Linear distortion magnitudes
Parts per million | Centimeters per kilometer | Feet per mile | Dimensionless ratio | Examples
20 ppm | 2 cm/km | 0.11 ft/mile | 1:50,000 | Typical “low distortion projection” limit
50 ppm | 5 cm/km | 0.26 ft/mile | 1:20,000 | Minimum distortion for designs by NGS
100 ppm | 10 cm/km | 0.53 ft/mile | 1:10,000 | Historic State Plane distortion design limit
400 ppm | 40 cm/km | 2.11 ft/mile | 1:2,500 | UTM distortion design limit

## Slide 10
SPCS2022 linear distortion (preliminary)
Green is ±50 ppm (±0.26 ft/mile)
Distortion performance: ±46 ppm
Performance percentages:
90% population
87% cities & towns
70% total area
Mean weighted by population: -3 ppm
GREEN: grid = ground (within ±50 ppm)
Grid versus ground distance
BLUE: grid SHORTER than ground
RED: grid LONGER than ground
90%
75%
50%
Performance must satisfy at least:

## Slide 11
SPCS 83 linear distortion (existing)
Green is ±50 ppm (±0.26 ft/mile)
Distortion performance: ±159 ppm
Performance percentages:
90% population
85% cities & towns
59% total area
Mean weighted by population: -75 ppm

## Slide 12: State Plane Coordinate System of 2022
Third generation of State Plane
  Likely most widely used projected coordinate system in United States
  SPCS2022 designed to minimize linear distortion at “ground”
  Supports use of NSRS in surveying and engineering
SPCS2022 will be released with rollout of Modernized NSRS
  Final definitions available in early 2025
  Release with “new datums” in 2026
  A truly customer-driven solution…
NGS Presentations Library
Online interactive SPCS2022 maps
Thank you!
GEODESY for the PEOPLE