## Slide 1
Grids for the Future A New Approach for Designing State Plane Coordinate System Zones
Michael Dennis, PhD, PE, PLS, M.ASCE

## Slide 2
SPCS2022
Making the Earth flat again
…one zone at a time
Surveyors and engineers love projected coordinate systems

## Slide 3
How surveyors and engineers see the Earth…

## Slide 4: A “flat Earth” for the future
State Plane Coordinate System of 2022 (SPCS2022)
Similar to existing State Plane…
  Same 3 map projection types
  Same ellipsoid (GRS 80)
But different…
  Based on new datums instead of NAD 83
  Designed to reduce difference between “grid” and “ground”
  Many more “zones”
  Zones “layers” will exist in most states
Transverse Mercator (TM)
Oblique Mercator (OM)
Lambert Conformal Conic (LCC)

## Slide 5: Getting acquainted with SPCS2022
Overall distortion design philosophy
  Linear distortion minimized (or “optimized”) at topographic surface (not at ellipsoid surface)
  Purpose: to reduce difference between and projected “grid” and actual “ground” distances in areas where people actually work
What is linear distortion?
  Defined at a point (infinitesimal distances)
  Unique (i.e., same in every direction) only for conformal projections
  Given here in parts per million (ppm) = mm per km
Linear distortion | = | δ | = | Projected minus actual distance
 |  |  |  | Actual distance

## Slide 6: Map projection linear distortion
Distortion at a point computed as:
  where
    k = grid point scale factor (distortion due to Earth curvature)
    h = ellipsoid height of point (distortion due to change in height)
    R = Earth geometric mean radius curvature
  < 0  projected (grid) distance shorter than true (ground) distance
  > 0  projected (grid) distance longer than true (ground) distance
Height (“elevation”) factor
Grid point scale factor
Combined factor

## Slide 7
Grid distance < ellipsoid distance < ground distance (k < 1 and δ < 0)
Grid distance > ellipsoid distance < ground distance (k > 1 and δ < 0)
Projection axis (k0 < 1)
Ellipsoid surface
Ellipsoid distance
Topographic surface
Horizontal ground distance
Ellipsoid distance
> ellipsoid distance and > grid distance
Linear distortion with respect to ellipsoid surface
h
R
Projection surface (secant)
This design approach used for SPCS 27 and 83 (minimizes distortion with respect to ellipsoid)
7
k0 = scale at projection axis

## Slide 8
Projection axis (k0 > 1)
Projection surface (non-intersecting)
Ellipsoid surface
Ellipsoid distance
Topographic surface
Horizontal ground distance
> ellipsoid distance and > grid distance
Linear distortion with respect to topographic surface
h
R
Grid distance > ellipsoid distance ≈ ground distance (k > 1 and δ ≈ 0)
8

## Slide 9: Projection axis
Projection axis is line along which scale = is minimum and constant*
Projection axes for projections used in State Plane:
  Lambert Conformal Conic (LCC): central parallel,
  Transverse Mercator (TM): central meridian,
  Oblique Mercator (OM): skew axis (“initial line”) with azimuth at origin
Distortion a function of the following projection parameters:
  LCC: and
  TM: and
  OM: , , , and
  *Scale is not constant on OM skew axis (equals at origin and changes slowly with distance from origin)

## Slide 10: Minimizing linear distortion
Distortion function of both and
  = distance from projection axis (kilometers)
  = change in ellipsoid height (meters)
Minimize both and simultaneously
  increases with square of distance
  increases linearly with change in height
  Treating separately can lead to poor results

## Slide 11
Projection axis
“Non-intersecting” conformal map projection
Non-intersecting
( > 1)
Ellipsoid surface
Purpose is to reduce linear distortion at “ground” (topographic surface).
But distortion can vary considerably across area of interest.
Grid distance = ground distance at a point
Grid distance = ground distance at a point
Grid distance ≈ ground distance over finite distance
Topographic surface
11

## Slide 12
Projection axis
“Non-intersecting” conformal map projection
Non-intersecting
( > 1)
Ellipsoid surface
Topographic surface
12

## Slide 13
Projection axis
Changing projection axis to reduce distortion variation
Non-intersecting
( > 1)
Ellipsoid surface
h2
h1
Grid distance = ground distance at many points
ONLY way to reduce variation in distortion is to change projection axis location (or change projection).
Ellipsoid height of surface not constant:
h1 ≠ h2
Topographic surface
IMPORANT: For large areas, there is no single defining ellipsoid height for scaling the projection.
13
This design approach used for SPCS2022 (minimizes distortion with respect to topography)
Projection axis scale can be less than 1 for steeply sloping areas even if heights are large.

## Slide 14
Projection axis
Non-intersecting
( > 1)
Ellipsoid surface
Grid distance = ground distance at a point
Grid distance = ground distance at a point
Topographic surface
h2
h1
Ellipsoid height of surface not constant:
h1 ≠ h2
IMPORANT: For large areas, there is no single defining ellipsoid height for scaling the projection – even if there is no attempt to account for topographic slope.
NOT changing projection axis to reduce distortion variation
14

## Slide 15: Linear distortion design criterion
Initial estimate of linear distortion design criterion as:
  w = zone width (perpendicular to projection axis) in km
  with following simplifying assumptions:
    R = constant mean earth radius (6371 km)
    = 1 (i.e., tangent to ellipsoid)
    Constant topographic height
Following distortion range categories (in ppm) used in design:
  Small “low distortion” zones: ±5, ±10, ±20, ±30, ±40 ppm
  Typical SPCS zones: ±50, ±75, ±100, ±150, ±200, ±300, ±400, ±500 ppm
  Very large zones: ±750, ±1000 , ±1500 , ±2000 , ±3000 , ±4000 , ±5000 ppm

## Slide 16: Linear distortion magnitudes
Parts per million | Centimeters per kilometer | Feet per mile | Dimensionless ratio
20 ppm | 2 cm/km | 0.1 ft/mile | 1:50,000
50 ppm | 5 cm/km | 0.3 ft/mile | 1:20,000
100 ppm | 10 cm/km | 0.5 ft/mile | 1:10,000
400 ppm | 40 cm/km | 2.1 ft/mile | 1:2,500

## Slide 17: Four steps of overall design process
Select projection type and initial distortion design criterion,
  Place projection axis in center of design area
  Set axis scale to reasonable initial value (e.g., gives zero mean distortion)
  OM projection origin location and skew axis azimuth requires special process
    Initially determined using minimum bounding rectangle by width
    Bounded polygon must be in projected coordinate system
    Refined during design process to account for systematic topographic slope
Move projection axis to minimize range in distortion for entire zone
  Also evaluate distortion range for cities and towns
  Also balance positive distortion at zones edges

## Slide 18: Four steps of overall design process (cont’d)
Modify axis scale such that all of the following are within :
  ≥ 90% of population
  ≥ 75% of all cities and towns (by location only)
  ≥ 50% of entire zone area
Evaluate and refine design
  Mean for entire zone (arithmetic and weighted by population) and for all cities
  Balance positive and negative distortion for entire zone area (and for cities)
  Avoid positive distortion > 2 × negative distortion magnitude
  60 – 80% of zone area with negative distortion (for zones with ~50 ppm)
  IMPORTANT: Create distortion map

## Slide 19: U.S. Census blocks
Used blocks from 2010 Census for SPCS2022 zone design

## Slide 20: Population density
Created density raster from Census block data (done for visualization, not for design)

## Slide 21: Population count
Equal area population count raster created from block data at 1 km resolution for design.
(note white cells with zero population)

## Slide 22: Topographic heights
Topographic ellipsoid heights added to population point data (computed from DEM and hybrid geoid model)

## Slide 23: Final dataset for entire state
Equal area 1-km resolution point dataset with population, position, and height for SPCS2022 design
Range in ellipsoid height for population points = 3166 m (10,387 ft)

## Slide 24: Dataset for zone design
Select subset of population points that are within polygon of zone being designed (Arizona Central Zone).
Range in ellipsoid height for population points = 3058 m (10,033 ft)

## Slide 25
Design process
Projection type and distortion design criterion
  TM (long north-south)
  = ±114 ppm  ±100 ppm
  Select 111°54’W (midpoint)
  = 1.000 12 (zero mean)
Projection axis location
  Minimize overall range
  Minimize range for cities
  Not same as min std dev
  Select 112°03’W

## Slide 26
Design process
Projection type and distortion design criterion
  TM (long north-south)
  = ±114 ppm  ±100 ppm
  Select 111°54’W (midpoint)
  = 1.000 12 (zero mean)
Projection axis location
  Minimize overall range
  Minimize range for cities
  Not same as min std dev
  Select 112°03’W
  Consider distortion extremes
  Balance positive distortion

## Slide 27
Design process
Modify axis scale based on design criterion of ±100 ppm
  For = 1.000 07 have:
  90% of population
  76% of cities and towns
  55% of total area
Evaluate and refine
  Balance positive & negative

## Slide 28
Design process
Modify axis scale based on design criterion of ±100 ppm
  For = 1.000 07 have:
  90% of population
  76% of cities and towns
  55% of total area
Evaluate and refine
  Balance positive & negative
  Weighted mean by population
  Mean entire zone & all cities
  Max and min entire zone
  Max and min all cities
  Create distortion map…

## Slide 29: Linear distortion map SPCS2022
Arizona Central Zone
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±50 | 76% | 49% | 34%
±75 | 81% | 61% | 45%
±100 | 90% | 76% | 55%
±150 | 96% | 88% | 74%
City and area statistics (ppm): |  |  | 
 | Min | -323 | -505
 | Max | +188 | +232
 | Range | 511 | 737
 | Mean | -20 | -54
Mean weighted by pop = +21 |  |  | 

## Slide 30: Linear distortion map SPCS 83
Arizona Central Zone
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±50 | 0.1% | 3% | 6%
±75 | 0.5% | 7% | 10%
±100 | 5% | 10% | 14%
±150 | 48% | 36% | 25%
City and area statistics (ppm): |  |  | 
 | Min | -491 | -684
 | Max | +54 | +100
 | Range | 544 | 784
 | Mean | -195 | -224
Mean weighted by pop = -154 |  |  | 

## Slide 31: Status of zone layout and designs
Designs by NGS
  159 zones (including 54 statewide)
  Plus 3 “special use zones” (in more than one state)
Designs by state stakeholders
  806 zones in 28 states
  Most are “low-distortion projections” (LDPs)
Total = 968 zones for 56 states and territories
  Number will likely decrease slightly
Compare to 125 zones in existing State Plane

## Slide 32: SPCS2022 zone layers (preliminary)
1 layer: 12 states plus 6 territories
2 layers: 28 states
3 layers: 10 states

## Slide 33: Number of SPCS2022 zones (preliminary)
CONUS, Alaska, and Hawaii
Three island zones not shown:
Puerto Rico and U.S. Virgins Islands
American Samoa
Guam and the Commonwealth of the Northern Mariana Islands

## Slide 34: Existing SPCS 83 linear distortion
106 zones (CONUS)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 17% | 11% | 6%
±50 | 40% | 30% | 17%
±100 | 74% | 68% | 41%
±400 | 99% | 98% | 91%
City and area statistics (ppm): |  |  | 
 | Min | -913 | -1038
 | Max | +206 | +223
 | Range | 1120 | 1261
 | Mean | -98 | -178
Mean weighted by pop = -75 |  |  | 

## Slide 35: SPCS2022 linear distortion (prelim)
49 zones (CONUS)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 14% | 12% | 7%
±50 | 27% | 26% | 18%
±100 | 48% | 48% | 36%
±400 | 91% | 93% | 88%
City and area statistics (ppm): |  |  | 
 | Min | -1512 | -1627
 | Max | +2888 | +2987
 | Range | 4400 | 4614
 | Mean | -86 | -120
Mean weighted by pop = -100 |  |  | 

## Slide 36: SPCS2022 linear distortion (prelim)
646 zones (35 states)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 76% | 70% | 54%
±50 | 92% | 88% | 73%
±100 | 98% | 97% | 89%
±400 | 100% | 100% | 99.9%
City and area statistics (ppm): |  |  | 
 | Min | -400 | -684
 | Max | +245 | +295
 | Range | 644 | 979
 | Mean | -5 | -23
Mean weighted by pop = -4 |  |  | 

## Slide 37: SPCS2022 linear distortion (prelim)
187 zones (10 states)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 78% | 78% | 73%
±50 | 91% | 90% | 88%
±100 | 99.8% | 99% | 97%
±400 | 100% | 100% | 100%
City and area statistics (ppm): |  |  | 
 | Min | -261 | -465
 | Max | +120 | +240
 | Range | 381 | 705
 | Mean | -3 | -12
Mean weighted by pop = -1 |  |  | 

## Slide 38: SPCS2022 linear distortion (prelim)
846 zones (CONUS)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 76% | 71% | 58%
±50 | 92% | 89% | 76%
±100 | 98% | 97% | 89%
±400 | 100% | 100% | 99.9%
City and area statistics (ppm): |  |  | 
 | Min | -407 | -1438
 | Max | +486 | +2624
 | Range | 893 | 4062
 | Mean | -6 | -23
Mean weighted by pop = -4 |  |  | 

## Slide 39: Existing SPCS 83 linear distortion
106 zones (CONUS)
Percent within distortion (ppm):
Distor | Pop | Cities | Area
±20 | 17% | 11% | 6%
±50 | 40% | 30% | 17%
±100 | 74% | 68% | 41%
±400 | 99% | 98% | 91%
City and area statistics (ppm): |  |  | 
 | Min | -913 | -1038
 | Max | +206 | +223
 | Range | 1120 | 1261
 | Mean | -98 | -178
Mean weighted by pop = -75 |  |  | 

## Slide 40: What to expect for SPCS2022
Coordinates will change by at least 10,000 m (~6 miles)
Less difference between “grid” and “ground”
More than one zone “layer” in most states
  Zones will be similar to SPCS 83 in some states
  Zones will be very different in most states
Every state will have a statewide zone layer
Rollout in 2025
  Along with rest of modernized NSRS
  Earlier usage with NAD 83 in some states
Questions?