## Slide 1: The Circle is Now Complete
Introducing the State Plane Coordinate System of 2022
Michael L. Dennis, PhD, PE, PLS
SPCS2022 Project Manager
UESI Surveying & Geomatics 2024 Conference
June 4, 2024
nearly

## Slide 2
This is what we were hoping to show you today…

## Slide 3
…but this is where we are (functional but still under construction)

## Slide 4
Perhaps “flatten” the Death Star with its own SPCS2022 zone?

## Slide 5: State Plane Coordinate System of 2022 (SPCS2022)
Part of modernizing the National Spatial Reference System (NSRS)
Third generation of State Plane
  First in 1930s (SPCS 27), second in 1980s (SPCS 83)
  Same 3 conformal map projection types
  Same ellipsoid as SPCS 83 (GRS80)
Same as existing State Plane, but different…
  Based on new terrestrial reference frames instead of NAD 83
  More zones, most designed by state stakeholders
  Designed to reduce linear distortion at topographic surface (i.e., reduce difference between “grid” and “ground” distances)
Design of all SPCS2022 zones (nearly) done!
Transverse Mercator
Hotine Oblique Mercator
Lambert Conformal Conic

## Slide 6: SPCS2022 zone layers
1 layer: 12 states plus 6 territories
2 layers: 28 states
3 layers: 10 states

## Slide 7: Number of SPCS2022 zones (preliminary)
Designs by NGS
  165 zones
  Includes 54 statewide zones…
  …and 3 “special use” zones (in more than one state)
Designs by state stakeholders
  802 zones in 28 states
Total = 967 zones for 56 states and territories
Compare to 125 zones in existing State Plane

## Slide 8: State Plane Coordinate Systems of 1983 and 1927

## Slide 9: State Plane Coordinate System of 2022

## Slide 10: SPCS2022 distortion design philosophy
Linear distortion minimized at topographic surface (not ellipsoid surface)
  Purpose: reduce difference between projected “grid” and actual “ground” distances
  Population distribution also taken into account in NGS designs
What is linear distortion?
  Map projection “scale error” at topographic surface
  Unique (i.e., same in every direction) only for conformal projections
  Given here in parts per million (ppm) = mm of distortion per km
Linear distortion | = | Projected minus actual distance | 
 |  | Actual distance | 
= | Combined factor - 1

## Slide 11: Linear distortion magnitudes
Parts per million | Centimeters per kilometer | Feet per mile | Dimensionless ratio | Examples
20 ppm | 2 cm/km | 0.11 ft/mile | 1:50,000 | Typical “low distortion projection” limit
50 ppm | 5 cm/km | 0.26 ft/mile | 1:20,000 | Minimum distortion for designs by NGS
100 ppm | 10 cm/km | 0.53 ft/mile | 1:10,000 | Historic State Plane distortion design limit
400 ppm | 40 cm/km | 2.11 ft/mile | 1:2,500 | UTM distortion design limit

## Slide 12
SPCS2022 linear distortion (preliminary)
Green is ±50 ppm (±0.26 ft/mile)
Distortion performance: ±370 ppm
Performance percentages:
90% population
91% cities & towns
86% total area
Mean weighted by population: -99 ppm
GREEN: grid = ground (within ±50 ppm or ±0.26 ft/mile)
Grid versus ground distance
BLUE: grid SHORTER than ground
RED: grid LONGER than ground

## Slide 13
SPCS 83 linear distortion (existing)
Green is ±50 ppm (±0.26 ft/mile)

## Slide 14
SPCS 83 linear distortion (existing)
Green is ±50 ppm (±0.26 ft/mile)
These 2 zones removed

## Slide 15
SPCS 83 linear distortion (existing)
Green is ±50 ppm (±0.26 ft/mile)
This zone changed, 7 zones added in multizone layer

## Slide 16
SPCS2022 linear distortion (preliminary)
Green is ±50 ppm (±0.26 ft/mile)
Distortion performance: ±45 ppm
Performance percentages:
90% population
87% cities & towns
69% total area
Mean weighted by population: -4 ppm

## Slide 17
SPCS 83 linear distortion (existing)
Green is ±50 ppm (±0.26 ft/mile)
Distortion performance: ±159 ppm
Performance percentages:
90% population
85% cities & towns
59% total area
Mean weighted by population: -75 ppm

## Slide 18
SPCS2022 linear distortion (preliminary)
Green is ±50 ppm (±0.26 ft/mile)
Distortion performance: ±45 ppm
Performance percentages:
90% population
87% cities & towns
69% total area
Mean weighted by population: -4 ppm

## Slide 19: Burning questions about NSRS Modernization
When will it be done?
What will it consist of?
What formats will be used?
What will it look like?
Products on alpha will move to beta starting this year

## Slide 20: Alpha products are NOT final products!
Preliminary
For illustrative purposes only
Not authoritative
Under active development
Subject to change without notice
Feedback to: ngs.feedback@noaa.gov
https://alpha.ngs.noaa.gov/index.shtml

## Slide 21: Alpha SPCS2022 Home
https://alpha.ngs.noaa.gov /SPCS/index.shtml
Gives date last updated
Links to other SPCS2022 pages in sidebar:
  Zone information
  Distortion maps
  Online interactive maps (SPCS2022 Experience)
  Alpha NCAT
  Additional information
  Feedback

## Slide 22: ArcGIS Online SPCS2022 Experience
Online interactive maps
Shows distortion and gives zone definitions
Being updated now
Accessible on mobile devices

## Slide 24: That’s great, but when will SPCS2022 be done?
SPCS2022 included with rollout of Modernized NSRS
  Getting feedback from stakeholders and others NOW
  In process of finalizing designs NOW
Zone designs done and shared with world by late 2024 or early 2025
  Provide definitions directly usable by commercial partners
  Definitions also in EPSG Geodetic Parameter Dataset and ISO Geodetic Registry
Modernized NSRS becomes official in 2026 (after beta)
  SPCS2022 zones can then be added, removed, changed
  Updated Policy and Procedures will describe the process

## Slide 25: Where to learn more…
geodesy.noaa.gov
Thank you!