## Slide 1
The State Plane Coordinate System
History, Policy, and Future Directions
March 8, 2018
Michael L. Dennis
SPCS2022 Project Manager

## Slide 2: A Tale of Two Webinars on the State Plane Coordinate System (SPCS)
First webinar today (March 8)
  History and status of SPCS 27 and SPCS 83
  Map projection concepts
  Introduction to SPCS2022
Next webinar on April 12
  Greater detail on SPCS2022 policy and procedures
  Additional technical information
  More SPCS2022 zone design examples
Your questions today will help with April webinar!

## Slide 4: Why a new State Plane system?
geodesy.noaa.gov

## Slide 5: New State Plane Coordinate System
State Plane Coordinate System of 2022 (SPCS2022)
  Referenced to new 2022 Terrestrial Reference Frames (TRFs)
  Based on same reference ellipsoid (GRS 80)
  Same 3 conformal projection types
    Lambert Conformal Conic (LCC)
    Transverse Mercator (TM)
    Oblique Mercator (OM)
NGS in process of specifying SPCS2022 characteristics
  Draft policy and procedures for public comment
  Federal Register Notice (FRN) on policy and procedures
  New report on State Plane history, policy, and future (done!)
NOTE: SPCS2022 policy, procedures, and FRN currently in review
  Approved version may differ from what is presented here but should be finalized before April 12 webinar

## Slide 6: When feedback is needed (draft)
SPCS2022 Federal Register Notice
August 31, 2018 for public comment on draft policy & procedures
Includes “special purpose” zones
SPCS2022 procedures
December 31, 2019 for SPCS2022 zone requests and proposals
  Requests are for zone designs by NGS
  Proposals are for zone designs by others
December 31, 2020 for submittal of approved designs by others
  Proposal must first be approved by NGS
  Designs must be complete before NGS review
After deadlines, requests will be for changes to SPCS2022
More details will be provided in April 12 webinar

## Slide 7: History and Future of State Plane
SPCS created 85 years ago
  SPCS 27: 1933 – 1986 (53 years, with some changes)
  SPCS 83: 1986 – 2022 (36 years, with some changes)
  SPCS2022: 2022 – ? (at least a few decades…)
SPCS2022 will likely be around for a long time
  Honor the history and legacy of SPCS…
  …while building a system for the future
High visibility and big impact
  SPCS used by many in US geospatial community
  NGS already contacted by 16 states about SPCS2022

## Slide 8: SPCS Special Publication
History of NGS projections (1853 to present)
SPCS policies and legislation
Departures from policy and convention
Recent developments in projected coordinate systems
Appendices
  Defining parameters for ALL zones of ALL versions of SPCS, plus additional information
  Status of SPCS 83 legislation and foot conversions
https://geodesy.noaa.gov/library/pdfs/ NOAA_SP_NOS_NGS_0013_v01_2018-03-06.pdf

## Slide 9
geodesy.noaa.gov/SPCS/
On “Learn More” page will soon add:
Spreadsheets with complete definitions for all SPCS 27 and SPCS 83 zones
Shapefiles of all SPCS 27 and SPCS 83 zones with parameters as attributes

## Slide 10: An interesting and varied history
Initially created for North Carolina at customer request
  Gave practical access to National Spatial Reference System (NSRS)
  SPCS 27 started in 1933, completed in 1934(!)
Changes from SPCS 27 to SPCS 83:
  Multi-zone to single-zone for some states (SC, NE, MT)
  Change in grid origin and units (US feet to meters)
  American Samoa has no SPCS 83 zone
Departures from policy and convention:
  Guam used non-conformal projection for SPCS 27
  Michigan used “scaled” ellipsoid for SPCS 27 (after 1963)
  California added small Los Angeles County zone for SPCS 27
  Kentucky has “layered” (overlapping) SPCS 83 zones
  Montana single SPCS 83 zone greatly exceeds 1:10,000 scale error

## Slide 11
State Plane Coordinate Systems of 1927 (134 zones) and 1983 (125 zones)
Guam SPCS 27 zone a non-conformal projection
American Samoa only in SPCS 27, not SPCS 83
Two zones in SPCS 27, one in SPCS 83
Guam SPCS 83 zone added in 1995

## Slide 12
Original SPCS 27, as of 1934 (110 zones total)

## Slide 13
Final SPCS 27, as of 1968 (112 zones in CONUS, 131 zones total)
Reduced distortion zones added: CA 7 (1945) MI (1964)

## Slide 14
Final SPCS 83, as of 2001 (108 zones in CONUS, 125 zones total)
KY statewide zone added in 2001

## Slide 15
Alaska State Plane Coordinate Systems of 1927 and 1983 (10 zones)
Islands in Zone 9 are referenced to local datums other than NAD 27

## Slide 16
Hawaii State Plane Coordinate Systems of 1927 and 1983 (5 zones)
“SPCS 27” version referenced to Old Hawaiian Datum
Puerto Rico and U.S. Virgin Islands State Plane Coordinate Systems of 1927 (2 zones) and 1983 (1 zone)
“SPCS 27” version referenced to
Puerto Rico 1940 Datum

## Slide 17: Issues with SPCS 83
Incomplete NGS documentation (until now)
Inconsistent zone definitions
  Highly variable linear distortion
  “Layered” zones exist (Kentucky)
  Inconsistent specification of grid origins
  Scale explicitly defined for some zones, implicitly for others
  Incomplete coverage of U.S. territories
Note common usage of SPCS “at ground”
  Many surveyors & engineers scale SPCS to topo surface
  NGS used to give workshops on this methodology
  Process incorporated in most surveying software
  Shows desire to work “at ground”

## Slide 18: Map projection concepts
Linear distortion (“scale error”)
  Amount map projection “grid” distance differs from true (curved) horizontal distance
    Usually at topographic surface (“grid” vs. “ground” distance)
    Can also be at ellipsoid surface (“grid” vs. ellipsoid distance)
Conformal map projection
  Linear distortion unique at a point (same in every direction)
  Simple relationship between grid and geodetic azimuth
  SPCS2022 zones will use following conformal projections:
    Lambert Conformal Conic (LCC)
    Transverse Mercator (TM)
    Oblique Mercator (OM)

## Slide 19: SPCS2022 characteristics (draft)
Technical requirements
  Linear distortion design criterion at topographic surface (not at ellipsoid surface)
    Difference in distance between “grid” and “ground”
  Use 1-parallel definition for LCC projections
Other characteristics
  Default designs (if no consensus stakeholder input)
  “Layered” zones
  Low-distortion projections (LDPs)
  “Special purpose” zones

## Slide 20
Gnomonic projection (non-conformal)
Stereographic projection (conformal)
Orthographic projection (non-conformal)
Ray source
at infinity
Ray source at opposite side of Earth
Ray source at center of Earth
Projection surface
Projection surface
Projection surface
Can think of projection as “light rays” projecting onto surface
However, this only works for a few sphere-based projections

## Slide 21
e.g., Lambert conformal conic
(used for SPCS)
Polar aspect
Oblique aspect
Central parallel
Standard parallels
Origin
e.g., stereographic (not used for SPCS)
One-parallel (tangent)
Two-parallel (secant)
Conic projections
Planar (azimuthal) projections
Developable surfaces: Planes and cones
Examples given are CONFORMAL projections
Standard parallel

## Slide 22
Cylindrical projections
Central meridian
Skew axis
Equator
“Regular” aspect
Transverse aspect
Oblique aspect
e.g., Mercator
(not used for SPCS)
e.g., transverse Mercator
(used for SPCS)
e.g., oblique Mercator
(used for SPCS)
Developable surfaces: Cylinders
Examples given are CONFORMAL projections

## Slide 23
Grid distance > ellipsoid distance
Projection axis
Linear distortion with respect to ellipsoid
Ellipsoid surface
Grid distance < ellipsoid distance
Ellipsoid distance
Ellipsoid distance
Projection surface (secant)
This design approach used for SPCS 27 and 83 (minimizes distortion with respect to ellipsoid)

## Slide 24
Grid distance < ellipsoid distance < ground distance
Grid distance > ellipsoid distance < ground distance
Ellipsoid surface
Ellipsoid distance
Topographic surface
Horizontal ground distance
Ellipsoid distance
> ellipsoid distance and > grid distance
Linear distortion with respect to topographic surface
Projection surface (secant)
This design approach used for SPCS 27 and 83 (minimizes distortion with respect to ellipsoid)
Projection axis

## Slide 25
Projection surface (non-intersecting)
Ellipsoid surface
Ellipsoid distance
Topographic surface
Horizontal ground distance
> ellipsoid distance and > grid distance
Linear distortion with respect to topographic surface
Grid distance > ellipsoid distance ≈ ground distance
This design approach will be used for SPCS2022 (minimizes distortion with respect to topography)
Projection axis

## Slide 26: Linear distortion magnitudes ppm = parts per million (mm/km)
±20 ppm = 2 cm/km = 0.1 ft/mile = 1 : 50,000
  Often used as “low distortion” design criterion (at ground)
±50 ppm = 5 cm/km = 0.3 ft/mile = 1 : 20,000
  Minimum design criterion for SPCS2022 designs by NGS (at ground)
±100 ppm = 10 cm/km = 0.5 ft/mile = 1 : 10,000
  “Nominal” maximum State Plane value (on ellipsoid)
  Can be much greater at topo surface
±400 ppm = 40 cm/km = 2.1 ft/mile = 1 : 2,500
  Maximum design criterion for SPCS2022 zones (at ground)
  Maximum UTM value (on ellipsoid)
Nominal distortion criterion (on ellipsoid) for SPCS 27 and 83 zones (although greatly exceeded for some zones in SPCS 83).

## Slide 27: Linear distortion magnitudes ppm = parts per million (mm/km)
±20 ppm = 2 cm/km = 0.1 ft/mile = 1 : 50,000
  Often used as “low distortion” design criterion (at ground)
±50 ppm = 5 cm/km = 0.3 ft/mile = 1 : 20,000
  Minimum design criterion for SPCS2022 designs by NGS (at ground)
±100 ppm = 10 cm/km = 0.5 ft/mile = 1 : 10,000
  “Nominal” maximum State Plane value (on ellipsoid)
  Can be much greater at topo surface
±400 ppm = 40 cm/km = 2.1 ft/mile = 1 : 2,500
  Maximum design criterion for SPCS2022 zones (at ground)
  Maximum UTM value (on ellipsoid)
Distortion range (at ground) for zones designed by NGS, as proposed in draft SPCS2022 policy and procedures.

## Slide 28: Linear distortion magnitudes ppm = parts per million (mm/km)
±20 ppm = 2 cm/km = 0.1 ft/mile = 1 : 50,000
  Often used as “low distortion” design criterion (at ground)
±50 ppm = 5 cm/km = 0.3 ft/mile = 1 : 20,000
  Minimum design criterion for SPCS2022 designs by NGS (at ground)
±100 ppm = 10 cm/km = 0.5 ft/mile = 1 : 10,000
  “Nominal” maximum State Plane value (on ellipsoid)
  Can be much greater at topo surface
±400 ppm = 40 cm/km = 2.1 ft/mile = 1 : 2,500
  Maximum design criterion for SPCS2022 zones (at ground)
  Maximum UTM value (on ellipsoid)
Distortion criterion (at ground) often used for “low distortion projection” (LDPs); designed by others for SPCS2022 (not by NGS)

## Slide 29: SPCS2022 characteristics (draft)
Technical requirements
  Linear distortion design criterion at topographic surface (not at ellipsoid surface)
    Difference in distance between “grid” and “ground”
  Use 1-parallel definition for LCC projections
Other characteristics
  Default designs (if no consensus stakeholder input)
  “Layered” zones
  Low-distortion projections (LDPs)
  “Special purpose” zones

## Slide 30: Lambert Conformal Conic projection
Conical developable surface
Used for many State Plane zones
Can define scale two different ways:
  Define scale explicitly on central standard parallel
  Compute scale implicitly
    From separation between two “standard” parallels
    Scale (at ellipsoid) is exactly 1 for standard parallels
The two types are mathematically identical!
  “Projection axis” for both is central standard parallel

## Slide 31: Why only a 1-parallel LCC?
Consistency
  Explicitly define projection scale (same as TM and OM)
  Can use same number of parameters as TM
  Applicable to both “secant” and “non-intersecting” cases
Simplicity
  Easier to design with respect to topography
  Scale due to separation of 2 standard parallels not obvious
  Can more readily use “clean” values for parallels
Mathematically identical to 2-parallel
  Any 2-parallel LCC can be recast as 1-parallel that behaves exactly the same

## Slide 32: Consider North Carolina SPCS 83 Zone
Central “standard” parallel
Ellipsoid
North standard parallel
South standard parallel
(projection axis)
Scale = 1
Scale = 1
(1:7849)
Scale = 0.9998 7259…
Secant Lambert Conformal Conic projection, 2-parallel definition:
Standard parallels
North = 36°10’N (exact)
South = 34°20’N (exact)
It is EXACTLY the same as this 1-parallel definition:
Central standard parallel
35°15’06.33096…”N
Scale = 0.9998 7259…
An LCC projection is defined by its projection axis, which is ALWAYS the central standard parallel

## Slide 33: SPCS2022 characteristics (draft)
Technical requirements
  Linear distortion design criterion at topographic surface (not at ellipsoid surface)
    Difference in distance between “grid” and “ground”
  Use 1-parallel definition for LCC projections
Other characteristics
  Default designs (if no consensus stakeholder input)
  “Layered” zones
  Low-distortion projections (LDPs)
  “Special purpose” zones

## Slide 34: Default SPCS2022 designs (draft)
Default needed in absence of stakeholder input
Same projections and zones for most SPCS 83 zones
Performance and coverage very similar to SPCS 83
Characteristics that differ from SPCS 83:
  Projection scale modified to minimize distortion at ground
  Lambert Conformal Conic converted to one-parallel type
  Most geodetic origins with arc-minutes evenly divisible by 3
  A few zones with different projection & zone extents

## Slide 35
 |  | SPCS 83 NC | 
Central parallel |  | 35°15’06.33…”N | 
Cen parallel scale |  | 0.9998 7259… | 
 | Height (m) | Distortion (ppm) | 
Min | -41 | -413 | 
Max | 1939 | +176 | 
Mean | 197 | -93 | 
SPCS 83 North Carolina (Lambert Conformal Conic 2-parallel)

## Slide 36
 |  | SPCS 83 NC | SPCS2022
Central parallel |  | 35°15’06.33…”N | 35°15’N
Cen parallel scale |  | 0.9998 7259… | 0.99996
 | Height (m) | Distortion (ppm) | 
Min | -41 | -413 | -325
Max | 1939 | +176 | +263
Mean | 197 | -93 | -5
SPCS2022 “default” NC (Lambert Conformal Conic 1-parallel)
No change in projection type or zone extents

## Slide 37
 |  | SPCS 83 AZ C | 
C.M. |  | 111°55’W | 
Scale |  | 0.9999 | 
 |  | Distortion (ppm) | 
Min |  | -660 | 
Max |  | +102 | 
Mean |  | -224 | 
SPCS 83 Arizona Central Zone (Transverse Mercator)
 | Height (m)
Min | 96
Max | 3607
Mean | 1177

## Slide 38
 |  | SPCS 83 AZ C | SPCS2022
C.M. |  | 111°55’W | 112°W
Scale |  | 0.9999 | 1.0001
 |  | Distortion (ppm) | 
Min |  | -660 | -455
Max |  | +102 | +277
Mean |  | -224 | -24
SPCS2022 “default” Arizona Central Zone (Transverse Mercator)
 | Height (m)
Min | 96
Max | 3607
Mean | 1177
No change in projection type or zone extents

## Slide 39: “Layered” zones (draft)
Limitations
  Max of TWO layers: Statewide and sub-zones
  If two layers, one MUST be statewide
  Minimum sub-zone dimension > 50 km
States often want statewide and small zones
  Statewide: Single geometry required for state GIS
  Sub-zones: Lower distortion for surveying/engineering
Accommodates state needs, but with restrictions
  Prevent poor design choices for statewide zones
  One already exists in SPCS 83…

## Slide 40: Kentucky layered zones
 |  | North | South | 
N parallel |  | 38°58’N | 37°56’N | 
S parallel |  | 37°58’N | 36°44’N | 
 |  | Distortion (ppm) |  | 
Min |  | -93 | -211 | 
Max |  | +17 | +42 | 
Mean |  | -56 | -67 | 
“Layered” zones
SPCS 83 Kentucky N and S zones (Lambert Conformal Conic)

## Slide 41: Kentucky layered zones
 |  | North | South | Statewide
N parallel |  | 38°58’N | 37°56’N | 38°40’N
S parallel |  | 37°58’N | 36°44’N | 37°05’N
 |  | Distortion (ppm) |  | 
Min |  | -93 | -211 | -166
Max |  | +17 | +42 | +181
Mean |  | -56 | -67 | -58
“Layered” zones
SPCS 83 Kentucky statewide zone (Lambert Conformal Conic)

## Slide 42: Linear distortion design criteria (draft)
NGS design of zones requested by stakeholders
  Limited to zones with 50-400 ppm distortion criterion
    50 ppm = 5 cm/km = 0.3 ft/mi = 1:20,000
    400 ppm = 40 cm/km = 2.1 ft/mi = 1:2,500
Design criterion < 50 ppm (“low distortion”)
  Min criterion 20 ppm = 2 cm/km = 0.1 ft/mi = 1:50,000
  Must be designed by others (not by NGS)
  Proposed and final design reviewed by NGS
What is the current situation with “low distortion” projected coordinate systems?

## Slide 44: “Special purpose” zones (FRN)
For areas with inadequate SPCS zone coverage
  Usually areas that are in more than one zone
Categories:
  Major urban areas (e.g., New York, Chicago, St. Louis)
  Large Indian reservations (e.g., Navajo Nation)
  Federal applications covering large areas (e.g., coastal mapping of Atlantic Coast; Grand Canyon)
Permitted for metro areas in 1977 policy (but never used)
Only in FRN, not in draft policy & procedures
  Intent is to get input on concept first

## Slide 45: Wrap-up
State Plane has a long and varied history
Main characteristics of SPCS2022 (draft)
  Designed with respect to “ground”
  Use 1-parallel definitions for LCCs
  Default designs similar to existing State Plane
  Can include a statewide zone plus a sub-zone layer
  LDPs can be used but must be designed by others
Stakeholder input on zones for their states
Next State Plane webinar on April 12 – register at:
  https://geodesy.noaa.gov/web/science_edu/webinar_series/Webinars.shtml
NOTE: SPCS2022 policy, procedures, and FRN currently in review
  Approved version may differ from what is presented here but should be finalized before April 12 webinar