## Slide 1: Progress of GEOID2022 beta v01
YM Wang, X Li, K Ahlgren, R Hardy, J Krcmaric
National Geodetic Survey, U.S.A.
J Huang, I Foroughi, M Veronneau
Canadian Geodetic Survey, Canada
D Avalos-Naranjo
National Institute of Statistics and
Geography, Mexico
IUGG2023 Berlin, Germany | July 10 - 20, 2023

## Slide 2: Outline
Geoid teams (NGS, CGS and INEGI)
Parameters used for GEOID2022 (a realization of NAPGP2022)
Datasets used for GEOID2022 beta v01
GRAV-D reprocessing
Development of the reference coefficient model
The experiment geoid xGEOID2020
Schedule of North American-Pacific Geopotential Datum of 2022 (NAPGD2022)

## Slide 3
T
E
A
M
S
US National Geodetic Survey
Yan Ming Wang, lead
Xiaopeng Li
Kevin Alhgren
Jordan Krcmaric
Ryan Hardy
Canadian Geodetic Survey
Jianliang Huang, lead
Marc Véronneau
John Crowley
Ismael Foroughi
National Institute of Statistics and Geography
David Naranjo Avalos, lead
Marco A. Mendoza-Martinez
Raul Munoz-Abundes

## Slide 4: Parameters used for NAPGD2022
Parameters | NAPGD2022
W0 | 62,636,856 m2s-2
GM | 3.986004415x1014 m3s-2
Realization | GEOID2022
Geometric RF | NATRF2022
Height (type) | Orthometric H = h - N
Tide system | Tide Free
Velocity of height | 
Velocity of geoid height | 
Reference epoch | 2020.0 (update 5-10 years)

## Slide 5: GEOID2022 coverage (1’x1’)
North American region
¼ of the Earth
Guam
American Samoa

## Slide 6: Data used (common data sets)
NGS, CGS, INEGI and NGA terrestrial gravity data (~ 1.9 million pts.)
Repro GRAV-D airborne gravity data (U.S. Territories)
DEM2022 at a 3″ spatial resolution
Marine gravity data: DTU21 (Andersen personal Comm., 2022) and shipboard gravity
ArcGPv2020 (Beale personal comm., 2020)
Ice thickness (Greenland)
For validation: 3 Geoid slope validation surveys, ~40,000 GPS/GNSS, TOPEX/POSEIDON over Great Lakes, water gauge data

## Slide 7: Data used (common data sets)
Canada
~255 k pts
Mexico ~110 k pts
NGA/NGS
~1.5 M pts
ARCGP20

## Slide 8: GRAV-D reprocessing
What’s NEW?
Off-level correction: proper alignment with the gravity vector
Filtering free-air disturbances: instead of full-field gravity
Absolute gravity ties: all reprocessed and checked
Trims and Edits: performed as consistently as possible
ITRF2020 reference frame
GRAV-D observations minus EGM2008 predictions [mGal]. The left panel is the original/published data, and the right is the reprocessed data.
Lake Erie
Lake Erie

## Slide 9
CONUS and PR/VI

## Slide 10
Guam and CNMI
Hawaii
Alaska

## Slide 11
Alaska

## Slide 12: Altimetric gravity anomalies (DTU21) used
DTU17 1 arcmin used in xGEOID2020
DTU21 – DTU17

## Slide 13: ARCGP20 from NGA

## Slide 14: DEM2022 and distribution of GNSS/leveling data
Resolution: 3″, or ~90 m
#GPS points over Canada: 4308
Mean: -2.1 m (xG20DEM)
RMSE: 6.9 m (xG20DEM)
# GPS on BMs over USA : 31851
Mean: -0.3 m (xG20DEM)
RMSE: 2.1 m (xG20DEM)

## Slide 15
For more details: G02p-030-IUGG23-2975July162023-1700-1830
Fourier Legendre transformation
Reference model: “Adding” GRAV-D to refA

## Slide 16: NGS CGS/INEGI computation schemes
Approach | CGS | NGS
GBVP type | Stokes – Helmert | Molodensky
Remove-Compute-Restore | Yes | Yes
Data combination | >180 km (Sat) , 55 - 180 (GRAV-D), < 55 km (Terr) | > 40 km (EGM including GRAV-D), < 40 km (Terr)
Geoid-to-Quasigeoid separation correction | No | Yes
Gravity Data Interpolation | Complete Bouguer Anomalies | Residual Free-air Anomalies/Bouguer anomalies
Glacial Ice Correction | Yes (over Greenland) | Yes (over Greenland)
Topo Mass Density Effect | No | 

## Slide 17: Experimental geoid xGEOID2020A/B
NGS and CGS computed geoid models independently in 1’×1’ spatial resolution
The combined models include the common area of the NGS and CGS models (N0°/N85°/E180°/E350°)
xGEOID20 A and B were computed using the simple arithmetic mean between CGS’s and NGS’s Models A and B, respectively.

## Slide 18: Historical GNSS/leveling Comparison in cm
 | CA #2451 A/B | USA #32276 A/B | MX #2641 A/B
Mean | -15/-15 | -56/-56 | -40/-40
STD | 14/14 | 30/30 | 18/18
Min | -68/-68 | -125/-125 | -116/-113
Max | 39/39 | 54/57 | 78/78
Range | 107/107 | 178/182 | 194/191

## Slide 19: Historical GNSS/leveling comparison by province Canada in cm

## Slide 20: Historical GNSS/leveling comparison by state, USA in cm

## Slide 21: Residual geoid along three GSVS lines

## Slide 22: TOPEX/Poseidon ground track over the Great Lakes

## Slide 23: Summery and conclusions
After removing the biases of each 1º by 1º block, standard deviations of GNSS/leveling comparisons are better than 5 cm (1σ) for all US states. The differences are slightly larger for individual Canadian provinces.
The Great Lakes satellite altimetry comparisons show 1-2 cm agreement on most tracks, but differences are larger on track 3 (Green Bay), 11 (Lake Huron), and 13 (Lake Erie).
The xGEOID20 agrees with the GSVS lines over 300 km within 1-2 cm (1σ) with no noticeable slopes, except on GSVS14.

## Slide 24: GEOID2022 schedule
2023
- beta version of GEOID2022 to be computed
- GRAV-D to be completed 100% and processed
2024
GEOID2022 to be computed and validated. It will be ready for
release with its time varying components, deflections of the
vertical and their accuracy estimation. A EGM enhanced by
GRAV-D to degree and order 2160 will be part of the release.
2025
NAPGD2022 to be released with the North America Terrestrial
Reference Frame NATRF2022