## Slide 1
NGS Overview and New Datums
Jeff Jalbrzikowski, P.S., GISP, CFS
Appalachian Regional Geodetic Advisor
jeff.jalbrzikowski@noaa.gov
240-988-5486
WVSPS Annual Convention
February 2020

## Slide 2: My Background
Licensed Surveyor in OH, PA, and WV (PS)
Certified GIS Professional (GISP)
Certified Floodplain Surveyor (CFS)
BS in Surveying & Mapping, Univ. of Akron
Came to NGS from USACE Pittsburgh District
  primary experience is engineering surveys, including structural deformation, hydrographic/bathymetric, terrestrial lidar, GNSS control, local/legacy datum resolution

## Slide 3
So… NAD83 and NAVD88 are scheduled to be replaced
Who’s nervous?
Who’s ready?
Who’s already working in ITRF?

## Slide 4: Organizational Structure
  -Department of Commerce (DoC)
  (~47,000 employees)
  -National Oceanic and Atmospheric Administration (NOAA)
  -National Ocean Service (NOS)
  -National Geodetic Survey (NGS)
  (~175 employees)

## Slide 5: Organizational Structure
  -Department of Commerce (DoC)
  (~47,000 employees)
  -National Oceanic and Atmospheric Administration (NOAA)
  -National Ocean Service (NOS)
  -National Geodetic Survey (NGS)
  (~175 employees)
≠
We’re not USGS, we’re NGS

## Slide 6: NGS Mission
To define, maintain and provide access to the National Spatial Reference System (NSRS) to meet our Nation’s economic, social, and environmental needs.

## Slide 7: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach

## Slide 8: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach

## Slide 9: Continuously Operating Reference Station (CORS)
2000+ sites
~225 organizations

## Slide 10: NOAA CORS Network (NCN)
2000+ sites
~225 organizations

## Slide 11: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach

## Slide 12: National Height Modernization Program
“…the establishment of accurate, reliable heights using GNSS technology in conjunction with traditional leveling, gravity, and modern remote sensing information…”
propagation and long-term monitoring of control thru static GPS campaigns, GPS on BMs, and digital leveling
combined with gravity and lidar data

## Slide 13: National Height Modernization Program
Funded partners
States engaged in HM without Federal funding
Spatial Reference Centers
Regional Leaders
Other funded partners

## Slide 14: National Height Modernization Program
supports various Federal Programs
  FEMA: Flood Hazard Mapping Program (FIRM, etc.)
  USACE: Levee & Dam Safety Programs, etc.
  USGS: National Geospatial Program (3DEP, NHD+, etc.)
and countless non-Federal programs
still an active program but there have not been any grants in many years

## Slide 15: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach

## Slide 16: Gravity for the Redefinition of the American Vertical Datum
Two major campaigns within GRAV-D
High-resolution snapshot of gravity
  airborne observations of relative gravity
  collected in as short of a timespan as is realistic
  full coverage
Low-resolution “movie” of gravity changes
  on-the-ground observations of absolute gravity
  periodic or episodic; repeat every ___ years
  large spacing, a few per state

## Slide 17: Gravity for the Redefinition of the American Vertical Datum
As of DEC2019:
81% complete
10 km data lines
70 km cross lines
20,000 ft altitude
230 kt flight speed
Green = Complete
Blue = In Processing
Yellow = Underway
White = Planned

## Slide 18
Dynamic Aviation’s King Air 200T

## Slide 19
NOAA’s Gulfstream IV-SP

## Slide 20
in the King Air
Gravimeters in the Aircraft
in the Gulfstream IV

## Slide 21
What does a flight plan look like?

## Slide 22
What does processed data look like?
mGal
mGal = milligal

## Slide 23: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach

## Slide 24: Online Positioning User Service
  OPUS Rapid Static (OPUS-RS)
      dual frequency receiver data
      static sessions only
      30 seconds epoch rate (aka recording interval)
      15 minutes to 2 hours of GPS data
  OPUS Static (OPUS-S)
      same requirements as above
      2 to 48 hours of GPS data
  OPUS Projects (OP)
      adds session processing and network adjustment
      training by NGS required; typically 12 hours
      upload to OPUS with a “Project ID” keyed in Options

## Slide 25: a note on OPUS “my profile”
be careful!

## Slide 26: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach

## Slide 27: https://www.ngs.noaa.gov/ADVISORS/

## Slide 28: Regional Geodetic Advisor Program
www.ngs.noaa.gov/ADVISORS/
query any major search engine: “ngs advisors”

## Slide 29: State Geodetic Coordinators
Not an NGS employee, rather:
  State/Commonwealth government
    RTN manager
    DOT survey lead
    Geospatial Information Officer
  Academia
    Professor or Program Director
  Professional society representative
Serves as a liaison between the State’s geospatial community and the NGS

## Slide 30: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach

## Slide 31: Phase Center Offset - conceptual
Orange dot = mean point of signal reception
Blue dot = Antenna Reference Point (ARP)
Red line = Phase Center Offset (PCO)

## Slide 32: Phase Center Offset
The PCO is one reason it is important to select the correct antenna for OPUS upload!
choose
carefully!
if you have questions… drop me a line

## Slide 33: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach

## Slide 34: NGS Coordinate Conversion And Transformation Tool (NCAT)

## Slide 35
NGS Coordinate Conversion And Transformation Tool (NCAT)

## Slide 36: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach

## Slide 37: Calibration Base Lines - CBL
Three types of CBL defined by NGS
  Primary CBL (PCBL): in Woodford, VA at NGS TTC; it is open for use to organizations like the PLSO
  Federal CBL (FCBL): established with EDM checked at the NGS PCBL and IAW NOAA TM NGS-8
      2 in West Virginia: Marshall County Airport, Byrd L&D
  Cooperative CBL (CCBL): established with EDM checked on an FCBL and IAW that same NGS-8 manual

## Slide 38: Calibration Base Lines - CBL
https://www.ngs.noaa.gov/CBLINES/
NGS commitment to the CBL Program:
  A minimum of one FCBL per State
  Establishment procedures document
  Public access to the CBL database
  Software to process your observations
  Verification and re-measurement data review
  Technical support (Advisors or other personnel)

## Slide 39: CBL Datasheets

## Slide 40: Beta CBL Map Viewer
https://www.ngs.noaa.gov/CBLINES/

## Slide 41: NGS Overview
Modernizing the NSRS
OPUS
Orbit Data
CORS
GRAV-D
NHMP
ECO
ASP
VDatum
Geodetic Advisors
ERI
National Shoreline
NGS Products and Services
Antenna Calibrations
NCAT
CUSP
CBL
Outreach

## Slide 42: Outreach & Educational Resources

## Slide 43: NGS Mission
To define, maintain and provide access to the National Spatial Reference System (NSRS) to meet our Nation’s economic, social, and environmental needs.

## Slide 44: National Spatial Reference System (NSRS)
A consistent coordinate system that defines
latitude
longitude
height
scale
orientation
gravity
throughout the United States.
…and their time variants

## Slide 45: National Spatial Reference System (NSRS)
These items ARE part of the NSRS
Horizontal Datums (aka Geometric Reference Frames) | Vertical Datums | Great Lakes Datums | Geoid Models | Transformations and Conversions
NAD83 | NAVD88 | IGLD85 | GEOID18 | NADCON
NAD27 | NGVD29 | IGLD55 | GEOID12B | VERTCON
USSD | VIVD09 |  | GEOID09 | 
 | GUVD04 |  | GEOID06 | SPCS83
 | NMVD03 |  | GEOID03 | SPCS27
 | ASVD02 |  | GEOID99 | 
 | PRVD02 |  | GEOID96 | 
 |  |  | ALASKA94 | 
 |  |  | GEOID93 | 
 |  |  | GEOID90 | 

## Slide 46: National Spatial Reference System (NSRS)
Horizontal Datums (aka Geometric Reference Frames) | Vertical Datums | Geoid Models | Transformations and Conversions
WGS84 | IHRS (by IAG) | OSU91A | CORPSCON
WGS72 |  | EGM96 | Appendix B.6 of DMA TR 8350.2 (WGS 84)
ITRF (Intl. Terrestrial Reference Frame by IERS) |  | EGM2008 | Oregon Coordinate Reference System (ORCS)
IGS (Intl. GNSS Service reference frame) |  |  | The Kansas Regional Coordinate System
These items are NOT part of the NSRS
Hyperlink to ITRF station map

## Slide 47: NSRS … do I have to use it?
OMB Circular A-16
  requires all Federal civilian agencies to utilize geodetic control for their geospatial activities
  places NOAA in responsible charge of that control
  NGS has defined that control as the NSRS
  FGCS has issued requirements, via FRNs, to reference data to the most recent components of the NSRS
            1989 FRN designated NAD 83
            1993 FRN designated NAVD 88
Hyperlink to NAVD88 FRN
Hyperlink to NAD83 FRN

## Slide 48
NSRS … do I have to use it?
Not necessarily, but it’s a great idea!
States may mandate use (does West Virginia?)
All Federal spatial data and GIS activities financed directly or indirectly, in whole or in part, by Federal funds are required to be tied to the NSRS
If you want to get involved in survey contracting with the Federal Government it’s a necessity

## Slide 49: Not just new datums…
  NSRS Modernization
Replace NAD83
Replace NAVD88
Re-invent Bluebooking
Improve Geodetic Toolkit
Better Surveying Methods
Blueprint for 2022, Part 3
Blueprint for 2022, Part 1
Blueprint for 2022, Part 2

## Slide 50: Evolution of the NSRS
NAD27
NAD83 (1986)
NAD83 (2011)

## Slide 51: Modernized NSRS is our “smartphone”
You resisted it for a while…
It was a little cumbersome to get used to…
But soon you were hooked!

## Slide 52
Two Major Components of
Modernized NSRS
Geometric (LLh)
Latitude, Longitude, Ellipsoid Height
Geopotential (H)
Orthometric Height

## Slide 53
North American Datum
of 1983
NAD83
will be replaced by

## Slide 54
North American Terrestrial Reference Frame of 2022
NATRF2022
(pronounced: nat-ref)

## Slide 55: Reference Frame ≈ Datum
Reference Frame is a more scientifically appropriate way of saying “datum”
could be debated that “datum” was misused in NAD83(2011)
you will continue to see NGS use the phrase “New Datums” for 2022

## Slide 56: Datum Defined
The adopted standard latitude and longitude of a given station, together with the adopted standard azimuth of a line from that station.
e.g. Meade’s Ranch and it’s azimuth mark, Waldo
Source: Proceedings of the 14th General Conference of the International Geodetic Association (IAG) - ”Report on Geodetic Operations in the United States”, O.H. Tittmann, Superintendent of the USC&GS

## Slide 57: Reference Frame Defined
A point of view or a ‘frame of reference’.
If your reference frame is North America, you are standing somewhere within North America, seeing how other places move from your point of view.

## Slide 58: Why replace NAD83?
Main driver: Global Navigation Satellite System (GNSS)
ACCESS
  GNSS equipment is fast, inexpensive, reliable
  Reduces reliance on physical control marks
ACCURACY
  Insensitive to distance-dependent errors
  Immune to instability; active control via CORS
CONSISTENCY
Eliminates systematic errors in current datums
Aligned with global reference frame

## Slide 59: A very brief history of U.S. horizontal & geometric datums
US Standard Datum
time
+
shift
<10 m
tens of meters
few 0.1m
few 0.01m
few 0.01m
triangulation
GNSS
+
+
+
+
+
~2m
NATRF2022
NAD83(2011)
NAD83(2007)
NAD83(HARN/199#)
NAD83(1986)
NAD27
NAD83(HARN/199#)
+

## Slide 61: Replacing NAD83
develop four "plate-fixed" reference frames
remove non-geocentricity of NAD83
align to ITRF2014 at epoch 2020.00
remove most of tectonic plate rotation from ITRF2014 via Euler Pole Parameters
Shift and Drift…

## Slide 62: Replacing NAD83
develop four "plate-fixed" reference frames
remove non-geocentricity of NAD83
align to ITRF2014 at epoch 2020.00
remove most of tectonic plate rotation from ITRF2014 via Euler Pole Parameters
Shift and Drift…

## Slide 63: Four “Plate-Fixed” Reference Frames
North American Terrestrial Reference Frame of 2022
(NATRF2022)
Pacific Terrestrial Reference Frame of 2022
(PATRF2022)
Caribbean Terrestrial Reference Frame of 2022
(CATRF2022)
Mariana Terrestrial Reference Frame of 2022
(MATRF2022)

## Slide 65: Four “Plate-Fixed” Reference Frames
North American Terrestrial Reference Frame of 2022
(NATRF2022)
Pacific Terrestrial Reference Frame of 2022
(PATRF2022)
Caribbean Terrestrial Reference Frame of 2022
(CATRF2022)
Mariana Terrestrial Reference Frame of 2022
(MATRF2022)

## Slide 66: Replacing NAD83
develop four "plate-fixed" reference frames
remove non-geocentricity of NAD83
align to ITRF2014 at epoch 2020.00
remove most of tectonic plate rotation from ITRF2014 via Euler Pole Parameters
Shift and Drift…

## Slide 67
Geocentric:
  relating to, measured from, or as if observed from the earth's center of mass
Non-geocentricity?
The goal was to accomplish that… but didn’t.

## Slide 68: Non-geocentricity of NAD83
GRS80 ellipsoid
ITRF2014
NAD83
GRS = Geodetic Reference System

## Slide 69: Non-geocentricity of NAD83
ITRF2014
NAD83
GRS80 ellipsoid

## Slide 70: Non-geocentricity of NAD83
~2.2 meters
NAD83
origin
ITRF2014
origin
Earth’s
Surface
h83
h14
GRS80
ellipsoid

## Slide 71: Non-geocentricity of NAD83
Earth’s
Surface
GRS80
ellipsoid
NAD83
ITRF2014
NATRF2022
h22
Shift…

## Slide 72: Geometric change due to ellipsoid non-geocentricity
Horizontal (Lat, Lon)
Ellipsoidal (h)
Shift…

## Slide 73: Replacing NAD83
develop four "plate-fixed" reference frames
remove non-geocentricity of NAD83
align to ITRF2014 at epoch 2020.00
remove most of tectonic plate rotation from ITRF2014 via Euler Pole Parameters
Shift and Drift…

## Slide 74
International Terrestrial Reference Frame
(ITRF)
International Earth Rotation and Reference Systems Service (IERS)
International Union of Geodesy and Geophysics (IUGG)

## Slide 75: International Terrestrial Reference Frame
The stable coordinate system that allows us to measure change over space, time and evolving technologies.
An accurate, stable set of station positions and velocities.
Network measurements interconnected by co-location of different space geodetic techniques.
“Approximately represents the motions of the tectonic plates with respect to the Earth's deep interior”… huh?

## Slide 76
Watch the grid!
ITRF concept
Drift…

## Slide 77
eh-puck? ee-pock? … to-may-to, to-mah-to
  an instant of time or a date selected as a point of reference
Epoch?

## Slide 78: Replacing NAD83
develop four "plate-fixed" reference frames
remove non-geocentricity of NAD83
align to ITRF2014 at epoch 2020.00
remove most of tectonic plate rotation from ITRF2014 via Euler Pole Parameters
(pronounced: “oiler”)
Shift and Drift…

## Slide 79: The wrong question, circa 2022:
“What’s the position of that point?”
The right question, circa 2022:
“What’s the position of that point, on some specific date?”
Drift…

## Slide 80: Two types of drift
Tectonic Plate Rotation
    horizontal
Everything Else
    residual motions left after rotation
    regional linear motions
    localized subsidence or uplift
simple to model
complex

## Slide 81
Tectonic Plate Rotation
    horizontal
simple to model

## Slide 82
Euler Pole Parameters
of 2022
EPP2022

## Slide 83: Plate Rotation visualized
Drift…

## Slide 84: Euler Poles and “Plate-Fixed”
  In the ITRF, many tectonic plates have a dominant motion: rotation
  Euler Pole - point about which a plate rotates (yellow star)
NATRF2022 Euler Pole

## Slide 85: Euler Poles and “Plate-Fixed”
ITRF
Frame = constant
NA Plate = rotating
NATRF
Frame = rotating
NA Plate = constant

## Slide 86: Euler Poles and “Plate-Fixed”
ITRF
Frame = constant
NA Plate = rotating
NATRF
Frame = rotating
(relative to ITRF)
NA Plate = constant
(relative to NATRF2022)

## Slide 87
ITRF – constant frame, rotating plate

## Slide 88: “Plate-Fixed”
NATRF – rotating frame, constant with plate

## Slide 89
ITRF or NATRF – your choice, just use EPP

## Slide 90: EPP – Euler Pole Parameters
Latitude
Longitude
Rotation Speed
yellow star off west coast of S. America

## Slide 91: CORS Velocities in ITRF2014
Drift…

## Slide 92
CORS Velocities in NATRF2022
Think of this map as ITRF2014 + EPP2022
Still SomeDrift…

## Slide 93
NATRF2022
CATRF2022
PATRF2022
MATRF2022
Rotation of the
North American Plate
Rotation of the
Caribbean Plate
Rotation of the
Pacific Plate
Rotation of the
Mariana Plate
ITRF2014
EPP2022
ITRF2014 + EPP2022 = --TRF2022

## Slide 94
Rotation of the
North American Plate
ITRF2014
EPP2022
ITRF2014 + EPP2022 = --TRF2022
NATRF2022

## Slide 95: Two types of drift
Tectonic Plate Rotation
    horizontal
Everything Else
    residual motions left after rotation
    regional linear motions
    localized subsidence or uplift
simple to model
complex

## Slide 96
Everything Else
    residual motions left after rotation
    regional linear motions
    localized subsidence or uplift
complex
Still SomeDrift…

## Slide 97
Intra-Frame Velocity Model of 2022
IFVM2022

## Slide 98
Longitude (Easting) History of DI4044
BLUE IS ITRF COORDINATE
RED IS NATRF2022
COORDINATE
Trend: -14.3 mm / year
Trend: -1.7 mm / year
2004 2006 2008 2010 2012 2014 2016 2018
Still Some Drift…
Concept of goal of IFVM

## Slide 99
CORS Velocities in NATRF2022
Think of this map as ITRF2014 + EPP2022
Still SomeDrift…

## Slide 100
IFVM goal = model all velocities
Think of this map as ITRF2014 + EPP2022 + IFVM2022

## Slide 101: Still Some Drift…
  Everything in the world moves
  Coordinates will be associated with the actual date when the data was collected!
  Velocities at all marks can be estimated using this Intra-Frame Velocity Model
  IFVM goal being to move collected data thru time to Reference Epochs for coordinate comparisons/analysis

## Slide 102
A model of all residual velocities, after removal of tectonic rotation via EPP:
  Horizontal residual motion
  Total vertical motion (ellipsoid heights)
  Replaces / Improves upon HTDP
Given t1 and t2, compute Δλ, Δϕ, Δh at any point, accounting for all motions
Likely be built upon CORS data, geodynamic models and InSAR, but not yet finalized
Intra-Frame Velocity Model

## Slide 103
EPP2022 – Euler Pole Parameters – Simple Rotation
  Three parameters: lat, lon, rotation speed
  Horizontal only: just latitude and longitude
  Changes the frame: ITRF2014 + EPP2022 = NATRF2022
  Does not change the epoch
IFVM2022 – Intra-Frame Velocity Model - Complex
  Complex set of parameters
  Residual horizontal motion: all the motion leftover after Euler Pole rotation
  All vertical motion: localized subsidence or uplift
  Changes the epoch
  Does not change the frame: “intra” = on the inside; within

## Slide 104: EPP2022 IFVM2022
They work together to account for the Drift…
Two new tools that will make time dependent geodetic control practical

## Slide 105: Example of application of EPP and IFVM
It’s 2039 and you are working in San Diego using NATRF2022
And you want to compare your work to another survey from 2028
Important: This slide only covers geometric coordinates.
NATRF2022
ep. 2028.048
PATRF2022
ep. 2028.048
ITRF2014
ep. 2028.048
NATRF2022
ep. 2039.704
ITRF2014
ep. 2039.704
PATRF2022
ep. 2039.704
EPP2022
(PA)
EPP2022
(NA)
EPP2022
(NA)
EPP2022
(PA)
IFVM2022
(PA)
IFVM2022
(NA)
…the catch is, that survey was done in PATRF2022

## Slide 106: Alright Jeff... enough jibba-jabba, what’s the impact?

## Slide 108
What’s that going to look like?
PHOTO = NAD83
RED = NAD83 shoreline data
GREEN = shoreline transformed to NATRF2022

## Slide 109: If you’re only working in this region…
North American Terrestrial Reference Frame of 2022
(NATRF2022)

## Slide 110
Two Major Components of
Modernized NSRS
Geometric (LLh)
Latitude, Longitude, Ellipsoid Height
Geopotential (H)
Orthometric Height

## Slide 111
North American Vertical Datum
of 1988
NAVD88
will be replaced by

## Slide 112
North American-Pacific Geopotential Datum of 2022
NAPGD2022
(pronounced: nap-jee-dee)

## Slide 113
A brief history of (the most prevalent) U.S. vertical datums

## Slide 114
NGVD29
Referenced to 26 tide gauges in the US and Canada

## Slide 115: NGVD29 – based on 26 tide gauges
Concept

## Slide 116
Referenced to a single tide gauge in Canada
Father Point Lighthouse, Quebec
Why one gage fixed this time?
removed local sea level variation problem of NGVD29
But it did introduce possibility of cross-continent error build-up…

## Slide 117: NAVD88 – based on single tide gauge
Concept

## Slide 118
Approximate Error in NAVD88 "zero elevation” (H=0)
Map is the H=0 surface overlaid onto satellite gravity data

## Slide 119: Why Replace NAVD88?
tilt in the "zero surface” (intended to be flat)
subsidence, uplift, freeze & thaw of BMs
limited availability of undisturbed marks
Approximate Error in NAVD88 "zero surface”

## Slide 120: Passive marks may lie still… but they still may lie! (small instability x long time = large inaccuracy)

## Slide 121: Replacing NAVD88
primary access via GNSS and geoid (think OPUS)
accurate continental gravimetric geoid (1-2 cm)
aligned with:
  NATRF2022 (or CATRF, PATRF, MATRF)
  global mean sea level (GMSL)
monitor time-varying nature of gravity (NGS Geoid Monitoring Service GeMS)

## Slide 122
  Gravimetric
  Hybrid
Two types of geoid models…

## Slide 123
  Gravimetric geoid is created from “scratch” with various types of gravity data
      USGG2003, USGG2009, USGG2012, xGEOID19
  Hybrid geoid is simply a gravimetric geoid warped to fit some vertical datum… like NAVD88
      GEOID03, GEOID09, GEOID12B, GEOID18
Gravimetric  Hybrid

## Slide 124
      USGG2003, USGG2009, USGG2012, xGEOID19
      GEOID03, GEOID09, GEOID12B, GEOID18
Gravimetric  Hybrid
best fit to NAVD88
best fit to NAVD88
best fit to NAVD88
best fit to NAVD88

## Slide 126: Calculating Ng is not easy!
First you need a gravity field
  data collected from different distances away from Earth
Next calculate gravity anomaly, or ∆g
Then, just solve Stokes’ integral!
R is the mean radius of the earth
ɣ0 is mean surface gravity on ellipsoid
S is a geometric function of position
…there’s a catch
Need to know ∆g over entire surface of the earth

## Slide 127: Calculating Ng is not easy!
First you need a gravity field
  data collected from different distances away from Earth
Next calculate gravity anomaly, or ∆g
Then, just solve Stokes’ integral!
R is the mean radius of the earth
ɣ0 is mean surface gravity on ellipsoid
S is a geometric function of position
…there’s a catch
Need to know ∆g over entire surface of the earth

## Slide 128: Building a Gravity Field Model
Airborne Observations
Terrestrial/Surface Observations and Predicted Gravity from Topography
Short Wavelengths (< 100 km)
+
Long Wavelengths (> 250 km)
GRACE/GOCE/Satellite Altimetry
Intermediate Wavelengths (20km to 300 km)
+

## Slide 129: GRACE - 2 Satellites measuring separation

## Slide 130: GRAV-D – airborne relative gravimeters

## Slide 131: Terrestrial Gravimeter - Relative

## Slide 132: Terrestrial Gravimeter - Relative

## Slide 133: Terrestrial Gravimeter - Absolute

## Slide 134: Terrestrial Gravimeters - Absolute and Relative

## Slide 135: Individual Components of NAPGD2022
Global Model of the geopotential field
  GM2022
Geoid undulation models by region
  GEOID2022 aka “0 elevation”
Deflection of the Vertical (DoV) models by region
  DEFLEC2022
Surface Gravity models by region
  GRAV2022

## Slide 137: Sea Level Change and the Geoid

## Slide 138: Sea Level Change and the Geoid

## Slide 139: Sea Level Change and the Geoid

## Slide 140
Estimated change in orthometric heights from NAVD88 to NAPGD2022
(NAPGD2022 approximated using xGEOID16B)

## Slide 141
(NAPGD2022 approximated using xGEOID16B)
Estimated change in orthometric heights from NAVD88 to NAPGD2022
Vertical change of about -0.6 to -2.0 feet

## Slide 142
North American-Pacific Geopotential Datum of 2022
(NAPGD2022)

## Slide 143: How can I prepare? Where did this all start? What’s the benefit to me? How is all this possible?
Well, besides learning a whole new set of terminology and methods…

## Slide 144: How can surveyors prepare?
Get familiar with terms, ask now, be ready
Set/occupy RTN Validation Stations (OPUS)
Research your published control
    pre-1995 will NOT get new coordinates (GPS only)
Use OPUS Projects to re-observe/process

## Slide 145: What’s the benefit?
  Reduce all definitional & access-related errors in geometric reference frame to 1 cm when using 15 min of GNSS data
  aka “Replace NAD83”
  Reduce all definitional & access-related errors in orthometric heights in geopotential datum to
  2 cm when using 15 min of GNSS data
  aka “Replace NAVD88”
https://geodesy.noaa.gov/web/about_ngs/info/tenyearfinal.shtml

## Slide 146: How is all this possible?
CORS
Co-location of space geodetic instruments worldwide that feed into ITRF development
Teamwork with other geodetic organizations
Research and Development
Testing
Science, dude!

## Slide 147: Co-location Site NASA Goddard Space Flight Center, Greenbelt MD, USA
  GNSS, SLR, VLBI, DORIS

## Slide 148: Co-location Site NASA Goddard Space Flight Center, Greenbelt MD, USA
  GNSS, SLR, VLBI, DORIS

## Slide 149: Co-location Site NASA Goddard Space Flight Center, Greenbelt MD, USA
  GNSS, SLR, VLBI, DORIS

## Slide 150: SLR
Satellite Laser Ranging

## Slide 152: Co-location Site NASA Goddard Space Flight Center, Greenbelt MD, USA
  GNSS, SLR, VLBI, DORIS

## Slide 153: VLBI
Very Long Baseline Interferometry

## Slide 154
VLBI

## Slide 155
VLBI

## Slide 156: Co-location Site NASA Goddard Space Flight Center, Greenbelt MD, USA
  GNSS, SLR, VLBI, DORIS

## Slide 157: DORIS
Doppler Orbitography and Radiopositioning Integrated by Satellite

## Slide 158
Doppler Orbitography and Radiopositioning Integrated by Satellite

## Slide 159: Space Geodesy Co-location Diagram
Generic concept of “co-location survey”, typically more complex.

## Slide 160: Altogether now!
All these techniques work together to create a well-defined, robust reference frame that improves positioning for users globally.

## Slide 161: Not just new datums…
  NSRS Modernization
-OPUS enhancements/additions
-new types of coordinates
-new methods for establishing control
-streamlined Bluebooking
-retire the US Survey Foot

## Slide 162: Blueprint for 2022, Part 3

## Slide 163: Let’s look at some new terminology

## Slide 164: NOAA CORS Network (NCN)
As of 2019, this is the official name of the national network of CORS whose data are managed by NGS
  Historically referred to as “CORS” or “the CORS”
Remember, not all CORS are in the NCN
  For example: the WVDOH CORS Network, not all of those Stations are in the NCN
CORS = Continuously Operating Reference Station

## Slide 165: NOAA CORS Network (NCN)

## Slide 166: WVDOH CORS Network

## Slide 167: GPS Month
A span of four consecutive GPS weeks, where the first GPS week in the GPS month is an integer multiple of 4
  GPS Month 0 = GPS Weeks 0, 1, 2 and 3
  GPS Month 1 = GPS Weeks 4, 5, 6 and 7
  GPS Month 2 = GPS Weeks 8, 9, 10, and 11
  GPS Month 3 = GPS Weeks 12, 13, 14, and 15
  You get the idea…

## Slide 168: New Types of Coordinates

## Slide 169: Five types of coordinates in Modernized NSRS
Name | Generally on… | Description
Reported | Passive | “Quick and Dirty”. Smartphone accuracy.
Preliminary | Passive | Computed by you with OPUS using your data. Unchecked by NGS.
Final Discrete | Passive | Most accurate. Time-dependent. Computed by NGS every four weeks.
Final Running | CORS | Continuous time-dependent CORS coordinates. Checked by NGS every day.
Reference Epoch | Passive and CORS | Modeled from Final Discrete, Final Running, IFVM2022 and GeMS. Computed by NGS every five years.

## Slide 170: Reported Coordinates
  These are from any source in which the coordinate is directly reported to NGS without the data necessary for NGS to replicate the coordinate.
  Compares to:
    SCALED – like on a datasheet
    HD_HELD – like on a datasheet
    Smartphone/Device GNSS
    From NCAT or VDatum
    Coordinates from and RTK/RTN rover without data files

## Slide 171: Reported Coordinates

## Slide 172: Preliminary Coordinates
  These are coordinates at survey epoch that have been computed from OPUS, but not yet quality checked and loaded into the National Spatial Reference System Database (NSRS DB).
  Compares to:
    OPUS Solution Report – NGS does not QC these
    OPUS-Projects results – only QC’d if submitted
  Note:
    These are the only coordinates a user will get directly from OPUS

## Slide 173: Final Discrete Coordinates
  These are coordinates computed by NGS using submitted data and metadata, checked, adjusted, and referenced to a single survey epoch for loading into the NSRS DB.
    Represent the best estimate of the time-dependent coordinates at any given mark
  What will the Survey Epochs be?
    GNSS: GPS Month
      Stand-alone occupations, RTK/RTN, Campaigns, etc.
    Leveling: Calendar Year; Annually
      Will be adjusted to GNSS-based orthometric heights

## Slide 174: Final Running Coordinates
  These are the only type which will have a published coordinate at any epoch.
    Generally will only be available at CORSs
    Will be generated by a “fit” to daily processed data
    Another new term!
      We’ll refer to these as the Coordinate Function

## Slide 175: Daily Epochs?!?
It seems unlikely that the majority of surveyors will embrace these (e.g. 2028.048, 2039.074 from last slide)
To mitigate that, NGS will issue “snapshots” of the NSRS every five years
  We’re calling these Reference Epochs
  These will be estimates of coordinates at specific 5 year intervals - based on historic coordinates and the IFVM2022
Beginning with 2020.00
  Each “snapshot” will be published 2-3 years after the reference epoch, so the 2020.00 Reference Epoch Coordinates get published by the end of calendar year 2022… thus the name/date of 2022

## Slide 176: Reference Epoch Coordinates
  These are coordinates which have been estimated by NGS based on time-dependent (final discrete and final running) coordinates, at an Official NSRS Reference Epoch (ONRE).
  Compares to:
    NAD 83(2011) epoch 2010.00 on a Datasheet
  When will NGS compute these?
    Every 5 years, on a timeline of 2-3 years post-date
    2020.00 coordinates will be computed in 2022
    2025.00 coordinates will be computed in 2027

## Slide 177: Let’s visualize some of these new things.

## Slide 178
1990
2.000
2.050
2.100
2.150
2.200
2.250
h
time
Assume “h” was determined four different times:
1990: 2.100
1994: 2.110
2002: 2.190
2009: 2.180
‘95
‘00
‘05
‘10
‘15
‘20
‘25
‘30

## Slide 179
1990
2.000
2.050
2.100
2.150
2.200
2.250
‘95
‘00
‘05
‘10
‘15
‘20
‘25
‘30
In today’s NSRS, a height is held fixed until replaced. So plotting the height of these coordinates as seen on an NGS Datasheet over time would look like this:
h
time

## Slide 180
1990
2.000
2.050
2.100
2.150
2.200
2.250
‘95
‘00
‘05
‘10
‘15
‘20
‘25
‘30
In the Modernized NSRS these time-dependent
coordinates, estimated at the actual date when
the surveys took place, will be called
Final Discrete Coordinates
All measurements have error. Shown here are the same
Values of “h”, but with their error estimates.
1990: 2.100 +/- 0.0375 (3.75 cm)
1994: 2.110 +/- 0.0250 (2.50 cm)
2002: 2.190 +/- 0.0200 (2.00 cm)
2009: 2.180 +/- 0.0250 (2.50 cm)
h
time

## Slide 181
1990
2.000
2.050
2.100
2.150
2.200
2.250
‘95
‘00
‘05
‘10
‘15
‘20
‘25
‘30
In the Modernized NSRS we will also have an estimate of
crustal motion from IFVM2022
Combining Final Discrete Coordinates
with IFVM2022 allows NGS to estimate Reference Epoch Coordinates
h
time
The IFVM2022 will (statistically)
align to these Reference Epoch Coordinates.

## Slide 182
1990
2.000
2.050
2.100
2.150
2.200
2.250
‘95
‘00
‘05
‘10
‘15
‘20
‘25
‘30
In the absence of new survey data, error estimates will
grow through time.
h
time

## Slide 183
1990
2.000
2.050
2.100
2.150
2.200
2.250
‘95
‘00
‘05
‘10
‘15
‘20
‘25
‘30
The (in)ability of current approach to
properly inform users of the height of
this mark can be seen in blue.

## Slide 184
State Plane Coordinate System of 2022
SPCS2022

## Slide 185
Bumper Stickers I’ll be selling in Booth #22 tomorrow afternoon 

## Slide 186: SPCS2022 stakeholders
State groups that formally interface with NGS
  Departments of transportation
  Cartographer/GIS office
  Professional surveying, engineering, GIS societies
  Colleges/universities with geospatial curriculum
Can submit requests and proposals for designs
  Requests are for designs by NGS
  Proposals are designs by stakeholders
Stakeholder input must be unanimous

## Slide 187: General SPCS2022 characteristics
Distortion design requirements
  Linear distortion minimized at topographic surface (not at ellipsoid surface)
  Purpose: to reduce difference between projected “grid” and actual “ground” distances
Other characteristics
  Default designs (if no consensus stakeholder input)
  Statewide and “layered” zones
  Positive east longitudes
  Low-distortion projections (LDPs)
  “Special use” zones

## Slide 188: Linear distortion with respect to ellipsoid
Grid distance > ellipsoid distance
Projection axis
Grid distance < ellipsoid distance
Ellipsoid distance
Ellipsoid distance
Projection surface (secant)
This design approach used for SPCS 27 and 83 (minimizes distortion with respect to ellipsoid)
Ellipsoid surface

## Slide 189: Changing projection axis to reduce distortion variation
Projection axis
Ellipsoid surface
h2
h1
Grid distance = ground distance at many points
Only way to reduce variation in distortion is to change projection axis location.
IMPORTANT: For large areas, there is no single defining ellipsoid height, h, for scaling the projection.
Ellipsoid height of surface not constant:
h1 ≠ h2
Topographic surface
This design approach is being used for SPCS2022 (minimizes distortion with respect to topography)

## Slide 190: “Non-intersecting” conformal map projection
Projection axis
Non-intersecting
Ellipsoid surface
Purpose is to reduce linear distortion at “ground” (topographic surface).
But distortion can vary considerably across area of interest.
Grid distance = ground distance at a point
Grid distance ≈ ground distance over finite distance
Topographic surface
Grid distance = ground distance at a point

## Slide 191: Default SPCS2022 zones
To ensure all states and U.S. territories covered
  For complete system if no consensus stakeholder input
  Nearly same as SPCS83 but with some changes
  Almost all zone projection types and extents the same
Modify existing zones to meet SPCS2022 policy
  Scale redefined with respect to topographic surface
  Minor changes to parameters to meet requirements
NGS will create a statewide zone for all states

## Slide 192: Zone “layers” and LDPs
Each state may have max of THREE zone “layers”
  One layer must be statewide zone (designed by NGS)
  Other layers have two or more zones (“multi-zone”)
  Only one layer can have discontinuous coverage
Multi-zone layer can consist of LDPs
  Designed by stakeholder “contributing partners”
  Minimum zone width 50 km (if height range < 250 m)
OR 10 km (if height range > 250 m)
  LDP coverage can be discontinuous

## Slide 193: Alaska statewide “base” layer
1. Statewide layer
Alaska zone layers

## Slide 194: Alaska complete “intermediate” layer
194
1. Statewide layer
2. “Intermediate” layer (complete state coverage)
Alaska zone layers

## Slide 195: Alaska with THREE SPCS2022 layers
195
1. Statewide layer
2. “Intermediate” layer (complete state coverage)
3. LDP layer (partial state coverage)
Alaska zone layers

## Slide 196: SPCS2022 deadlines
Consensus input per SPCS2022 procedures
  Requests for designs done by NGS
  Proposals for designs by contributing partners
Submittal of approved designs
  Proposal must first be approved by NGS
  Designs must be complete for NGS to review
Later requests will be for changes to SPCS2022
by March 31, 2020 for requests and proposals
by March 31, 2021 for submittal of approved designs

## Slide 197: SPCS2022 in West Virginia
We have received no requests from WV
Regardless, NGS will design a single statewide Zone that covers the entire State
  This will enable State agencies, etc., to maintain all GIS data within one zone
Is there a need for the two North and South Zones?
If the performance of the single zone is better than the existing N-S Zones… why have both?

## Slide 198
US Survey Foot
and
International Foot
…or Feets Don’t Fail Me Now

## Slide 199: The problem
Two versions of same unit in current use
  “New” international foot and “old” U.S. survey foot
  “New” shorter than “old” by 2 ppm (0.01 ft per mile)
  A real problem with real costs
What’s in a name?
  “U.S. survey” versus “international”
Who is using U.S. survey feet?
  Surveyors exclusively, in most (not all) states
  But it impacts everyone

## Slide 200
1,000,000.00 sft = 999,998.00 ift
10,000,000.00 sft = 9,999,980.00 ift
International  1 ft = .3048 m
US  1 ft = .30480061 m (approx.)
  frequently calculated by
2 parts per million (ppm)

## Slide 201
When does this matter?
  Not typically in lengths/distances
  But in published planar coordinate systems
Like what?
  SPCS and UTM are very popular and both fall victim to mix-ups
Why?
  Large false eastings and northings
What’s impacted?

## Slide 202
Who is responsible for standards?
National Institute of Standards and Technology

## Slide 203: Adopted International Foot in 1959
National Bureau of Standards created
1901
1959
1933
1952
New foot definition adopted by ANSI predecessor
New foot definition adopted by NASA predecessor
1954
International nautical mile
Adopted as “new” foot for entire U.S.
1,852 m exact
With one little exception…
1 foot = 0.3048 meter exactly (1 yard = 0.9144 m)

## Slide 204: With one little exception…
“Any data expressed in feet derived from and published as a result of geodetic surveys within the United States will continue to bear the following relationship as defined in 1893: 1 foot = 1200/3937 meter
The foot unit defined by this equation shall be referred to as the U.S. Survey Foot and it shall continue to be used, for the purpose given herein, until such a time as it becomes desirable and expedient to readjust the basic geodetic survey networks in the United States, after which the ratio of a yard, equal to 0.9144 meter, shall apply.”

## Slide 205: More Federal Register Notices
International vs. U.S. Survey Foot
1975
1990
1977
1988
NGS goes entirely metric (for NAD 83)
Proposed permanent use of U.S. Survey Foot
1989
NAD 83 announced
Restatement that metric used for U.S.
Surveying and mapping only (pending analysis, never resolved)
We readjusted the basic geodetic network!
International foot used for “engineering”
U.S. survey foot used for “mapping and land measurement”

## Slide 206
Out of order, chaos
A foot still in limbo
2008 - NIST “Guide to the Use of the SI”
U.S. survey foot still used
  but never officially permanently adopted
Repeats 1975 FRN ideas about the two feet:
  International ft used for engineering
  U.S. ft used for surveying & mapping
At odds with very idea of “standards”

## Slide 207: Oops!
Problem created and perpetuated by NGS
In 1959. Then in 1986. And again in 2016…

## Slide 208: What are the choices?
Do nothing (i.e., NGS stays “metric” only)
  States choose whatever foot they want
  Both feet will creep back into NGS products & services
Officially adopt U.S. survey foot for specific things
  U.S. survey foot for surveying and mapping
  International foot for engineering (and everything else)
Use international foot for everything
  Support only foot = 0.3048 meter after 2022
Use U.S. survey foot for everything (highly unlikely)
Go entirely metric (ideal situation, but also unlikely)

## Slide 209: NGS proposal
Only one foot after 2022 (1 foot = 0.3048 meter)
  Make official through NIST
  NO option for U.S. survey foot in NATRF/SPCS2022
NGS will help with the transition
  Will fully support backward compatibility
  Use “correct” foot for SPCS83 and SPCS27
  Automatically done by NGS products and services
Guiding ideas
  Of all changes in 2022, this is the least significant
  About the future, not the past

## Slide 210: Putting our best “foot” forward…
NGS created problem, will help fix it
  Fully support backward compatibility (NAD83, NAD27)
  Unit change minor compared to other 2022 changes
  Contact us at NGS.Feedback@noaa.gov
Federal Register Notice – 17 October 2019
  Deprecate US Survey Foot on 31 December 2022
  After, use International conversion (1 ft = 0.3048 m)
  Drop “International” refer to unit simply as “foot”
  Comment period open thru 02 December 2019
  Follow-up webinar was 12 December - recorded

## Slide 211: Using the modernized NSRS
OPUS
  Guidance (such as pre-selected CORSs and assistance in locating marks in project areas)
  Users will decide what control to hold fixed and what epochs they wish to set for the adjustment
    “Preliminary coordinates”
  If submitted to NGS (aka “Shared”), we will harvest your raw GNSS data and use it to compute Final Discrete coordinates

## Slide 212: Using the modernized NSRS
GNSS is the only entry for now
Leveling and Total Station surveys will need some GNSS if you wish to submit your survey to NGS for inclusion in the NSRS database
    Some GNSS is fine; e.g. RTK or RTN
    No decision yet on whether OPUS Projects will operate if with no GNSS in a project

## Slide 213: So much more to NSRS Modernization!
New version of PAGES
  Multi-Constellation  GPS, Galileo, GLONASS, Beidou, etc.
  Target: 15 minute occupations
OPUS expansion plan
  RTK/RTN: 2020 rollout, see demo tomorrow
  Leveling, Classical (Total Station), Gravity: 2020-2025
  Ease of submission to NGS for inclusion in the NSRS
New Mark Recovery Tool
  current draft version in Beta
Fully integrate conversions and transformations
  NCAT and VDatum

## Slide 214: What new tools are already live?
VERTCON 3.0 – functionality now in NCAT
Mark Recovery – mobile browser compatible
VDatum 4.0.1 – released in October
GEOID18 – latest, greatest, and last hybrid
GPSonBM – updated tracking map (AGOL)
    for NAVD88NAPGD2022 transformation

## Slide 215: Mark Recovery – mobile browser compatible
use your smartphone to submit recovery
Any major search engine:
  “NGS survey mark recovery”
beta.ngs.noaa.gov/cgi-bin/recvy_entry_www.prl
Try it out! Give us feedback!
NGS.Feedback@noaa.gov

## Slide 216: Mark Recovery – mobile browser compatible

## Slide 217
https://www.ngs.noaa.gov/ADVISORS/
-use any major search engine: “NGS advisors”
Jeff Jalbrzikowski, P.S., GISP, CFS
Appalachian Regional Geodetic Advisor
jeff.jalbrzikowski@noaa.gov
240-988-5486