## Slide 1
Modernizing the National Spatial Reference System: Contextual Background
Dru Smith
NSRS Modernization Manager
NOAA’s National Geodetic Survey

## Slide 2: Outline
NGS mission
NGS and the NSRS – legal context
So what is and is not the NSRS?
Accuracy
Notes: This is a listing of the parts of subject matters to be covered. Cut out entire chapters if they are unimportant to your audience.
Updated October 2010.

## Slide 3: NGS mission
To define, maintain, and provide access to the National Spatial Reference System to meet our nation’s economic, social, and environmental needs
Notes: Our mission statement is widely available on various NGS web pages. But how did we get here?

## Slide 4: NGS and the NSRS – legal context
OMB A-16:
  Requires all federal civilian geospatial agencies to use geodetic control
  Puts DOC/NOAA (=NGS) in charge of that control
  NGS has defined that control as the NSRS
  FGCS has issued requirements via FRNs to use the most recent components of the NSRS
    1989: NAD 83
    1993: NAVD 88
    2009: ASVD02, NMVD03, GUVD04
    2011: VIVD09
    2012: PRVD02

## Slide 5: NGS and the NSRS – legal context
FGCS requirements do not apply to:
  Military/Intelligence federal agencies
  State and local governments
  Private individuals and companies
But these groups often do adopt all or part of the NSRS to be compatible with most federal geospatial data
  Could lead to mixing NSRS and non-NSRS information.
    Fine, but has to be done right.

## Slide 6: So what is and is not the NSRS?
If NGS (or its predecessors*) did not make it, it is not in the NSRS**
* Survey of the Coast (1807-1836)
Coast Survey (1836-1878)
Coast and Geodetic Survey (1878-1970)
** The term “NSRS” was adopted in 1994, but today is used to encompasses all historic datums of NGS and its predecessors, though the FGCS regularly adopts the latest components

## Slide 7: These are part of the NSRS
Hor Datums / Geometric Reference Frames | Vertical Datums | Great Lakes Datums | Geoid Models | Transformations / Conversions
USSD | NGVD 29 | IGLD55 | GEOID90 | NADCON
NAD 27 | NAVD 88 | IGLD85 | GEOID93 | VERTCON
NAD 83 | PRVD02 |  | ALASKA94 | 
 | ASVD02 |  | GEOID96 | SPCS 27
 | NMVD03 |  | GEOID99 | SPCS 83
 | GUVD04 |  | GEOID03 | 
 | VIVD09 |  | GEOID06 | 
 |  |  | GEOID09 | 
 |  |  | GEOID12(A,B) | 
These are select entries, not a complete list

## Slide 8: These are not part of the NSRS
Hor Datums / Geometric Reference Frames | Vertical Datums | Great Lakes Datums | Geoid Models | Transformations / Conversions
WGS 84 | IHRS |  | OSU91A | CORPSCON
ITRF |  |  | EGM96 | Appendix B.6 of DMA TR 8350.2 (WGS 84)
IGS |  |  | EGM2008 | Oregon Coordinate Reference System
 |  |  |  | The Kansas Regional Coordinate System
These are select entries, not a complete list

## Slide 9: Mixing NSRS and non-NSRS?
Just do it right
Right:
  The Oregon CRS has a mathematically defined relationship to the NSRS
Wrong:
  “WGS 84 is the same as NAD 83”
  “WGS 84 is the same as the ITRF”
    Such statements gloss over critical facts about history, accuracy and application

## Slide 10: Accuracy
Consider your users’ accuracy needs
  3 Meters?
    Then WGS 84 is NAD 83
    Global 14 parameter transformations will suffice
  3 Decimeters?
    Then NAD 83(2011) is NAD 83(NSRS2007)
      But NAD 83(1986) is not the same as NAD 83(HARN)
    NADCON will suffice as a transformation
  3 Centimeters?
    Every detail matters

## Slide 11: Thank you

## Slide 12: Questions?

## Slide 13: Extra Slides

## Slide 14: Accuracy
The NSRS foundation is the ITRF
  And, subsequently, the IGS frame
    Doesn’t make either frame part of the NSRS
    But does:
      Give us access to the global standards in coordinate and orbit accuracy
      Give us a reason to support and contribute to both frames

## Slide 15
ITRF (station coordinates)
SLR
GNSS
DORIS
VLBI
IGS frame (station coordinates and GNSS orbits)
NAD 83 (CORS and passive coordinates)
Transformations
OPUS (diff. GPS posn)
Cm-accuracy surveys in the NSRS
NGA “Fits” WGS-84 GPS orbits to IGS GPS orbits
Cm-accuracy WGS-84 orbits (@ NGA)
MCS predicts GPS orbits & uploads for broadcast
5+ meter broadcast GPS positioning in WGS-84
How to access and use?
NSRS